## Slide 1: Address-Stride Assisted Approximate Load Value Prediction in GPUs
Haonan Wang, Mohamed Ibrahim (College of William & Mary),
Sparsh Mittal (IIT Hyderabad),
Adwait Jog (College of William & Mary)

## Slide 2
June 26, DSN
presentation
Portland, OR
(DSN)
Phoenix, AZ
(FCRC)
Haonan
Williamsburg, VA
(William & Mary)
June 27, ICS
presentation
Haonan
Adwait
I’m correlated with Haonan. I can present for him.
I don’t actually need to go.
Consumes time/energy Also, I might be late!
Wait.. this is exactly the case for Value Approximation. If a value is correlated with existing local values, it does not need to be fetched from the memory!

## Slide 3
Problem: Data movement across different levels of the memory hierarchy
  High energy consumption and memory bandwidth utilization
  Existing value prediction solutions are not optimal
Observation: Values can be more accurately predicted by exploiting correlation between the address stride and the value stride
  Exists in many data inputs processed by GPU applications
Solution: ASAP – a novel value approximation technique for GPUs
  Low hardware overhead
  Better prediction accuracy
Executive Summary

## Slide 4: Outline
Background & Motivation
Design of ASAP
Evaluation
Conclusion

## Slide 5: GPU Architecture with a (Roll-back Free) Value Predictor
L1
L2
DRAM
Core2
Core30
Interconnect
Core1
VP
L1
VP
L1
VP
Core
L1 Cache
Value
Predictor
(VP)
Training/Update Data
Predicted Data
Interconnect
L2 Cache
DRAM
…
…
L2
DRAM
L2
DRAM
R1
R2
Value
R1
Value
If certain quality loss can be tolerated
Rollbacks are not needed
Notes: After the prediction, if the predicted value is not the correct value, the execution of the program must be rolled back to the state before the prediction. However, if …

## Slide 6: CPUs: Prior Value Prediction Works
Context based predictor:
Use context table (containing history PCs) to index into prediction table
Not optimized for GPUs:
Use per-thread large prediction table – expensive for multi-threading
Does not directly consider the memory access order
Does not handle memory divergence
Hash function based predictor:
Use instruction info (e.g., PCs) to index into prediction table
Notes: Roll back is more expensive in GPUs.

## Slide 7: GPUs: Prior Value Prediction Works
....
word 0-15
word 16-31
Value Base0
Hash Fn
PC
Warp ID
Value Stride1
Value Base16
Value Stride2
Limitations:
Does not consider memory addresses and their order
-- Limiting the predictability of values
Using per Warp and PC information
-- May require large number of entries
One Stride Predictor (OSP):
Training:
Stride = Difference between Values
Prediction:
Value = Base + Stride
Rollback-Free Value prediction (RFVP)
Amir Yazdanbakhsh, et al. “RFVP: Rollback-Free Value Prediction with Safe-to-Approximate Loads.” TACO’2016.
Two Stride Predictor (TSP):
In training, it confirms:
Current Stride = Previous Stride
Sub-predictor 1
Sub-predictor 2
Notes: Mention TSP. – add confidence to training

## Slide 8: How can we improve existing GPU value predictors?

## Slide 9: Observation: Address Stride & Value Stride Correlation
Row-major:
Column-major:
Tracking address strides can help in better value predictoion
Nearby pixels are related (e.g., have linearly increasing grayscales).
row size

## Slide 10
Training
Prediction
Sequence1 (
Sequence2 (
Trained
0
0
2
2
4
1
0
0
2
1
4
2

Value
Base
Value
Stride
0
--
2
2
4
2
Training
Prediction
Trained
0
0
4
2
2
1
Value
Base
Value
Stride
0
--
4
4
8
4
Track Address Strides for Better Value Prediction (1)

## Slide 11
Error Indicator
(lower the better)
No enforcement
Only accepting address stride = 1 or address stride = row size
Only accepting constant address strides
Using address stride improves the predictability of values.
Request order
enforced by:
Track Address Strides for Better Value Prediction (2)
Notes: We prefer lower stride differences as constant value strides indicates good predictability.

## Slide 12: Outline
Background & Motivation
Design of ASAP
Evaluation
Conclusion

## Slide 13
How to efficiently track address strides?
How do we handle irregular memory access patterns?
How do we ensure the design of the value predictor is area-efficient?
Challenges of ASAP

## Slide 14: Address Stride Assisted Approximate Load Value Predictor (ASAP)
Upcoming
Address = 3
word 0-15
Address Base
Value Base0
Address
Stride Short
Value Stride Short1
Address Stride Long
Value Stride Long1
Value Base16
Value Stride Short2
Value Stride Long2
Entries with
LRU Eviction
word 16-31
MUX
MUX
....
....
Value = 6
2
1
2
4
2
4
2
8
4
match
Value = 10
match
Upcoming
Address = 4
Value = 8
Value = 12
Sub-predictor 1
Sub-predictor 2

## Slide 15: Walkthrough Example – Effectiveness of ASAP over Prior Work

## Slide 16: Operation of RFVP (Prior GPU Value Predictor)
1
0
Training
Prediction
0
2
4
8
6
10

Coverage = 4 / 6
Accurate Predictions = 2 / 4
Address Sequence: 0 → 1 → 2 → 4 → 3 → 5
0
2
2
4
4
8
3
6
5
10

Value
Base
Value
Stride
0
--
2
2
4
2
6
2
8
2
10
2

## Slide 17: Operation and Advantage of our new ASAP Predictor
Training
Prediction
ASAP:
Coverage = 3 / 6
Accurate Predictions = 3 / 3
0
2
4
8
6
10


Address
Base
Address
Stride
Short
Address
Stride
Long
0
--
--
1
1
--
2
1
2
4
1
2
5
1
2
Value
Base
Value
Stride
Short
Value
Stride
Long
0
--
--
2
2
--
4
2
4
8
2
4
10
2
4

No Prediction
Not Applicable
1
0
2
4
3
5
0
2
4
8
6
10
Address Sequence: 0 → 1 → 2 → 4 → 3 → 5
RFVP
Coverage = 4 / 6
Accurate Predictions = 2 / 4

## Slide 18: Outline
Background & Motivation
Design of ASAP
Evaluation
Conclusion

## Slide 19: Evaluation Methodology
Evaluated using GPGPU-Sim
  A cycle-level GPU simulator
Baseline Configuration (More details in the paper)
  30 SMs, 32-SIMT Lanes, 32 Threads/Warp, 48 Warps/SM
  16KB L1 (4-way, 128B Cache Block) + 32KB Shared Memory per SM
  256KB L2 (8-way, 128B Cache Block) per Memory Partition
  6 GDDR5 Memory Partitions, 16 Banks/Partition
  1 Crossbar/Direction
Workloads -- 12 Applications
  From CUDA SDK, Polybench
  Divided into different groups based on their characteristics

## Slide 20: Application Error
10% Coverage:
20% Coverage:
ASAP achieves better prediction accuracy with low entry requirement .
ASAP leads to more improvements at higher prediction coverages.
Notes: The error increase from 10% to 20% coverage is much higher in RFVP predictors than in ASAP predictors.

## Slide 21: Image Quality at 10% Coverage
No Prediction
App. Error: 0%
RFVP-TSP-8
App. Error: 40.1%
ASAP-TSP-8
App. Error: 13.6%
RFVP-TSP-Unlimited
App. Error: 16.9%
Utilizing address stride & value stride correlation for value approximation is effective in improving the output quality.

## Slide 22: IPC & Energy
ASAP achieves:
Similar performance and energy improvements with less application error.
More performance and energy improvements with same application error budget.

## Slide 23: Conclusions
Goal: Design low overhead, more accurate value approximation technique for GPUs.
Contributions:
  Demonstrate the correlation between address stride and value stride.
  Design a novel value approximation technique for GPUs (ASAP):
  Low capacity requirement
  Adaptive to complex access patterns in GPUs
  Across a variety of GPGPU applications, ASAP reduces application error by 84% to 95% in different scenarios.

## Slide 24: Thank You! Questions?
We acknowledge the support of the National Science Foundation (NSF) grants (#1657336, #1717532 and #1750667)
and Science & Engineering Research Board(SERB) award (#ECR/2017/000622)

## Slide 25: Application Characterization

## Slide 26: Case Study: Effective of Address Stride Long
  Miss Match Rate: The maximum percentage of missed requests that can be matched with ASAP.
Address stride long effectively improves the miss match rate.
  Miss Match Rate: The maximum percentage of missed requests that can be matched with ASAP.

## Slide 27: Case Study: Effect of Number of Entries
  Generally, 8 entries can provide enough Miss Match Rate for ASAP.
  Miss Match Rate: The maximum percentage of missed requests that can be matched with ASAP.
  The prediction table size requirement for ASAP is limited.

## Slide 28: Case Study: Effect of Warp Scheduler
Miss Match Rate increases with more a regular scheduling scheme.
  Miss Match Rate: The maximum percentage of missed requests that can be matched with ASAP.

## Slide 29: CPUs: Prior Value Prediction Works
Context based predictor:
Use context table (containing history PCs) to index into prediction table
Not optimized for GPUs:
Use per-thread large prediction table – expensive for multi-threading
Does not directly consider the memory access order
Does not handle memory divergence
Hash function based predictor:
Use instruction info (e.g., PCs) to index into prediction table
CPU
GPU
Multi-threading
Limited
Highly multi-threaded
Instruction Order
Limited out-of-order
Determined by warp scheduler
Memory Divergence
Limited
Yes
Notes: Roll back is more expensive in GPUs.

## Slide 30: Compiler Assisted Code Annotation
#pragma add_pred{fetch, 9, predict , 1}
...
#pragma approx{B}
C[i] = A[i] + B[i];
.fetch 9
.predict 1
...
ld.global.u32.approx %r0, [%r1]
Annotated CUDA code:
Generated PTX code: