## Slide 1: A Case for Core-Assisted Bottleneck Acceleration in GPUs Enabling Flexible Data Compression with Assist Warps
Nandita Vijaykumar
Gennady Pekhimenko, Adwait Jog, Abhishek Bhowmick, Rachata Ausavarangnirun, Chita Das, Mahmut Kandemir, Todd C. Mowry, Onur Mutlu
Notes: In this work we observe that different bottlenecks and imbalances in execution leave different GPU resources idle
Our goal in this work is employ these idle resources to accelerate different bottlenecks in execution
In order to do this we propose to employ light-weight helper threads
However, there are some key challenges that need to be addressed to enable helper threading in GPUs
We propose a new framework CABA that effectively addresses these challenges
The framework is flexible enough to be applied to a wide range of use case
In this work, the apply the framework to enable flexible data compression
We find that CABA shows that improves the performance of a wide range of GPGPU applications evaluated

## Slide 2: Executive Summary
Observation: Imbalances in execution leave GPU resources underutilized
Our Goal: Employ underutilized GPU resources to do something useful – accelerate bottlenecks using helper threads
Challenge: How do you efficiently manage and use helper threads in a throughput-oriented architecture?
Our Solution: CABA (Core-Assisted Bottleneck Acceleration)
  A new framework to enable helper threading in GPUs
  Enables flexible data compression to alleviate the memory bandwidth bottleneck
  A wide set of use cases (e.g., prefetching, memoization)
Key Results: Using CABA to implement data compression in memory improves performance by 41.7%
Notes: I’ll start by summarizing our work in a nutshell.
We make the observation that bottlenecks in executions and imbalances in resource requirements leave different resources in the GPU idle.
For example the memory bandwidth bottleneck leaves the cores idle while the threads are waiting for data to return from memory.
Our goal is to employ underutilized GPU resources to accelerate different bottlenecks in execution.
To this end, we introduce a new flexible framework to enable helper threading in GPUs that we call CABA.
We then apply this framework to enable flexible data compression to the memory bandwidth bottleneck.
However, CABA is a general framework that we believe can have many other uses like prefetching and memoization.
We find that CABA is provides a 42% performance improvement when used to implement data compression.

## Slide 3: GPUs today are used for a wide range of applications …
Computer Vision
Data Analytics
Scientific Simulation
Medical Imaging
Notes: Modern GPUs are used for a diverse set of important applications today. This is because they offer high performance and energy efficiency which comes from massive parallelism, high memory bandwidth and compute power.

## Slide 4: Challenges in GPU Efficiency
Memory
Hierarchy
Register File
Cores
GPU Streaming Multiprocessor
Thread
0
Thread
1
Thread
2
Thread
3
Full!
Idle!
Thread limits lead to an underutilized register file
The memory bandwidth bottleneck leads to idle cores
Threads
Idle!
Full!
Notes: However there are some challenges that introduce some inefficiency in execution.
GPU support a fixed number of threads and the GPU register files is partitioned among the threads running at any given time, there’s a fixed number compute units to execute these threads and of course, off-chip memory. A key challenge is maximizing utilization of different resources in the GPU to enable better efficiency in execution. However, this is difficult to achieve in practice because different applications may utilize different resources to varying extents, leaving some of them underutilized. A single GPU architecture cannot fit all applications with differing characteristics.
Let’s take an example where the GPU can run just four threads and each thread requires less than a quarter of the register file, there is going to some amount of the register file that is going to be underutilized.
Similarly, in memory bound workloads, the available memory bandwidth can quickly become the execution bottleneck, leaving the cores idle while the threads are waiting for data to come back from memory.

## Slide 5: Motivation: Unutilized On-chip Memory
24% of the register file is unallocated on average
Similar trends for on-chip scratchpad memory
Chart: % Unallocated Registers
| CONS | JPEG | LPS | MUM | SCP | MM | PVC | PVR | bfs | TRA | NN | STO | bp | hw | hs | SLA | nw | pf | mc | Geomean
 | 0.6875 | 0.625 | 0.375 | 0.125 | 0.0625 | 0.34375 | 0.25 | 0.34375 | 0.375 | 0.5625 | 0.67188 | 0.4375 | 0.25 | 0.125 | 0.15625 | 0.25 | 0.625 | 0.25 | 0.5 | 0.25246
Notes: We ran some experiments to analyze the impact of these balances and bottlenecks.
First, we look at the register file utilization for a representative set of workloads. On the Y-axis we plot the fraction of the register than remain unallocated. We find that in some applications more than 60% of the register file is unallocated and on average as much as 24% of the register file remains unutilized. We also see a similar trend in the utilization of on-chip shared memory.

## Slide 6: Motivation: Idle Pipelines
Memory Bound
Compute Bound
Chart: % Cycles
| CONS | JPEG | LPS | MUM | RAY | SCP | PVC | PVR | bfs | Avg.
Stalls | 0.6111 | 0.49131 | 0.3635 | 0.87077 | 0.27955 | 0.61036 | 0.78819 | 0.65211 | 0.71483 | 0.6659
Active | 0.3889 | 0.50869 | 0.6365 | 0.12923 | 0.72045 | 0.38964 | 0.21181 | 0.34789 | 0.28517 | 0.33384
Chart: % Cycles
| NN | STO | bp | hs | dmr | NQU | SLA | lc | pt | mc | Avg.
Stalls | 0.30138 | 0.20957 | 0.17554 | 0.21653 | 0.39608 | 0.36874 | 0.1523 | 0.10564 | 0.070168 | 0.34908
Active | 0.69862 | 0.79043 | 0.82446 | 0.78347 | 0.60392 | 0.63126 | 0.8477 | 0.89436 | 0.92983 | 0.65092
67% of cycles idle
35% of cycles idle
Notes: Second, we analyze a breakdown of idle time in the GPU pipeline. We first take a look at memory bound applications. The Y axis depicts the percentage of total issue cycles.
Compute stalls are due backed up pipelines when one of the hardware structures in the compute pipeline is unavailable . Memory stalls occur as a result of saturation in the memory hierarchy preventing further requests from being serviced. Waiting is the time spent waiting for data to come back from memory or a long latency computation or synchronization to complete. And active cycles include those cycles where instructions were actually issued into the pipelines to perform useful work. We find that in the case of memory bound workloads, as much of the 67% of the cycles are wasted. In the case of compute bound workloads, we see a similar trend where the primary cause of idleness comes from compute stalls and data dependencies leading to 35% of total issue cycles being idle.
TODO: Add banner with results on the graphs

## Slide 7: Motivation: Summary
Heterogeneous application requirements lead to:
Bottlenecks in execution
Idle resources
Notes: In summary, because there is a multitude of resources different resources become bottlenecks at different times and this leads to underutilization and idling of other resources.
We’ve seen that a) there are bottlenecks in execution and b) these bottlenecks tend to leave other resources underutilized.

## Slide 8: Our Goal
Memory
Hierarchy
Cores
Register File
Use idle resources to do something useful: accelerate bottlenecks using helper threads
A flexible framework to enable helper threading in GPUs: Core-Assisted Bottleneck Acceleration (CABA)
Helper
threads
Notes: Our goal in this work is to use these underutilized resources to alleviate the bottleneck in execution.
For example we can use the idle cores and register file to help alleviate the bandwidth bottleneck by using enabling an optimization like data compression using these idle resources.
In order to do this we develop a flexible framework in GPUs to enable helper threads to perform different optimizations which we refer to as CABA.
In order to do this we can use light-weight hardware generated threads to employ available resources to perform different optimizations which we use in this case to attack the memory bandwidth bottleneck. Some optimizations that can be performed with these helper threads include data compression, prefetching, etc.
In this work our goal is to develop a flexible framework to do this in GPUs which we refer to as CABA.
TODO: Should we swap the last two points?

## Slide 9: Helper threads in GPUs
Large body of work in CPUs …
  [Chappell+ ISCA ’99, MICRO ’02], [Yang+ USC TR ’98], [Dubois+ CF ’04], [Zilles+ ISCA ’01], [Collins+ ISCA ’01, MICRO ’01], [Aamodt+ HPCA ’04], [Lu+ MICRO ’05], [Luk+ ISCA ’01], [Moshovos+ ICS ’01], [Kamruzzaman+ ASPLOS ’11], etc.
However, there are new challenges with GPUs…
Notes: There’s been a large body of work that targets different helper threading mechanisms in CPUs. However there are some new challenges with GPUs which leads us to the question of how do we manage and use helper threads in GPUs.

## Slide 10: Challenge
How do you efficiently
manage and use helper threads
in a throughput-oriented architecture?

## Slide 11: Managing Helper Threads in GPUs
Thread
Warp
Block
Software
Hardware
Where do we add helper threads?
Notes: GPUs however execute thousands of threads in parallel. These threads are grouped at different levels of abstractions into threads, warps, blocks and grids. Programmers and software reason about threads at the granularity of a block which consists of hundreds of threads but hardware cannot execute all these hundreds of threads at the same time. So, threads are managed in hardware at the granularity of a warp which is a set of a few tens of threads. Software does not control the execution of warps. That leads us to the question of where do we add helper threads?
We could envision a software only approach where we enable helper threads entirely in software.

## Slide 12: Approach #1: Software-only
Regular threads
Helper threads
  No hardware changes
  Coarse grained
  Not aware of runtime program behavior
  Synchronization is difficult
Notes: We could create helper threads entirely in software, essentially at the granularity of a block, with special kernels just for helper threads and this would be great because now we don’t need any modifications to hardware. However, there are some drawbacks. The SW cannot control the scheduling and execution of threads at a finer granularities than a block. This means that we cannot control threads at a fine granularity. Since these threads are run independently of each other, synchronizing the execution of the helper threads and regular threads. Not aware of architectural events as well as the runtime behavior of the program.
A hardware only approach at the granularity of a warp could potentially provide fine-grained control over the management of helper threads however, providing contexts for execution would be tricky and enabling data communication and synchronization would be difficult and I’ll talk about why in a minute.

## Slide 13: Where Do We Add Helper Threads?
Thread
Warp
Block
Software
Hardware

## Slide 14: Approach #2: Hardware-only
  Fine-grained control
    Synchronization
    Enforcing Priorities
GPU
Cores
Register File
Warps
Core 0
Core 1
Reg File 0
Reg File 1
CPU
Reg File 0
Reg File 1
  Providing contexts efficiently is difficult
Notes: In CPUs threads have a fixed number of contexts. For example a 2-way 2 core processor has 4 contexts and can run 4 threads at a time. You can simply use one of the spare contexts to run a helper thread or provide additional smaller contexts to support helper threads. However, in the case of GPUs, the register file is partitioned between threads depending on the per- thread requirement and the compute pipelines are time-multiplexed among all executing threads. The same register file could be shared between 10 threads or even a 100 threads. In that sense, GPUs have “fluid contexts” but this brings us to the question of how do we supply contexts for execution of all these executing helper threads when there don’t already exist fixed spare context and it would be expensive to just create new contexts for helper threads.
Put registers in core
Don’t label RF
Label GPU diagram

## Slide 15: CABA: An Overview
“Tight coupling” of helper threads and regular threads
SW
HW
“Decoupled management” of helper threads and regular threads
Efficient context management
Simpler data communication
Dynamic management of threads
Fine-grained synchronization
Notes: We now introduce our proposed framework where we split the functionality between HW and SW in order to get the best of both worlds and treat them differently in both hardware and software. I’ll now go into how exactly this works.

## Slide 16: CABA: 1. In Software
Helper threads:
Tightly coupled to regular threads
Simply instructions injected into the GPU pipelines
Share the same context as the regular threads
Regs
Block
Regular threads
Helper threads
Efficient context management
Simpler data communication
Notes: We leverage the different abstractions in handling threads in the existing programming model to handle helper threads differently in software and hardware.
From the point of the compiler, runtime and the programmer, helper threads are essentially treated as a part of the regular of the regular threads. They are simply a subroutine of instructions performing a specific optimization embedded within the application code. As a result it is tightly coupled with the regular threads and shares the same context with the regular threads. In this sense, it is treated as a part of the regular threads.
This simplifies the context problem as : additional registers are allocated to it by the runtime per block for execution of helper thread routines and then scheduled onto the GPU streaming multiprocessor. These free registers are allocated out of the unallocated registers which we find to be sufficient in most cases. Otherwise it may increase the number of spills of reduce the reduce regular threads occupancy on the chip. By tightly coupling the helper threads in this manner to the regular threads it makes it a lot simpler to provide contexts for execution, makes data communication simpler and makes them very light-weight.

## Slide 17: CABA: 2. In Hardware
Helper threads:
Decoupled from regular threads
Tracked at the granularity of a warp – Assist Warp
  Each regular (parent) warp can have different assist warps
Parent Warp: X
Assist Warp: A
Assist Warp: B
Dynamic management of threads
Fine-grained synchronization
Notes: However from the point of view of hardware, we decouple the helper threads from the regular threads in order to be able to manage them separately. We track them, in hardware, at the granularity of a warp which we refer to as an assist warp. This enables us to manage them at a very fine granularity allowing us to trigger and squash helper threads when required. Each warp consisting on regular threads which we refer to as a parent warp has associated with it different assist warps which are essentially dynamic instances of different optimization subroutines that maybe enabled at anytime. The hardware framework supporting CABA requires some additional components to be added to the GPU pipeline which we describe next.

## Slide 18: Key Functionalities
Triggering and squashing assist warps
  Associating events with assist warps
Deploying active assist warps
  Scheduling instructions for execution
Enforcing priorities
  Between assist warps and parent warps
  Between different assist warps
Notes: There are some key functionalities that the hardware components need to perform to support assist warp execution.
First, different assist warps need to be triggered at different points in execution, perhaps at some point in the program execution or at some architectural events. Once triggered for execution, these assist warps need to execute in conjunction with the parent warps using the same pipelines and this introduces new problems. We have to ensure that assist warps do not hinder the progress of the primary warps and hence they need be scheduled for execution at the appropriate times. Considering many different assist warps and regular warps active at the same time, we need a way to enforce priorities between both to ensure program correctness as well as forward progress. To handle these functionalities we introduce some new hardware components into the GPU pipeline which we describe next.
In order to make sure that any critical work offloaded to an assist warp gets completed, while non essential assist warp execution doesn’t stall parent warp progress

## Slide 19: CABA: Mechanism
Deploy
Scheduler
ALU
Fetch
I-Cache
Assist Warp Store
Wr
i
teback
Instruction
Buffer
Assist Warp
Buffer
Scoreboard
Decode
ALU
ALU
Mem
Issue
Trigger
Assist Warp Controller
Assist Warp Store
Holds instructions for different assist warp routines
Assist Warp Controller
  Central point of control for:
    Triggering assist warps
    Squashing them
  Tracks progress for active assist warps
Assist Warp
Buffer
Stages instructions from triggered assist warps for execution
Helps enforce priorities
Notes: So here we have a typical GPU pipeline.
…..
First we add the AWC which is the central point of control that associate trigger and kill events with different assist warp routines.
It also monitors the current status of all running assist warps.
We decouple triggering from the actual deployment of assist warps for execution in order so that it’s execution doesn’t interfere with the regular threads.
When a trigger event occur, the AWC activates the associated assist warps and it then monitors to find the appropriate time to deploy the assist warp. When the assist warp is deployed, the next instruction to be executed is retrieved from the instruction store for assist warps which we depict as the AWS.
The instruction is then decoded and is staged for execution in the AWB, till the warp scheduler selects it for issue once its dependences are met.
We can enforce priorities by controlling when assist warps are triggered, by controlling how often assist warps are deployed or by controlling when buffered instructions are scheduled for execution.

## Slide 20: Other functionality
In the paper:
More details on the hardware structures
Data communication and synchronization
Enforcing priorities

## Slide 21: CABA: Applications
Data compression
Memoization
Prefetching
…
Notes: Now that we’ve seen how CABA is implemented, how can we use it?
Some of the applications that could be enabled with CABA include….

## Slide 22: A Case for CABA: Data Compression
Data compression can help alleviate the memory bandwidth bottleneck - transmits data in a more condensed form
Memory
Hierarchy
Compressed
Uncompressed
CABA employs idle compute pipelines to perform compression
Idle!
Notes: Recall that one of the source of inefficiency In utilizing resources is the memory bandwidth bottleneck.
Data compression is a technique that can help alleviate this bottleneck by transmitting data in a more condensed form.
In bandwidth-constrained workloads, idle compute pipelines offer an opportunity to enable data compression with CABA.

## Slide 23: Data Compression with CABA
Use assist warps to:
  Compress cache blocks before writing to memory
  Decompress cache blocks before placing into the cache
CABA flexibly enables various compression algorithms
Example: BDI Compression [Pekhimenko+ PACT ’12]
  Parallelizable across SIMT width
  Low latency
Others: FPC [Alameldeen+ TR ’04], C-Pack [Chen+ VLSI ’10]
Notes: In order to perform data compression with CABA we use assist.
One of the nice things about using assist warps is that unlike a hardware based mechanism, we are tied down to using only one compression algorithm, CABA enables flexibility in algorithm choice. We actually studied three different compression algorithms which we detail in the paper, but an example of a compression algorithm that is amenable with CABA is BDI, because it easily:
We use BDI for this reason for our primary evaluations.

## Slide 24: Walkthrough of Decompression
Scheduler
L1D
L2 + Memory
Assist Warp
Store
Assist Warp
Controller
Cores
Uncompressed
Compressed
Hit!
Miss!
Trigger

## Slide 25: Walkthrough of Compression
Scheduler
L1D
L2 + Memory
Assist Warp
Store
Assist Warp
Controller
Cores
Trigger

## Slide 26: Evaluation

## Slide 27: Methodology
Simulator: GPGPUSim, GPUWattch
Workloads
  Lonestar, Rodinia, MapReduce, CUDA SDK
System Parameters
  15 SMs, 32 threads/warp
  48 warps/SM, 32768 registers, 32KB Shared Memory
  Core: 1.4GHz, GTO scheduler , 2 schedulers/SM
  Memory: 177.4GB/s BW, 6 GDDR5 Memory Controllers, FR-FCFS scheduling
  Cache: L1 - 16KB, 4-way associative; L2 - 768KB, 16-way associative
Metrics
  Performance: Instructions per Cycle (IPC)
  Bandwidth Consumption: Fraction of cycles the DRAM data bus is busy
Notes: We use GPGPUSim for our evaluations and use a number of representative benchmarks from several common GPGPU application suites. We focus on the applications that are benefit from compression. For other applications assist warps can easily be disabled while incurring no performance overhead.
We base our hardware model off the GTX 480.

## Slide 28: Effect on Performance
Chart: Normalized Performance
| BFS | CONS | JPEG | LPS | MUM | RAY | SLA | TRA | bfs | bh | mst | sp | sssp | KM | MM | PVC | PVR | SS | hw | nw | Geomean
CABA-BDI | 1.8261 | 1.1064 | 1.2188 | 1.156 | 1.3171 | 1.1092 | 1.0298 | 1.1764 | 1.5851 | 1.1896 | 2.0767 | 1.3236 | 1.469 | 1.3261 | 2.0075 | 2.6542 | 2.155 | 1.526 | 1.0422 | 1.1463 | 1.417
No-Overhead-BDI | 1.8031 | 1.1171 | 1.2849 | 1.2787 | 1.3123 | 1.115 | 1.0317 | 1.175 | 1.5729 | 1.1928 | 2.0398 | 1.3217 | 1.4464 | 1.3812 | 2.1852 | 2.6839 | 2.2809 | 1.6105 | 1.0438 | 1.1879 | 1.4454
CABA provides a 41.7% performance improvement
CABA achieves performance close to that of designs with no overhead for compression
41.7%
Notes: Here we show the impact on performance of using CABA to perform data compression. The Y-axis depicts the performance normalized to a baseline system with no compression.
CABA provides a performance improvement of as much as 2.7X and on average a 41% improvement in performance.
We also study a no-overhead design where we retain the benefits of compression while incurring none of the overheads of actually perfrming the compression and decompression.
We find that CABA loses only 3% on average in comparison to the no-overhead design, because of the existence of idle cycles to perform the compression/decompression..
We see in some cases that …….
For all of our memory bound compressible applications we see that the performance benefits from CABA always outweigh the assist warp overhead.
CABA- BDI refers to the design with CABA using the BDI. We find the CABA-BDI provides a 41% improvement in performance over baseline
We then evaluate an ideal design with none of the overheads of compression. We find that CABA loses only 3% in performance in comparison to the ideal case.
We also compare with a previously proposed hardware-based memory bandwidth compression design that involves compressing only for memory bandwidth. We find that CABA performs 9% better and this is because of significant benefits from compressing the on-chip interconnect traffic as well
Finally we compare with a dedicated hardware design that compresses both at the interconnect as well as at the memory and find that on average CABA only performs about 2% worse than the hardware based design. This is because of the existence of sufficient idle time in most case to effectively execute assist warps to perform the compression.
CABA-BDI provides a 41.7% average improvement
Only 2.8% less than the ideal case (Ideal-BDI) with none of the overheads associated with CABA
CABA-BDI’s performance
3. 9.9% better than the previous hardware-based memory bandwidth compression design (HW-BDI-Mem)
4. 1.6% worse than the purely hardware-based design (HW-BDI) that
performs both interconnect and memory bandwidth compression.

## Slide 29: Effect on Bandwidth Consumption
Chart: Memory Bandwidth Consumption
| BFS | CONS | JPEG | LPS | MUM | RAY | SLA | TRA | bfs | bh | mst | sp | sssp | KM | MM | PVC | PVR | SS | hw | nw | Geomean
Baseline | 0.12047 | 0.59557 | 0.62973 | 0.58068 | 0.76963 | 0.3491 | 0.48463 | 0.59309 | 0.63985 | 0.31001 | 0.65796 | 0.74128 | 0.62178 | 0.31175 | 0.80162 | 0.77174 | 0.71836 | 0.67746 | 0.41216 | 0.18543 | 0.53643
CABA-BDI | 0.069443 | 0.57077 | 0.45927 | 0.2344 | 0.71692 | 0.11165 | 0.28835 | 0.52474 | 0.36713 | 0.23793 | 0.49472 | 0.59498 | 0.40857 | 0.19225 | 0.50582 | 0.57938 | 0.50134 | 0.34015 | 0.36503 | 0.10932 | 0.35596
Data compression with CABA alleviates the memory bandwidth bottleneck
Notes: Now, let’s look at why we are able to achieve this speedup in performance. Here we show the memory bandwidth utilization for our different designs. We see that in most workloads the performance benefits correlate with reduction in the utilization of memory bandwidth. Data compression reduces the traffic and hence the contention in the DRAM channels and hence reduces the overall utilization. We see a drop in utilization from on average form 53% to 35% and this helps alleviate the memory bandwidth bottleneck.
REMOVE NO-OVERHEAD

## Slide 30: Different Compression Algorithms
Chart: Normalized Performance
| BFS | CONS | JPEG | LPS | MUM | RAY | SLA | TRA | bfs | bh | mst | sp | sssp | KM | MM | PVC | PVR | SS | hw | nw | Geomean
CABA-FPC | 1.5533 | 1.1068 | 1.0912 | 0.9179 | 1.2628 | 1.118 | 0.98312 | 1.0943 | 1.0409 | 1.1037 | 1.1795 | 1.1501 | 1.0452 | 1.27 | 1.703 | 1.7725 | 1.8333 | 1.3475 | 1.0471 | 1.021 | 1.2071
CABA-BDI | 1.8261 | 1.1064 | 1.2188 | 1.156 | 1.3171 | 1.1092 | 1.0298 | 1.1764 | 1.5851 | 1.1896 | 2.0767 | 1.3236 | 1.469 | 1.3261 | 2.0075 | 2.6542 | 2.155 | 1.526 | 1.0422 | 1.1463 | 1.417
CABA-CPack | 1.7011 | 1.113 | 1.2767 | 1.1182 | 1.3254 | 1.1159 | 1.0216 | 1.1652 | 1.4945 | 1.239 | 1.6995 | 1.3462 | 1.3928 | 1.3558 | 1.8038 | 2.0357 | 1.8608 | 1.4189 | 1.0191 | 1.1087 | 1.3521
CABA-BestOfAll | 1.8043 | 1.1727 | 1.2626 | 1.1419 | 1.3886 | 1.1083 | 1.0297 | 1.2371 | 1.5641 | 1.2315 | 2.073 | 1.345 | 1.4662 | 1.4765 | 2.0073 | 2.6545 | 2.1547 | 1.5254 | 1.0477 | 1.125 | 1.4383
CABA is flexible: Improves performance with different compression algorithms
Notes: Here we show performance results while using 3 different compressions. BestOfAll refers to an oracle design that picks the best compression algorithm for each cache line. We find that all our designs improve performance over the baseline with different algorithms performing best for different workloads. The flexibility essentially enables leveraging different algorithms in obtaining better performance across all workloads.

## Slide 31: Other Results
CABA’s performance is similar to pure-hardware based BDI compression
CABA reduces the overall system energy (22%) by decreasing the off-chip memory traffic
Other evaluations:
  Compression ratios
  Sensitivity to memory bandwidth
  Capacity compression
  Compression at different levels of the hierarchy

## Slide 32: Conclusion
Observation: Imbalances in execution leave GPU resources underutilized
Our Goal: Employ underutilized GPU resources to do something useful – accelerate bottlenecks using helper threads
Challenge: How do you efficiently manage and use helper threads in a throughput-oriented architecture?
Our Solution: CABA (Core-Assisted Bottleneck Acceleration)
  A new framework to enable helper threading in GPUs
  Enables flexible data compression to alleviate the memory bandwidth bottleneck
  A wide set of use cases (e.g., prefetching, memoization)
Key Results: Using CABA to implement data compression in memory improves performance by 41.7%
Notes: Now let me conclude:
We make the observation that bottlenecks in executions and imbalances in resource requirements leave different resources in the GPU idle.
For example the memory bandwidth bottleneck leaves the cores idle while the threads are waiting for data to return from memory.
Our goal is to employ underutilized GPU resources to accelerate different bottlenecks in execution.
To this end, we introduce a new flexible framework to enable helper threading in GPUs that we call CABA.
We then apply this framework to enable flexible data compression to the memory bandwidth bottleneck.
However, CABA is a general framework that we believe can have many other uses like prefetching and memoization.
We find that CABA is provides a 42% performance improvement when used to implement data compression.

## Slide 33: A Case for Core-Assisted Bottleneck Acceleration in GPUs Enabling Flexible Data Compression with Assist Warps
Nandita Vijaykumar
Gennady Pekhimenko, Adwait Jog, Abhishek Bhowmick, Rachata Ausavarangnirun, Chita Das, Mahmut Kandemir, Todd C. Mowry, Onur Mutlu
Notes: In this work we observe that different bottlenecks and imbalances in execution leave different GPU resources idle
Our goal in this work is employ these idle resources to accelerate different bottlenecks in execution
In order to do this we propose to employ light-weight helper threads
However, there are some key challenges that need to be addressed to enable helper threading in GPUs
We propose a new framework CABA that effectively addresses these challenges
The framework is flexible enough to be applied to a wide range of use case
In this work, the apply the framework to enable flexible data compression
We find that CABA shows that improves the performance of a wide range of GPGPU applications evaluated

## Slide 34: Backup Slides

## Slide 35: Effect on Energy
Chart: Normalized Energy
| BFS | CONS | JPEG | LPS | MUM | RAY | SLA | TRA | bfs | bh | mst | sp | sssp | KM | MM | PVC | PVR | SS | hw | nw | Geomean
CABA-BDI | 0.90992 | 0.95589 | 0.87115 | 0.77296 | 0.78169 | 0.84966 | 0.88884 | 0.83254 | 0.6499 | 0.953 | 0.64154 | 0.7496 | 0.72874 | 0.81326 | 0.65887 | 0.55012 | 0.66062 | 0.7301 | 0.97736 | 0.77682 | 0.77884
Ideal-BDI | 0.80496 | 0.93548 | 0.81038 | 0.72398 | 0.78159 | 0.84521 | 0.87211 | 0.83561 | 0.59014 | 0.88743 | 0.59407 | 0.73239 | 0.682 | 0.76252 | 0.61167 | 0.50093 | 0.61642 | 0.69006 | 0.96606 | 0.75289 | 0.73946
HW-BDI-Mem | 0.95421 | 0.9418 | 0.8329 | 0.75382 | 0.79672 | 0.8626 | 0.87954 | 0.85249 | 0.64701 | 0.92122 | 0.62409 | 0.75087 | 0.72464 | 0.7971 | 0.64395 | 0.53927 | 0.64717 | 0.71546 | 0.96877 | 0.76458 | 0.77154
HW-BDI | 0.80705 | 0.93474 | 0.81244 | 0.72896 | 0.78383 | 0.80148 | 0.8731 | 0.84845 | 0.59051 | 0.8863 | 0.60945 | 0.73294 | 0.68396 | 0.76544 | 0.62839 | 0.51035 | 0.6317 | 0.70253 | 0.96694 | 0.75446 | 0.74319
CABA reduces the overall system energy by decreasing the off-chip memory traffic
Notes: Compression decreases energy consumption in two ways: 1)
by reducing bus energy consumption, 2) by reducing execution
time.
CABA-BDI reduces energy consumption by as much
as 22.2% over the baseline.
It is also only 4.0% more
than that of the Ideal-BDI design which has none of the overheads associated with compression ,
and only 3.6% more
than that of the HW-BDI design, which uses dedicated logic
for memory bandwidth compression.

## Slide 36: Effect on Compression Ratio

## Slide 37: Other Uses of CABA
Hardware Memoization
  Goal: avoid redundant computation by reusing previous results over the same/similar inputs
  Idea:
    hash the inputs at predefined points
    use load/store pipelines to save inputs in shared memory
    eliminate redundant computation by loading stored results
Prefetching
  Similar to CPU