## Slide 1
Exploiting Core Criticality for Enhanced GPU Performance
Adwait Jog, Onur Kayıran, Ashutosh Pattnaik,
Mahmut T. Kandemir, Onur Mutlu,
Ravishankar Iyer, Chita R. Das.
SIGMETRICS ‘16

## Slide 2: Era of Throughput Architectures
GPUs are scaling: Number of CUDA Cores, DRAM bandwidth
2016:
GTX 1080
(Pascal)
2560 cores
(320 GB/sec)
2010:
GTX 480
(Fermi)
448 cores
(178 GB/sec)
2012:
GTX 680
(Kepler)
1536 cores
(192 GB/sec)
Number of CUDA Cores are scaling rapidly
Memory bandwidth is scaling at a much slower pace
Notes: As we know GPU are scaling both in terms of number of CUDA cores as well peak DRAM
Bandwidth. For example, the latest NVIDIA GPU GTX 1080 has more than 2000 cores.
Given such powerful GPUs, the question is -- Are we “still” using them efficiently?
Memory Bandwidth not increasing fast enough.

## Slide 3: Current Trend
Modern Schedulers (e.g., FR-FCFS)
  assume that all memory requests are equally critical towards performance.
  maximize memory data throughput.
Inability of FR-FCFS to distinguish memory requests from different GPU cores lead to
  GPU cores experiencing significant variation in average memory access latencies
  some GPU cores becoming more “critical” than others
Notes: Due to such variation, the number of stalling warps that belong to the cores that suffer
from higher memory access latencies is typically higher than that of other cores, making
the former type of cores less latency tolerant, i.e., more critical for overall performance.
Thus, because different cores have varying degrees of tolerance to latency during
execution, their corresponding memory requests have varying degrees of criticality

## Slide 4: Coefficient of Variation (COV) in Average Memory Access Latencies
To understand further,
  consider the COV (ratio of Standard Deviation over Arithmetic Mean) in memory access latencies
  some GPU cores experience higher avg. memory latency than others
  these cores are less latency tolerant (“critical”)
  latency variations correlate with IPC variation
Chart: Average Coefficient of Variation (COV)
| 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | 1xB | 2xB | 4xB | LUH | RED | SCAN | LPS | RAY | CONS | SCP | BLK | HS | CFD | GAUSS | AVG.
Latency | 0.12 | 0.088889 | 0.0192 | 0.18 | 0.17 | 0.0306 | 0.19 | 0.15306 | 0.0418 | 0.05 | 0.03 | 0.0035 | 0.38 | 0.28875 | 0.0759 | 0.09 | 0.0225 | 0.0045 | 0.06 | 0.03 | 0.0042 | 0.05 | 0.033333 | 0.004 | 0.07 | 0.0504 | 0.0112 | 0.07 | 0.062632 | 0.0119 | 0.08 | 0.055385 | 0.0128 | 0.11727 | 0.08954 | 0.019964
IPC | 0.18 | 0.14211 | 0.0648 | 0.2 | 0.19 | 0.038 | 0.11 | 0.092889 | 0.0352 | 0.39 | 0.36279 | 0.1521 | 0.38 | 0.23688 | 0.1482 | 0.12 | 0.037895 | 0.0132 | 0.17 | 0.14086 | 0.0884 | 0.09 | 0.06 | 0.0162 | 0.05 | 0.034 | 0.008 | 0.19 | 0.18642 | 0.0988 | 0.07 | 0.061463 | 0.0252 | 0.17727 | 0.14048 | 0.062555
We need to take core criticality into account.
  Prioritize requests from GPU cores with less latency tolerance
Contention is present in entire memory hierarchy.
  In this work, we only consider main memory contention
  We propose CLAMS, a criticality aware memory scheduling mechanism

## Slide 5: Outline
Introduction and Motivation
Core Criticality: Metrics and Analysis
Design of Criticality Aware Memory Scheduler
Infrastructure Setup and Evaluation
Conclusions

## Slide 6: Core Criticality: Metrics
We need to quantify core criticality.
Use latency tolerance as a measure of core criticality.
  Classify warps into short- and long-latency warp
    Short-latency: compute instruction/data in private cache
    Long-latency: stalled due to pending memory requests
  Calculate short-latency ratio
    Ratio of short-latency warps over total issued warps
  Assign criticality rank
    Quantize short-latency ratio
      8 discrete steps, with step size of 1/8.
      rank-1: short-latency ratio < 1/8, Most critical
      rank-8: short-latency ratio > 7/8, Least critical

## Slide 7: Core Criticality: Metrics
ThCR : Criticality-Rank-Threshold
  Core is critical if current rank <= ThCR
  Takes any integer value from 1 to 8.
PCC(ThCR ): Percentage of critical cores for given ThCR
  PCC(ThCR ) of 100%, all cores critical
  PCC(ThCR ) of 0%, all cores non-critical
Chart: Rank
| Core-1 | Core-2 | Core-3
 | 7 | 5 | 2
ThCR = 7, PCC(7)=100%
ThCR = 4, PCC(4)=33%
ThCR = 1,
PCC(1)=0%

## Slide 8: Core Criticality: Metrics
PCC is dependent on the chosen criticality-rank threshold
PCC varies within an application over time
PCC varies across applications
PCC reduces significantly as main memory bandwidth increases
Chart: Average PCC(1)
| LUH | RED | SCAN | LPS | RAY | CONS | SCP | BLK | HS | CFD | GAUSS
1xB | 0.19 | 0.7 | 0.536 | 0.245 | 0.11 | 0.19 | 0.43 | 0.21 | 0.062 | 0.15 | 0.129
2xB | 0.16443 | 0.575 | 0.424 | 0.112 | 0.075063 | 0.04 | 0.33266 | 0.13637 | 0.037 | 0.14265 | 0.113
4xB | 0.14845 | 0.54 | 0.394 | 0.078 | 0.063648 | 0.022 | 0.32293 | 0.064861 | 0.032 | 0.13768 | 0.106
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 9
If PCC(ThCR ) is low for any given ThCR, then
  GPU cores have similar latency tolerance
  Memory scheduler should preserve locality
PCC(ThCR ) is calculated periodically and requires
  Exchange of global information across cores and MCs
  Hardware overhead of calculation
Expensive approach!
We need a metric which can be calculated at the MCs
9
Core Criticality: Metrics and Analysis

## Slide 10
We use Percentage of Critical Requests (PCR).
  Tag memory requests with core’s current rank
  Calculate the percentage of critical memory requests present in the MC request buffer
Eliminates the exchange of global information between GPU cores and MCs
Similar to PCC, PCR needs to be calculated for a given ThCR.
Core Criticality: Metrics and Analysis

## Slide 11
PCR patterns for an application similar to PCC
Core Criticality: Metrics and Analysis
Chart: PCR
Time
Chart: PCC
Chart: PCR
Chart: PCC
Time
Time
Similar observations hold for PCR
  PCR considers criticality of requests instead of their corresponding cores

## Slide 12
Scope of criticality aware memory scheduler
Distribution of criticality-rank differences across DRAM requests
  criticality-rank differences: difference between highest and lowest criticality-rank of requests in MC at the same time
diff-0 denotes % of DRAM cycles, all memory requests have same rank
Core Criticality: Analysis
Chart: Percentage of DRAM Cycles
| LUH | RED | SCAN | LPS | RAY | CONS | SCP | BLK | HS | CFD | GAUSS | AVG.
diff-0 | 0.178 | 0.122 | 0.188 | 0.061 | 0.256 | 0.083 | 0.063 | 0.023 | 0.161 | 0.782 | 0.831 | 0.24982
diff-1 | 0.137 | 0.716 | 0.133 | 0.083 | 0.071 | 0.059 | 0.387 | 0.092 | 0.116 | 0.06 | 0.039 | 0.17209
diff-2 | 0.149 | 0.082 | 0.043 | 0.133 | 0.057 | 0.067 | 0.373 | 0.28 | 0.108 | 0.083 | 0.028 | 0.12755
diff-3 | 0.077 | 0.02 | 0.043 | 0.17 | 0.039 | 0.084 | 0.122 | 0.485 | 0.131 | 0.047 | 0.015 | 0.11209
diff-4 | 0.054 | 0.019 | 0.056 | 0.189 | 0.058 | 0.133 | 0.038 | 0.104 | 0.249 | 0.015 | 0.014 | 0.084455
diff-5 | 0.048 | 0.015 | 0.06 | 0.248 | 0.054 | 0.216 | 0.013 | 0.005 | 0.109 | 0.005 | 0.013 | 0.071455
diff-6 | 0.05 | 0.004 | 0.067 | 0.079 | 0.069 | 0.288 | 0.004 | 0.004 | 0.09 | 0.002 | 0.019 | 0.061455
diff-7 | 0.307 | 0.022 | 0.411 | 0.038 | 0.397 | 0.07 | 0 | 0.007 | 0.035 | 0.005 | 0.041 | 0.12118
Significant rank difference in LUH, RAY, SCAN
  High scope
Rank difference is 0 for most of the time for CFD, GAUSS
  Low scope

## Slide 13: Outline
Introduction and Motivation
Core Criticality: Metrics and Analysis
Design of Criticality Aware Memory Scheduler
Infrastructure Setup and Evaluation
Conclusions

## Slide 14
Two major challenges
  Co-existence of critical and non-critical requests
    Finding appropriate value of ThCR
      Low ThCR -> less critical cores
      High ThCR -> too many critical cores
  Balancing DRAM locality and criticality
    Switching between schedulers optimized for criticality or locality
    Calculate PCR(ThCR) periodically and compare with Switching-Mode-Threshold(ThSM)
      PCR(ThCR) > ThSM, locality mode
      PCR(ThCR) <= ThSM, criticality mode
    Need to find appropriate value of ThSM
Design of CLAMS

## Slide 15
Three different approaches
  Static-CLAMS
    Single and fixed set values for ThCR and ThSM
  Semi-Dyn-CLAMS
    Dynamically calculates ThCR, based on fixed ThSM and PCR(k) ∀ k information at MC
  Dyn-CLAMS
    Calculates both, ThCR and ThSM.
Working modes of CLAMS
  Decided based on per bank’s memory requests
  Locality mode
  Criticality mode
Design of CLAMS
Notes: It prioritizes: 1) row-
hit requests over all other requests, 2) critical requests over
other requests, 3) older requests over younger ones. Hence,
if there are no critical requests present, this mode follows
the baseline FR-FCFS scheduling policy [74,93], which prioritizes: 1) row-hit requests over all other requests, 2) older
requests over younger ones.
Criticality mode.
In this mode, CLAMS is criticality-
focused, and optimizes mainly for criticality. It prioritizes:
1) critical requests over all other requests, 2) row hit requests
over other requests, 3) older requests over younger ones.
Hence, if there are no critical requests present, this mode
falls back to the baseline FR-FCFS policy.

## Slide 16
rank-4 provides a mix of both, critical and non-critical requests
  We choose ThCR = 4
But, many applications have different distribution such as SCP
  Assuming ThSM = 20% -> locality mode most of the time
  Assuming ThSM = 80% -> criticality mode most of the time
    Potentially degrade DRAM row buffer locality
Chart: Percentage of Requests
| LUH | RED | SCAN | LPS | RAY | CONS | SCP | BLK | HS | CFD | GAUSS | AVG.
rank-1 | 0.162 | 0.63 | 0.342 | 0.001 | 0.046 | 0.025 | 0.4 | 0.153 | 0.009 | 0.16 | 0.019 | 0.177
rank-2 | 0.312 | 0.197 | 0.121 | 0.019 | 0.043 | 0.087 | 0.401 | 0.431 | 0.029 | 0.148 | 0.019 | 0.16427
rank-3 | 0.162 | 0.029 | 0.063 | 0.143 | 0.05 | 0.149 | 0.127 | 0.303 | 0.045 | 0.105 | 0.019 | 0.10864
rank-4 | 0.069 | 0.004 | 0.079 | 0.178 | 0.07 | 0.186 | 0.035 | 0.086 | 0.101 | 0.094 | 0.015 | 0.083364
rank-5 | 0.032 | 0.029 | 0.062 | 0.193 | 0.05 | 0.168 | 0.013 | 0.01 | 0.095 | 0.041 | 0.012 | 0.064091
rank-6 | 0.027 | 0.002 | 0.052 | 0.173 | 0.062 | 0.137 | 0.008 | 0.002 | 0.124 | 0.036 | 0.019 | 0.058364
rank-7 | 0.014 | 0.001 | 0.038 | 0.112 | 0.064 | 0.102 | 0.003 | 0.003 | 0.213 | 0.01 | 0.031 | 0.053727
rank-8 | 0.223 | 0.108 | 0.242 | 0.18 | 0.615 | 0.145 | 0.012 | 0.012 | 0.384 | 0.405 | 0.864 | 0.29
Design of Static-CLAMS
Take away:
We need to adapt ThCR based on the application
ThCR and ThSM should not be determined independently

## Slide 17
    Computes ThCR
      Based on fixed ThSM value, and PCR(k) ∀ k ∈ {1...8} information at MC
  We find a value for ThCR such that PCR(ThCR) is ≦ThSM and is as close to it as possible
This will switch scheduler into criticality mode
In case no such ThCR can be found, switch to locality mode
Design of Semi-Dyn-CLAMS

## Slide 18: Design of Semi-Dyn-CLAMS
Lets look at SCP
Assume ThSM = 40%, and ThCR can take any value in {1,4,7}.
ThCR = 1, is chosen for first half of execution as PCR(1) <= 40%. Scheduler works in criticality mode.
For second half of execution, for no ThCR, is PCR(ThCR) <= 40%. Scheduler switches to locality mode.
  Most of the requests are critical and cannot be prioritized
Chart: Percentage of Requests
Time
1
2
1
2
ThCR is obtained using the PCR(k) information at the MC
But, actual working mode of scheduler determined based on the requests to be issued to a particular bank.
  Aware of requests destined to each bank
  Aware of all requests in the MC
Take away:
Semi-Dyn-CLAMS aggressively uses criticality mode
Only goes to locality mode, when too many critical requests present in the MC buffer
Can lead to significant loss in locality and performance
No feedback on ThSM when new value of ThCR is calculated.

## Slide 19
Even though Semi-Dyn-CLAMS facilitates criticality mode
  Actual mode based on requests to each bank
    Can be locality mode even though PCR(ThCR) <= ThSM
Dyn-CLAMS attempts to improve the loss in locality.
Dynamically calculates ThCR and updates ThSM based on the new value of ThCR.
Design of Dyn-CLAMS
Key Idea:
Gauge the negative effect of loss in row locality on latency tolerance
Mitigate the loss by lowering ThSM while maintaining the value of ThCR.

## Slide 20
Initialize ThSM = 40%, and ThCR = 8
Calculate ThCR based on Semi-Dyn-CLAMS
  ThCR updated to 1
Update ThSM to new value of PCR(ThCR)
In second half of execution
  Scheduler goes into locality mode, similar to Semi-Dyn-CLAMS
Chart: Percentage of Requests
Time
3
2
1
ThSM
Design of Dyn-CLAMS
3
1
2
Take away:
Dynamically updating ThCR allows scheduler to aggressively work in criticality mode
By reducing ThSM, the scheduler’s starts to improve locality by using locality mode for the banks
  chances of a bank’s PCR(ThCR) > ThSM increase

## Slide 21: Outline
Introduction and Motivation
Core Criticality: Metrics and Analysis
Design of Criticality Aware Memory Scheduler
Simulation Setup and Evaluation
Conclusions

## Slide 22: Simulation Setup
Evaluated on GPGPU-Sim, a cycle accurate GPU simulator
Baseline configuration similar to scaled-up version of GTX480
  32 SMs, 32-SIMT lanes, 32-threads/warp
  16KB L1 (4-way, 128B cache block) + 48KB Shared Mem/SM
  6 partitions/channels
Applications classified into 2 groups
  Group A: Moderate to High scope
  Group B: Low scope

## Slide 23: Performance with CLAMS (Normalized to FR-FCFS)
Performance improvement for Group A applications
Chart: Normalized IPC
| LUH | RED | SCAN | LPS | RAY | CONS | SCP | BLK | HS | CFD | GAUSS | GMEAN | GEMAN-A
Static-CLAMS | 1.1026 | 1.0124 | 1.0122 | 1.0376 | 1.0699 | 1.0446 | 1.0044 | 1.0351 | 1.0243 | 1.0089 | 1.0237 | 1.0338 | 1.0461
Semi-Dyn-CLAMS | 1.07 | 1.1351 | 1.0225 | 1.0498 | 1.0715 | 1.0431 | 0.97515 | 1.0124 | 1.0387 | 1.0043 | 1.006 | 1.0382 | 1.0647
Dyn-CLAMS | 1.1062 | 1.1228 | 1.0238 | 1.0598 | 1.1532 | 1.0462 | 1.0229 | 1.0337 | 1.0424 | 1.0045 | 1.0223 | 1.057 | 1.0844
FR-FCFS-Cap-Best | 1.0265 | 0.99898 | 1.0301 | 1.0637 | 1.1 | 1.0276 | 1.0185 | 1.0265 | 1.0451 | 1.0018 | 1.012 | 1.0315 | 1.0406
Static-CLAMS-Best | 1.1026 | 1.1549 | 1.0386 | 1.0649 | 1.1555 | 1.049 | 1.0352 | 1.0375 | 1.0466 | 1.0089 | 1.0643 | 1.0679 | 1.0932
  Static-CLAMS = 4.6%
  Static-CLAMS-Best = 9.3%
  FR-FCFS-Cap-Best = 4%
  Semi-Dyn-CLAMS = 6.5%
  Dyn-CLAMS = 8.4%
Group A
Group B
More results and detailed description
of Dyn-CLAMS effects in the paper

## Slide 24: Take Away Messages
Variation in average memory access latencies across the GPU cores, makes some GPU cores more “critical” than others.
Memory schedulers being agnostic to the criticality of GPU cores can lead to sub-optimal performance
We need to orchestrate the exploitation of core-criticality and DRAM locality
Dyn-CLAMS provides an average performance improvement of 8.4%.

## Slide 25
Exploiting Core Criticality for Enhanced GPU Performance
Adwait Jog, Onur Kayıran, Ashutosh Pattnaik,
Mahmut T. Kandemir, Onur Mutlu,
Ravishankar Iyer, Chita R. Das.
SIGMETRICS ‘16

## Slide 26: Backup Slides

## Slide 27: Design of Semi-Dyn-CLAMS
Lets look at CONS
Assume ThSM = 40%, and ThCR can take any value in {1,4,7}.
ThCR = 4, is chosen. Scheduler works in criticality mode most of the time.
Chart: Percentage of Requests
Time
1

## Slide 28
Initialize ThSM = 40%, and ThCR = 8
Calculate ThCR based on Semi-Dyn-CLAMS
  ThCR updated to 4
Update ThSM to new value of PCR(ThCR)
  Similar to the curve of PCR(4)
  With the reduction of ThSM, chances of scheduler going to locality mode increase
Design of Dyn-CLAMS
Chart: Percentage of Requests
Time
ThSM
1
3
1
3

## Slide 29: Take Away Messages
Memory schedulers being agnostic to the criticality of GPU cores can lead to sub-optimal performance
  Variation in average memory access latencies across the GPU cores, makes some GPU cores more “critical” than others.
Core criticality aware memory system is required for enhanced GPU performance
  Percentage of Critical Cores (PCC) is a good proxy to measure Percentage of Critical Requests (PCR) which defines the criticality of a GPU core.
  Dynamically choosing between either exploiting core-criticality or DRAM locality
Dyn-CLAMS provides an average performance improvement of 8.4% across Group-A applications.

## Slide 30: Scheme Runtime Plots

## Slide 31
Chart: 
Time
ThSM = 40%
ThSM = 80%
Chart: 
Time
ThSMinit = 40%
ThSMinit = 80%
Chart: Criticality-Rank Threshold a
Time
A
B
B
ThSM = 40%
ThSM = 80%
(ThCR )
Chart: Scheduling Mode Threshold a
Time
B
B
ThSMinit = 40%
ThSMinit = 80%
(ThSM )

## Slide 32: Results

## Slide 33
Chart: Normalized Core Stall Cycles
| LUH | RED | SCAN | LPS | RAY | CONS | SCP | BLK | HS | CFD | GAUSS | GMEAN | GMEAN-A
Static-CLAMS | 0.92843 | 0.97449 | 0.96588 | 0.93859 | 0.99599 | 0.94405 | 0.99996 | 0.96071 | 0.94538 | 0.99392 | 0.98845 | 0.96659 | 0.95826
Semi-Dyn-CLAMS | 0.9298 | 0.82635 | 0.95025 | 0.91667 | 0.98951 | 0.94253 | 1.0467 | 0.98475 | 0.91211 | 0.99661 | 1.0018 | 0.95257 | 0.93316
Dyn-CLAMS | 0.89661 | 0.83974 | 0.96392 | 0.91769 | 0.97338 | 0.93854 | 0.99059 | 0.95974 | 0.90433 | 0.99547 | 0.98293 | 0.94093 | 0.92322
Chart: Normalized Row Buffer Hit Rate
| LUH | RED | SCAN | LPS | RAY | CONS | SCP | BLK | HS | CFD | GAUSS | GMEAN | GMEAN-A
Static-CLAMS | 0.92575 | 0.87015 | 0.94611 | 0.96269 | 0.92521 | 0.94545 | 0.99204 | 0.98721 | 0.98501 | 0.9986 | 0.99862 | 0.95711 | 0.93961
Semi-Dyn-CLAMS | 0.86571 | 0.69104 | 0.89887 | 0.93695 | 0.86621 | 0.92221 | 0.70799 | 0.71356 | 0.95954 | 0.97425 | 0.99681 | 0.85965 | 0.83085
Dyn-CLAMS | 0.89694 | 0.7923 | 0.9405 | 0.91125 | 0.91221 | 0.95619 | 0.93196 | 0.90818 | 0.97148 | 0.99744 | 0.99873 | 0.92715 | 0.90316
Chart: Normalized Critical Latency
| LUH | RED | SCAN | LPS | RAY | CONS | SCP | BLK | HS | CFD | GAUSS | GMEAN | GMEAN-A
Static-CLAMS | 0.87278 | 0.62569 | 0.58669 | 0.70723 | 0.43183 | 0.56552 | 0.91406 | 0.97927 | 0.8343 | 1.0023 | 0.92771 | 0.74358 | 0.69948
Semi-Dyn-CLAMS | 0.86329 | 0.42525 | 0.64914 | 0.69312 | 0.47482 | 0.5269 | 0.61621 | 0.89635 | 0.81977 | 1.0211 | 1.003 | 0.69801 | 0.61409
Dyn-CLAMS | 0.87405 | 0.49612 | 0.66721 | 0.68078 | 0.5722 | 0.64828 | 0.72266 | 0.94225 | 0.8343 | 1.0575 | 1.0361 | 0.75507 | 0.67223

## Slide 34
Chart: Percentage of DRAM Cycles
| FR-FCFS | Dyn-CLAMS | FR-FCFS | Dyn-CLAMS | FR-FCFS | Dyn-CLAMS | FR-FCFS | Dyn-CLAMS | FR-FCFS | Dyn-CLAMS | FR-FCFS | Dyn-CLAMS | FR-FCFS | Dyn-CLAMS | FR-FCFS | Dyn-CLAMS | FR-FCFS | Dyn-CLAMS | FR-FCFS | Dyn-CLAMS | FR-FCFS | Dyn-CLAMS | LUH | RED | SCAN | LPS | RAY | CONS | SCP | BLK | HS | CFD | GAUSS
App-BW | 0.74052 | 0.80333 | 0.85302 | 0.9514 | 0.6983 | 0.71375 | 0.71497 | 0.75768 | 0.62325 | 0.7122 | 0.82737 | 0.86263 | 0.8733 | 0.89328 | 0.84422 | 0.87288 | 0.54415 | 0.56725 | 0.4721 | 0.47338 | 0.54353 | 0.55288
Waste-BW | 0.11065 | 0.13078 | 0.0086163 | 0.0096101 | 0.11368 | 0.09733 | 0.23832 | 0.21371 | 0.13681 | 0.15634 | 0.14601 | 0.10662 | 0.055743 | 0.057018 | 0.14898 | 0.11903 | 0.30608 | 0.31908 | 0.28935 | 0.29014 | 0.2442 | 0.2484
Idle-BW | 0.14883 | 0.065891 | 0.13837 | 0.03899 | 0.18802 | 0.18892 | 0.046711 | 0.028611 | 0.23994 | 0.13146 | 0.026627 | 0.030749 | 0.070957 | 0.049699 | 0.0068039 | 0.0080871 | 0.14977 | 0.11367 | 0.23855 | 0.23648 | 0.21227 | 0.19872
Useful-BW
Wasted-BW