## Slide 1: Exploiting Latency and Error Tolerance of GPGPU Applications for an Energy-efficient DRAM
Haonan Wang, Adwait Jog
College of William & Mary

## Slide 2: The Problem of Memory System Energy
Memory system consumes a large of fraction of GPU total energy.
Quadro 5600
GTX480
Memory power consumption is an impediment for further scaling.
2. O'Connor, Mike, et al. “Fine-grained DRAM: energy-efficient DRAM for extreme bandwidth systems.” MICRO2017
1. J. Leng, et al. “GPUWattch: Enabling Energy Optimizations in GPGPUs.” ISCA2013.
Non-linear increase!
Notes: Nowadays, memory energy consumption has become one of the biggest problems for GPUs.
The power supply is limited. However, the power increases non-linearly with increased bandwidth.
ICS

## Slide 3: Source of Memory Energy Consumption
Row Buffer Locality (RBL) =
# Row Buffer Data Reuse per Row Activation
Row open:
Activation
Row close:
Restore & Precharge
Expensive
Row Buffer
Memory Array
Higher RBL  Better Energy Efficiency
Notes: Stress more on rbl
Expensive -> reduce -> increase RBL -> RBL definition

## Slide 4: Row Energy Dominates Memory Energy
1. O'Connor, Mike, et al. "Fine-grained DRAM: energy-efficient DRAM for extreme bandwidth systems." MICRO2017
Reducing row energy is the key for reducing the overall memory energy consumption.
HBM energy proportions for different Row-Locality:
Notes: As shown by prior works,

## Slide 5: Goal & Solution
Goal: Improving GPU memory energy efficiency by enhancing the Row Buffer Locality of GPU memory
Solution: Designing novel memory scheduling techniques (Lazy Memory Scheduling)
  Delayed Memory Scheduling (DMS): utilizes the delay tolerance feature of GPGPU applications.
  Approximate Memory Scheduling (AMS): utilizes the error tolerance feature and non-uniform RBL distributions of GPGPU applications.
Notes: Use more colors

## Slide 6: Outline
Background & Motivation
Design of AMS & DMS
Evaluation
Conclusion

## Slide 7: Memory Row Operations
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 1, Column 0)
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address: Row Operation:
Similar behaviors exist in newer memory technologies like HBM and HBM2.
R0
R0
R1
Activation
Restore, Precharge, Activation
No operation
RBL=2
RBL=1
1. Credit: Onur Mutlu.
Notes: Reduce accesses
Stress R0 has row of 0

## Slide 8
……
RBL & Memory Scheduling Schemes in GPUs
Activation Counter:
R1: Activation = 1
R5: Activation = 2
R1: Activation = 3
R5: Activation = 4
R5: Activation = 4
Avg RBL = 5 / 4 = 1.25
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
In-order scheduling
(FIFO):
Request Stream
R5
……
Activation Counter:
R1: Activation = 1
R1: Activation = 1
R5: Activation = 2
R5: Activation = 2
R5: Activation = 2
Avg RBL = 5 / 2 = 2.5
……
requests currently
in the pending queue
oldest
request
R1
R5
R1
R5
future
requests
R2
R4
R3
Out-of-order scheduling
(FR-FCFS):
Request Stream
R5
Visible to the memory scheduler
Same
activation
Same
activation
Same
activation
Notes: introducing what is r1
Note that only requests in the pending queue are visible to the memory controller, and the pending queue has a capacity limit.

## Slide 9
How can we further improve the RBL?

## Slide 10: Observation I: Latency Tolerance
Many GPGPU applications are latency-tolerant and have different delay-tolerance levels.
95% Threshold
Numbers in the brackets are the applied delay
The average IPC of all applications does not drop below 95% with 256 cycles delay.
The IPC for each applications does not drop below 95% with 128 cycles delay.

## Slide 11: Motivation: Delayed Memory Scheduling (DMS)
……
……
requests currently
in the pending queue
oldest
request
R1
R2
R3
R4
future
requests
R2
request
X cycles away
R4
R3
R1
For R1 through R4:
Activations = 8
Requests = 8
Avg Locality = 8/8 = 1
……
……
requests currently
in the pending queue
request stalled
for X cycles
R1
R2
R3
R4
future
requests
R2
R4
R3
R1
For R1 through R4:
Activations = 4
Requests = 8
Avg Locality = 8/4 = 2
No delay:
With delay:
Request Stream
Request Stream
Visible to the memory scheduler
Visible to the memory scheduler
Notes: intuition

## Slide 12: Motivation: Delayed Memory Scheduling (DMS)
The average RBL of many GPGPU applications can be improved via adding delay:
Numbers in the brackets are the applied delay
Normalized
number of row activations
(lower the better)
More Delay  More Visibility  Less Activations
Notes: Based on the previous intuition,

## Slide 13: Observation II: Non-uniform RBL distribution
Many GPGPU applications have non-uniform RBL distributions.
Correlation of RBL and their corresponding read requests:
proportion of requests
Proportion of Activations
Number in the brackets is the RBL of an activation
Small proportions of requests can be approximated to reduce large proportions of activations
-- Approximate Memory Scheduling (AMS)
Notes: Correlation of RBL and their corresponding requests (read requests only).

## Slide 14: Approximate Memory Scheduling (AMS)
……
requests currently
In the pending queue
oldest
request
R1
R2
R1
R1
future
requests
R3
For R1 through R3:
If no request is dropped from the pending queue:
Activations = 3
Requests = 5
Avg Locality = 5/3 = 1.67
Request Stream
Visible to the memory scheduler
Given a coverage budget, AMS drops requests with low RBLs (user specified).
If one request with RBL<2 is dropped & approximated:
Activations = 2
Requests = 4
Avg Locality = 4/2 = 2
Notes: the oldest requests will be dropped for requests with the same RBL.

## Slide 15: Cooperation: DMS Can Help AMS
……
requests currently
In the pending queue
oldest
request
R1
R2
R3
R4
future
requests
R5
R2
R4
R3
R1
For R1 through R5:
If the oldest is dropped:
Activations = 5
Requests = 8
Avg Locality = 8/5 = 1.6
request
4 cycles away
……
requests currently
In the pending queue
R1
R2
R3
R4
future
requests
R5
For R1 through R5:
If the request to
R5 is dropped:
Activations = 4
Requests = 8
Avg Locality = 8/4 = 2
R2
R4
R3
R1
request stalled
for 4 cycles
AMS & No DMS:
AMS & DMS:
Request Stream
Request Stream
Visible to the memory scheduler
DMS can increase the visibility of requests for AMS.
Visible to the memory scheduler
Notes: Visibility is improved.

## Slide 16: Cooperation: AMS Can Help DMS
Application LPS
Metric names
AMS is able to increase the maximum delay used in DMS.

## Slide 17: Outline
Background & Motivation
Design of AMS & DMS
Evaluation
Conclusion

## Slide 18: Design Overview
AMS Unit
DMS Unit
Dropped
Reads
Main Memory
…
Bank
Row Buffer
Cell Arrays
……
Pending Queue
Interconnect
L2 Cache
Value
Predictor
Issued
Requests
L2 Misses
Timestamp
Address &
Read/Write
Request Metadata
Address
…
Read/Write
Timestamp
Memory
Controller
Normal
Reads
R1
R3
R2

## Slide 19: DMS Design: Static-DMS & Dynamic-DMS
Static-DMS: Using a static Delay-threshold
Does not work well for all applications
Not fine-grained
Dyn-DMS: Adjusting the Delay-threshold based on the current bandwidth utilization (BWUTIL)
Adjust Delay-threshold according to the Delay-tolerance of the application
Fine-grained tuning based on BWUTIL profiling
Correlation of BWUTIL & IPC:

## Slide 20: AMS Design: Static-AMS
Under a coverage budget, activations with RBLs <= static threshold will be dropped:
Does not work well for all applications
Number in the bracket is the RBL for an Activation
10% coverage budget
Application SCP:
proportion of requests
Proportion of Activations
Static RBL-threshold = 8

## Slide 21: AMS Design: Dynamic-AMS
Reducing the RBL-threshold based on the current prediction coverage:
Adjust RBL-threshold according to the RBL distribution of the application
Application SCP:
RBL-threshold
(to drop request)
Normalized number of row activations
(lower the better)
With same coverage: Lower RBL-threshold  Less Activations
Notes: Therefore, the dynamic ams tries to reduce the RBL threshold as much as possible whiling maintaining the prediction coverage.

## Slide 22: Value Prediction Unit
Prior works can further improve the prediction accuracy:
Load Value Approximation (MICRO’14), Doppelganger (MICRO’15),
RFVP (TACO’16), Bunker Cache (MICRO’16)
Baseline Output
Approximate Output
Our simple approach --- uses cache lines with closest addresses for approximation
Approximate Output
Notes: As these works shows good prediction accuracy meanwhile significantly improving the performance.
3 are from micro and 1 is from taco.

## Slide 23: Outline
Background & Motivation
Design of AMS & DMS
Evaluation
Conclusion

## Slide 24: Evaluation Methodology
Evaluated using GPGPU-Sim -- a cycle accurate GPGPU simulator
Baseline Configuration
  30 SMs, 32-SIMT Lanes, 32 Threads/Warp, 48 Warps/SM
  16KB L1 (4-way, 128B Cache Block) + 32KB Shared Memory per SM
  256KB L2 (8-way, 128B Cache Block) per Memory Partition
  6 GDDR5 Memory Partitions, 16 Banks/Partition, FR-FCFS, Open-row policy
  1 Crossbar/Direction
Workloads -- 20 Applications
  From CUDA SDK, Polybench and Axbench
  Divided into different groups based on their characteristics
  Contains both Error-tolerant and Non-error-tolerant applications

## Slide 25: Error Tolerant Applications: Row Energy
Static-DMS: 8%
Dyn-DMS: 12%
Static-AMS: 33%
Dyn-AMS: 33%
Applications with 10% coverage:
Static-AMS: 7%
Dyn-AMS: 11%
Static-DMS & Static-AMS: 42%
Dyn-DMS & Dyn-AMS: 44%
Individual schemes:
Combined schemes:

## Slide 26: Error-tolerant Applications: IPC & Error
Application Error:
Performance:
95% Threshold
20% Threshold

## Slide 27: Non-error-tolerant Applications: Row Energy & IPC
Non-error-tolerant Applications can run in Delay-only mode:
95% Threshold

## Slide 28: Conclusions
Problem: GPU memory energy consumption
Goal: Improving the Row Buffer Locality
Contributions:
Lazy Memory Scheduler
  Delayed Memory Scheduling (DMS): delaying the scheduling of memory requests can significantly improve the overall row buffer locality
  Approximate Memory Scheduling (AMS): approximating a small fraction of memory requests can reduce a large fraction of row activations (i.e., there is non-uniform reuse of row buffers)
Lazy Memory Scheduler reduces row energy by 44% with less than 1% IPC loss across a variety of GPGPU applications

## Slide 29: Thank You! Questions?
We acknowledge the support of the National Science Foundation (NSF) grants (#1657336, #1717532 and #1750667)

## Slide 30: Backup Slides

## Slide 31: Effect of Pending Queue Size
Normalized Row Activations for different pending queue sizes (baseline is 128):
The Row Activation Reduction is limited for many applications even with large pending queue size.
Number of Activations stops reducing after size 128 (red line)
Pending queue size
The capacity of the pending queue can limit the re-ordering ability of FR-FCFS.

## Slide 32: Effect of Pending Queue Size Under Delay
Effect of pending queue size with maximum delay (2048 cycles):
For almost all applications, queue size 128 is sufficient even with the maximum delay of DMS.
Pending queue size