## Slide 1: Neither More Nor Less: Optimizing Thread-level Parallelism for GPGPUs
Onur Kayıran, Adwait Jog, Mahmut Kandemir, Chita R. Das

## Slide 2: GPU Computing
GPUs are known for providing high thread-level parallelism (TLP).
Core
Uni-processors
Core
Core
Core
Core
Multi-cores
...
...
Many-cores, GPUs

## Slide 3: “Too much of anything is bad, but too much good whiskey is barely enough” - Mark Twain

## Slide 4: Executive Summary
Current state-of-the-art thread-block schedulers make use of the maximum available TLP
More threads → more memory requests
Contention in memory sub-system
Improves average application performance by 28%
Proposal:
A thread-block scheduling algorithm
Optimizes TLP and reduces memory sub-system contention

## Slide 5: Outline
Proposal
Background
Motivation
DYNCTA
Evaluation
Conclusions

## Slide 6: GPU Architecture
DRAM
SIMT Cores
Warp Scheduler
ALUs
L1 Caches
Threads
W
W
W
W
W
W
Warps
L2 cache
Interconnect
CTA
CTA
CTA
CTA
Cooperative
Thread
Arrays
(CTAs)
CTA Scheduler

## Slide 7: GPU Scheduling
Warp Scheduler
Warp Scheduler
CTA
CTA
CTA
CTA
Warp Scheduler
CTA Scheduler
CTA Scheduler
Warp Scheduler
Pipeline
Pipeline
W
W
W
W
W
W
W
W
CTA
CTA

## Slide 8: Properties of CTAs
Threads within a CTA synchronize using barriers.
There is no synchronization across threads belonging to different CTAs.
CTAs can be distributed to cores in any order.
Once assigned to a core, a CTA cannot be preempted.
Threads
CTA
barrier

## Slide 9: Properties of CTAs
The number of CTAs executing on a core is limited by:
  the number of threads per CTA
  the amount of shared memory per core
  the number of registers per core
  a hard limit (depends on CUDA version for NVIDIA GPUs)
  the resources required by the application kernel
These factors in turn limit the available TLP on the core.
By default, if available, a core executes maximum number of CTAs.

## Slide 10: Outline
Proposal
Background
Motivation
DYNCTA
Evaluation
Conclusions

## Slide 11: Effect of TLP on GPGPU Performance
Chart: Normalized IPC
| PVC | SSC | IIX | BFS | SAD | PFF | LUD | SPMV | NW | MUM | KM | WP | SCP | PVR | AES | LIB | NQU | FFT | SD2 | BP | JPEG | BLK | RAY | SD1 | LKC | PFN | HOT | NN | MM | STO | CP | avg
Minimum TLP | 3.3086 | 0.98568 | 4.9218 | 1.0549 | 1.8773 | 0.9964 | 1 | 1.4022 | 0.61014 | 1.0598 | 2.3929 | 0.7379 | 1.1058 | 0.92623 | 1.2285 | 0.52964 | 1.0005 | 1.0557 | 0.90059 | 0.99241 | 0.52197 | 0.74988 | 1.1531 | 0.96833 | 1.0239 | 0.79719 | 0.91141 | 0.21558 | 0.74366 | 0.86565 | 0.96894 | 1.1938
Optimal TLP | 3.4679 | 1 | 4.9218 | 1.0787 | 3.0367 | 1.0034 | 1 | 1.4872 | 1 | 1.0598 | 2.3929 | 1 | 1.1058 | 1.0577 | 1.2285 | 1 | 1.0005 | 1.3551 | 1 | 1.1534 | 1.1048 | 1.0463 | 1.4113 | 1 | 1.0357 | 1 | 1.0105 | 1.0014 | 1 | 1 | 1.2144 | 1.3927
19%
39% potential improvement

## Slide 12: Effect of TLP on GPGPU Performance
Chart: Normalized IPC
| PVC | SSC | IIX | BFS | SAD | PFF | LUD | SPMV | NW | MUM | KM | WP | SCP | PVR | AES | LIB | NQU | FFT | SD2 | BP | JPEG | BLK | RAY | SD1 | LKC | PFN | HOT | NN | MM | STO | CP | avg
Minimum TLP | 3.3086 | 0.98568 | 4.9218 | 1.0549 | 1.8773 | 0.9964 | 1 | 1.4022 | 0.61014 | 1.0598 | 2.3929 | 0.7379 | 1.1058 | 0.92623 | 1.2285 | 0.52964 | 1.0005 | 1.0557 | 0.90059 | 0.99241 | 0.52197 | 0.74988 | 1.1531 | 0.96833 | 1.0239 | 0.79719 | 0.91141 | 0.21558 | 0.74366 | 0.86565 | 0.96894 | 1.1938
Optimal TLP | 3.4679 | 1 | 4.9218 | 1.0787 | 3.0367 | 1.0034 | 1 | 1.4872 | 1 | 1.0598 | 2.3929 | 1 | 1.1058 | 1.0577 | 1.2285 | 1 | 1.0005 | 1.3551 | 1 | 1.1534 | 1.1048 | 1.0463 | 1.4113 | 1 | 1.0357 | 1 | 1.0105 | 1.0014 | 1 | 1 | 1.2144 | 1.3927
Chart: Active Time Ratio (RACT)
| PVC | SSC | IIX | BFS | SAD | PFF | LUD | SPMV | NW | MUM | KM | WP | SCP | PVR | AES | LIB | NQU | FFT | SD2 | BP | JPEG | BLK | RAY | SD1 | LKC | PFN | HOT | NN | MM | STO | CP | avg
RACT | 0.07176 | 0.072179 | 0.08 | 0.14854 | 0.14985 | 0.15304 | 0.17626 | 0.19361 | 0.2316 | 0.23378 | 0.23554 | 0.35586 | 0.41722 | 0.45975 | 0.46119 | 0.49176 | 0.55403 | 0.56519 | 0.61474 | 0.62557 | 0.6326 | 0.73901 | 0.74852 | 0.7585 | 0.86212 | 0.89006 | 0.92937 | 0.94031 | 0.97023 | 0.9743 | 0.98598 | 0.50718
16%
51%
95% potential improvement

## Slide 13: Why is not more TLP always optimal?
Chart: AES
IPC | 1.2285 | 1.0666 | 1.0702 | 1
Chart: AES
IPC | 1.2285 | 1.0666 | 1.0702 | 1
lat. | 0.1423 | 0.38324 | 0.68398 | 1
Chart: MM
IPC | 0.74366 | 0.98276 | 0.98561 | 0.98559 | 0.98768 | 0.99188 | 0.99698 | 1
Chart: MM
IPC | 0.74366 | 0.98276 | 0.98561 | 0.98559 | 0.98768 | 0.99188 | 0.99698 | 1
lat. | 1 | 0.82143 | 0.89286 | 0.96429 | 1 | 0.96429 | 0.96429 | 1
Chart: JPEG
IPC | 0.52197 | 0.9127 | 1.1048 | 1.0916 | 1.0798 | 1.0617 | 1.0645 | 1
Chart: JPEG
IPC | 0.52197 | 0.9127 | 1.1048 | 1.0916 | 1.0798 | 1.0617 | 1.0645 | 1
lat. | 0.09621 | 0.15743 | 0.23615 | 0.34694 | 0.52478 | 0.60058 | 0.76968 | 1
Chart: CP
IPC | 0.96894 | 1.094 | 1.2144 | 1.0979 | 1.099 | 1.1001 | 1.0991 | 1
Chart: CP
IPC | 0.96894 | 1.094 | 1.2144 | 1.0979 | 1.099 | 1.1001 | 1.0991 | 1
lat. | 0.1115 | 0.17422 | 0.26829 | 0.4216 | 0.50174 | 0.62369 | 0.78746 | 1

## Slide 14: Why is not more TLP always optimal?
More threads result in larger working data set
  Causes cache contention
More L1 misses cause more network injections
  Network latency increases
Chart: BP
| 1 | 2 | 3 | 4
L1 data miss rate | 0.67176 | 0.69618 | 0.86107 | 1
Chart: BP
| 1 | 2 | 3 | 4
L1 data miss rate | 0.67176 | 0.69618 | 0.86107 | 1
Network lat. | 0.13307 | 0.38794 | 0.68564 | 1

## Slide 15: Outline
Proposal
Background
Motivation
DYNCTA
Evaluation
Conclusions

## Slide 16: DYNCTA Approach
Execute the optimal number of CTAs for each application
Requires exhaustive analysis for each application, thus inapplicable
Idea:
Dynamically modulate the number of CTAs on each core using the CTA scheduler

## Slide 17: DYNCTA Approach
Objective 1: keep the cores busy
  If a core has nothing to execute, give more threads to it
Objective 2: do not keep the cores TOO BUSY
  If the memory sub-system is congested due to high number of threads, lower TLP to reduce contention
  If the memory sub-system is not congested, increase TLP to improve latency tolerance

## Slide 18: DYNCTA Approach
Objective 1: keep the cores busy
  Monitor C_idle, the number of cycles during which a core does not have anything to execute
  If it is high, increase the number of CTAs executing on the core
Objective 2: do not keep the cores TOO BUSY
  Monitor C_mem, the number of cycles during which a core is waiting for the data to come back from memory
  If it is low, increase the number of CTAs executing on the core
  If it is high, decrease the number of CTAs executing on the core

## Slide 19: DYNCTA Overview
L
H
H
M
L
C_mem
C_idle
Increase # of CTAs
Decrease # of CTAs
No change in # of CTAs

## Slide 20: CTA Pausing
Warps of the most recently assigned CTA are deprioritized
in the warp scheduler
Once assigned to a core, a CTA cannot be preempted!
Then, how to decrement the number of CTAs ?
CTA
PAUSE

## Slide 21: Outline
Proposal
Background
Motivation
DYNCTA
Evaluation
Conclusions

## Slide 22: Evaluation Methodology
Evaluated on GPGPU-Sim, a cycle accurate GPU simulator
Baseline Architecture
  30 SIMT cores, 8 memory controllers, crossbar connected
  1300MHz, SIMT Width = 8, Max. 1024 threads/core
  32 KB L1 data cache, 8 KB Texture and Constant Caches
  GDDR3 800MHz
Applications Considered (in total 31) from:
  Map Reduce Applications
  Rodinia – Heterogeneous Applications
  Parboil – Throughput Computing Focused Applications
  NVIDIA CUDA SDK – GPGPU Applications

## Slide 23: Dynamism
Chart: Average Number of CTAs
Default number of CTAs
Optimal number of CTAs
Chart: Active Time Ratio

## Slide 24: Dynamism
Chart: Average Number of CTAs
Default number of CTAs
Optimal number of CTAs
Chart: Active Time Ratio

## Slide 25: Average Number of CTAs
Chart: Average Number of CTAs/core
| PVC | SSC | IIX | BFS | SAD | PFF | LUD | SPMV | NW | MUM | KM | WP | SCP | PVR | AES | LIB | NQU | FFT | SD2 | BP | JPEG | BLK | RAY | SD1 | LKC | PFN | HOT | NN | MM | STO | CP | avg
Default | 4 | 4 | 4 | 4 | 8 | 2 | 4 | 8 | 8 | 4 | 4 | 8 | 4 | 4 | 4 | 8 | 2 | 8 | 4 | 4 | 8 | 8 | 6 | 2 | 5 | 8 | 4 | 8 | 8 | 2 | 8 | 5.3871
DYNCTA | 1.902 | 1.0965 | 1.9735 | 1.2984 | 4.279 | 1 | 1 | 2.9809 | 2.603 | 1.6252 | 1.7786 | 2.2451 | 1.9513 | 2.1184 | 2.8233 | 2.141 | 1.1831 | 3.7861 | 1.7627 | 2.4903 | 3.1682 | 2.4323 | 4.7203 | 1.6898 | 3.6986 | 1.8766 | 3.6104 | 7.1721 | 4 | 1.9182 | 7.0806 | 2.6905
Optimal TLP | 2 | 4 | 1 | 2 | 4 | 2 | 2 | 2 | 5 | 1 | 1 | 3 | 1 | 3 | 1 | 3 | 1 | 3 | 4 | 3 | 3 | 4 | 2 | 2 | 2 | 8 | 3 | 6 | 8 | 2 | 3 | 2.9355
5.4
Chart: Average Number of CTAs/core
| PVC | SSC | IIX | BFS | SAD | PFF | LUD | SPMV | NW | MUM | KM | WP | SCP | PVR | AES | LIB | NQU | FFT | SD2 | BP | JPEG | BLK | RAY | SD1 | LKC | PFN | HOT | NN | MM | STO | CP | avg
Default | 4 | 4 | 4 | 4 | 8 | 2 | 4 | 8 | 8 | 4 | 4 | 8 | 4 | 4 | 4 | 8 | 2 | 8 | 4 | 4 | 8 | 8 | 6 | 2 | 5 | 8 | 4 | 8 | 8 | 2 | 8 | 5.3871
DYNCTA | 1.902 | 1.0965 | 1.9735 | 1.2984 | 4.279 | 1 | 1 | 2.9809 | 2.603 | 1.6252 | 1.7786 | 2.2451 | 1.9513 | 2.1184 | 2.8233 | 2.141 | 1.1831 | 3.7861 | 1.7627 | 2.4903 | 3.1682 | 2.4323 | 4.7203 | 1.6898 | 3.6986 | 1.8766 | 3.6104 | 7.1721 | 4 | 1.9182 | 7.0806 | 2.6905
Optimal TLP | 2 | 4 | 1 | 2 | 4 | 2 | 2 | 2 | 5 | 1 | 1 | 3 | 1 | 3 | 1 | 3 | 1 | 3 | 4 | 3 | 3 | 4 | 2 | 2 | 2 | 8 | 3 | 6 | 8 | 2 | 3 | 2.9355
2.9
Chart: Average Number of CTAs/core
| PVC | SSC | IIX | BFS | SAD | PFF | LUD | SPMV | NW | MUM | KM | WP | SCP | PVR | AES | LIB | NQU | FFT | SD2 | BP | JPEG | BLK | RAY | SD1 | LKC | PFN | HOT | NN | MM | STO | CP | avg
Default | 4 | 4 | 4 | 4 | 8 | 2 | 4 | 8 | 8 | 4 | 4 | 8 | 4 | 4 | 4 | 8 | 2 | 8 | 4 | 4 | 8 | 8 | 6 | 2 | 5 | 8 | 4 | 8 | 8 | 2 | 8 | 5.3871
DYNCTA | 1.902 | 1.0965 | 1.9735 | 1.2984 | 4.279 | 1 | 1 | 2.9809 | 2.603 | 1.6252 | 1.7786 | 2.2451 | 1.9513 | 2.1184 | 2.8233 | 2.141 | 1.1831 | 3.7861 | 1.7627 | 2.4903 | 3.1682 | 2.4323 | 4.7203 | 1.6898 | 3.6986 | 1.8766 | 3.6104 | 7.1721 | 4 | 1.9182 | 7.0806 | 2.6905
Optimal TLP | 2 | 4 | 1 | 2 | 4 | 2 | 2 | 2 | 5 | 1 | 1 | 3 | 1 | 3 | 1 | 3 | 1 | 3 | 4 | 3 | 3 | 4 | 2 | 2 | 2 | 8 | 3 | 6 | 8 | 2 | 3 | 2.9355
2.7

## Slide 26: IPC
Chart: Normalized IPC
| PVC | SSC | IIX | BFS | SAD | PFF | LUD | SPMV | NW | MUM | KM | WP | SCP | PVR | AES | LIB | NQU | FFT | SD2 | BP | JPEG | BLK | RAY | SD1 | LKC | PFN | HOT | NN | MM | STO | CP | avg
TL | 3.3301 | 0.94625 | 1.2623 | 1.0105 | 1.323 | 1.009 | 1 | 1.0325 | 1 | 1.0741 | 1.472 | 0.99809 | 1.0023 | 1.0624 | 1.0128 | 0.9998 | 1.0005 | 0.99653 | 1.0252 | 1.0438 | 1.0265 | 1.2324 | 1.167 | 1.0088 | 1.0226 | 0.98106 | 1.0157 | 1.0073 | 1.0058 | 1.0008 | 1.0969 | 1.1344
DYNCTA | 3.5653 | 0.99694 | 2.8547 | 1.1153 | 2.9367 | 1.0019 | 1 | 1.1698 | 0.97861 | 1.0367 | 1.9242 | 1 | 0.96755 | 1.0258 | 1.1455 | 1 | 1.0005 | 1.2868 | 1.0167 | 1.1642 | 1.0838 | 0.97924 | 1.0832 | 1.0246 | 1.0191 | 0.97533 | 1.0007 | 0.98537 | 0.98559 | 1.0673 | 1.1903 | 1.2768
Optimal TLP | 3.4679 | 1 | 4.9218 | 1.0787 | 3.0367 | 1.0034 | 1 | 1.4872 | 1 | 1.0598 | 2.3929 | 1 | 1.1058 | 1.0577 | 1.2285 | 1 | 1.0005 | 1.3551 | 1 | 1.1534 | 1.1048 | 1.0463 | 1.4113 | 1 | 1.0357 | 1 | 1.0105 | 1.0014 | 1 | 1 | 1.2144 | 1.3927
39%
Chart: Normalized IPC
| PVC | SSC | IIX | BFS | SAD | PFF | LUD | SPMV | NW | MUM | KM | WP | SCP | PVR | AES | LIB | NQU | FFT | SD2 | BP | JPEG | BLK | RAY | SD1 | LKC | PFN | HOT | NN | MM | STO | CP | avg
TL | 3.3301 | 0.94625 | 1.2623 | 1.0105 | 1.323 | 1.009 | 1 | 1.0325 | 1 | 1.0741 | 1.472 | 0.99809 | 1.0023 | 1.0624 | 1.0128 | 0.9998 | 1.0005 | 0.99653 | 1.0252 | 1.0438 | 1.0265 | 1.2324 | 1.167 | 1.0088 | 1.0226 | 0.98106 | 1.0157 | 1.0073 | 1.0058 | 1.0008 | 1.0969 | 1.1344
DYNCTA | 3.5653 | 0.99694 | 2.8547 | 1.1153 | 2.9367 | 1.0019 | 1 | 1.1698 | 0.97861 | 1.0367 | 1.9242 | 1 | 0.96755 | 1.0258 | 1.1455 | 1 | 1.0005 | 1.2868 | 1.0167 | 1.1642 | 1.0838 | 0.97924 | 1.0832 | 1.0246 | 1.0191 | 0.97533 | 1.0007 | 0.98537 | 0.98559 | 1.0673 | 1.1903 | 1.2768
Optimal TLP | 3.4679 | 1 | 4.9218 | 1.0787 | 3.0367 | 1.0034 | 1 | 1.4872 | 1 | 1.0598 | 2.3929 | 1 | 1.1058 | 1.0577 | 1.2285 | 1 | 1.0005 | 1.3551 | 1 | 1.1534 | 1.1048 | 1.0463 | 1.4113 | 1 | 1.0357 | 1 | 1.0105 | 1.0014 | 1 | 1 | 1.2144 | 1.3927
13%
Chart: Normalized IPC
| PVC | SSC | IIX | BFS | SAD | PFF | LUD | SPMV | NW | MUM | KM | WP | SCP | PVR | AES | LIB | NQU | FFT | SD2 | BP | JPEG | BLK | RAY | SD1 | LKC | PFN | HOT | NN | MM | STO | CP | avg
TL | 3.3301 | 0.94625 | 1.2623 | 1.0105 | 1.323 | 1.009 | 1 | 1.0325 | 1 | 1.0741 | 1.472 | 0.99809 | 1.0023 | 1.0624 | 1.0128 | 0.9998 | 1.0005 | 0.99653 | 1.0252 | 1.0438 | 1.0265 | 1.2324 | 1.167 | 1.0088 | 1.0226 | 0.98106 | 1.0157 | 1.0073 | 1.0058 | 1.0008 | 1.0969 | 1.1344
DYNCTA | 3.5653 | 0.99694 | 2.8547 | 1.1153 | 2.9367 | 1.0019 | 1 | 1.1698 | 0.97861 | 1.0367 | 1.9242 | 1 | 0.96755 | 1.0258 | 1.1455 | 1 | 1.0005 | 1.2868 | 1.0167 | 1.1642 | 1.0838 | 0.97924 | 1.0832 | 1.0246 | 1.0191 | 0.97533 | 1.0007 | 0.98537 | 0.98559 | 1.0673 | 1.1903 | 1.2768
Optimal TLP | 3.4679 | 1 | 4.9218 | 1.0787 | 3.0367 | 1.0034 | 1 | 1.4872 | 1 | 1.0598 | 2.3929 | 1 | 1.1058 | 1.0577 | 1.2285 | 1 | 1.0005 | 1.3551 | 1 | 1.1534 | 1.1048 | 1.0463 | 1.4113 | 1 | 1.0357 | 1 | 1.0105 | 1.0014 | 1 | 1 | 1.2144 | 1.3927
28%

## Slide 27: Outline
Proposal
Background
Motivation
DYNCTA
Evaluation
Conclusions

## Slide 28: Conclusions
Maximizing TLP is not always optimal in terms of performance
We propose a CTA scheduling algorithm, DYNCTA, that optimizes TLP at the cores based on application characteristics
DYNCTA reduces cache, network and memory contention
DYNCTA improves average application performance by 28%

## Slide 29: Thanks! QUESTIONS?

## Slide 30: BACKUP

## Slide 31: Utilization
Core 1
Idle
CTA 1
CTA 3
CTA 5
CTA 7
Core 2
CTA 2
CTA 4
CTA 6
CTA 8
CTA 1
CTA 3
CTA 4
CTA 6
CTA 5
CTA 7
CTA 2
CTA 8
Idle
Core 1
Core 2

## Slide 32: Initial n
All cores are initialized with ⌊N/2⌋ CTAs.
Starting with 1 CTAs and ⌊N/2⌋ CTAs usually converge to the same value.
Starting with the default number of CTAs might not be as effective

## Slide 33: Comparison against optimal CTA count
Optimal number of CTAs might be different for different intervals for applications that exhibit compute- and memory- intensive behaviors at different intervals
Our algorithm outperforms optimal number of CTAs in some applications

## Slide 34: Parameters
Variable | Description | Value
Nact | Active time, where cores can fetch new warps | 
Ninact | Inactive time, where cores cannot fetch new warps | 
RACT | Active time ratio, Nact/(Nact + Ninact) | 
C_idle | The number of core cycles during which the pipeline is not stalled, but there are no threads to execute | 
C_mem | The number of core cycles during which all the warps are waiting for their data to come back | 
t_idle | Threshold that determines whether C_idle is low or high | 16
t_mem_l & t_mem_h | Thresholds that determine if C_mem is low, medium or high | 128 & 384
Sampling period | The number of cycles to make a modulation decision | 2048

## Slide 35: Round Trip Fetch Latency
Chart: Normalized Latency
| PVC | SSC | IIX | BFS | SAD | PFF | LUD | SPMV | NW | MUM | KM | WP | SCP | PVR | AES | LIB | NQU | FFT | SD2 | BP | JPEG | BLK | RAY | SD1 | LKC | PFN | HOT | NN | MM | STO | CP | avg
Round Trip Fetch Latency | 1.4369 | 0.92258 | 0.77415 | 0.89189 | 0.18499 | 1.0076 | 1 | 0.64306 | 0.99278 | 0.84358 | 0.50514 | 1 | 0.43491 | 0.45777 | 0.378 | 1 | 1.05 | 0.30735 | 0.79348 | 0.51754 | 0.27988 | 0.26361 | 0.57287 | 0.59821 | 0.16154 | 0.95455 | 0.69756 | 0.64516 | 0.96429 | 0.25 | 0.29965 | 0.67191
0.67

## Slide 36: Other Metrics
L1 data miss rate: 71% → 64%
Network latency: ↓ 33%
Active time ratio: ↑ 14%

## Slide 37: Sensitivity
Large system with 56 and 110 cores: around 20% performance improvement
MSHR size: 64 – 32 – 16: 0.3% and 0.6% performance loss
DRAM frequency: 1333 MHz: 1% performance loss
Sampling period 2048 – 4096: 0.1% performance loss
Thresholds: 50% - 150% of the default values: losses between 0.7% - 1.6%