## Slide 1
Scheduling Techniques for GPU Architectures
with Processing-In-Memory Capabilities
Ashutosh Pattnaik
Xulong Tang, Adwait Jog, Onur Kayıran, Asit Mishra,
Mahmut Kandemir, Onur Mutlu, Chita Das
PACT ‘16

## Slide 2: Era of Energy-Efficient Architectures
2010:
Tianhe-1A
4.7 PFlop/s, 4 MW
~1.175 TFlops/W
2013:
Tianhe-2
54.9 PFlop/s, 17.8 MW
~3.084 TFlops/W
2016:
Sunway TaihuLight
125.4 PFlop/s, 15.4 MW
~8.143 TFlops/W
Peak Performance increased by ~27x in past 6 years
Energy Efficiency increased by ~7x in
past 6 years
Future: 1 ExaFlops/s at 20 MW Peak power
Greatly need to improve energy efficiency
  as well as performance!

## Slide 3: Bottleneck
Continuous energy-efficiency and performance scaling is not easy.
Energy consumed by a floating-point operation is scaling down with technology scaling.
Energy consumption due to data transfer overhead is not scaling down!

## Slide 4: Bottleneck
Chart: Fraction
| BFS | BICG | BLK | CCL | CONV | CORR | FDTD | GRAM | LUH | MVT | PR | RED | SCP | SLA | STRM | APSP | CFD | CONS | FWT | GUPS | LIB | MST | PVC | SP | TRA | avg
Off-Chip Transactions | 0.65428 | 0.32259 | 0.9992 | 0.16013 | 0.18177 | 0.063281 | 0.30026 | 0.24121 | 0.57318 | 0.30196 | 0.53936 | 0.99221 | 0.99158 | 0.62535 | 0.66424 | 0.062272 | 0.19746 | 0.52828 | 0.42026 | 0.77509 | 0.42165 | 0.20769 | 0.45557 | 0.63656 | 0.78554 | 0.48404
Off-Chip Energy | 0.64745 | 0.37963 | 0.39278 | 0.32772 | 0.36943 | 0.10349 | 0.46376 | 0.14576 | 0.51037 | 0.36467 | 0.33956 | 0.56149 | 0.54445 | 0.30653 | 0.47835 | 0.01353 | 0.3295 | 0.38689 | 0.52811 | 0.69228 | 0.3461 | 0.42609 | 0.33289 | 0.68239 | 0.54708 | 0.40881
Data movement and system energy consumption caused by off-chip memory accesses.
Across these 25 GPGPU applications:
49% of all transactions are off-chip.
This is responsible for 41% of total energy consumption of the system.

## Slide 5: Bottleneck
Chart: Normalized Performance
| BFS | BICG | BLK | CCL | CONV | CORR | FDTD | GRAM | LUH | MVT | PR | RED | SCP | SLA | STRM | APSP | CFD | CONS | FWT | GUPS | LIB | MST | PVC | SP | TRA | avg
Normalized Performance | 0.96885 | 0.80612 | 0.48591 | 0.31297 | 0.80334 | 0.61145 | 0.44038 | 0.29679 | 0.44237 | 0.88066 | 0.32976 | 0.53441 | 0.26755 | 0.61298 | 0.52958 | 0.83279 | 0.20844 | 0.59477 | 0.43937 | 0.97566 | 0.63343 | 0.94067 | 0.97213 | 0.58016 | 0.58459 | 0.55447
Performance normalized to a hypothetical GPU where all the off-chip accesses hit in the last-level cache.
Main memory accesses lead to 45% performance degradation!

## Slide 6: Outline
Introduction and Motivation
Background and Challenges
Design of Kernel Offloading Mechanism
Design of Concurrent Kernel Management
Simulation Setup and Evaluation
Conclusions

## Slide 7: Revisiting Processing-In-Memory (PIM)
It’s a promising approach to minimize data movement.
The concept dates back to the late 1960s
Technological limitations of integrating fast computational units in memory was a challenge
Significant advances in adoption of 3D-stacked memory has
  enabled tight integration of memory dies and logic layer
  brought computational units into the memory stack

## Slide 8: PIM-Assisted GPU architecture
We integrate PIM units to a GPU based system and we call this as “PIM-Assisted GPU architecture”.
At least one 3D-stacked memory is integrated with PIM units and is placed adjacent to a traditional GPU design.

## Slide 9: PIM-Assisted GPU architecture
Traditional GPU architecture*
Memory
GPU
Memory Link
* Only a single DRAM partition is shown for illustration purposes

## Slide 10: PIM-Assisted GPU architecture
GPU architecture with 3D-stacked memory on a silicon interposer
GPU
Memory Link
on Interposer
Silicon Interposer
Memory Dice

## Slide 11: PIM-Assisted GPU architecture
Now we add a logic layer to the 3D-stacked memory and we call this logic layer as GPU-PIM.
The traditional GPU logic is now called GPU-PIC.
3D Stacked
Memory and Logic
Memory Dice
GPU-PIM
GPU-PIC
Memory Link
on Interposer
Silicon Interposer

## Slide 12: PIM-Assisted GPU architecture
Application can now be run on both GPU-PIC and GPU-PIM
Challenge: Where to execute the application on?
3D Stacked
Memory and Logic
Memory Dice
GPU-PIM
GPU-PIC
Memory Link
on Interposer
Silicon Interposer

## Slide 13: Application Offloading
We evaluate application execution on either GPU-PIC or GPU-PIM
Chart: Normalized IPC
| BFS | BICG | BLK | CCL | CONV | CORR | FDTD | GRAM | LUH | MVT | PR | RED | SCP | SLA | STRM | APSP | CFD | CONS | FWT | GUPS | LIB | MST | PVC | SP | TRA | GMean
GPU-PIC | 1.0757 | 1 | 1.0148 | 0.9792 | 0.8322 | 1.0001 | 0.99058 | 1 | 0.98637 | 1 | 0.96089 | 0.97244 | 1.0251 | 0.98083 | 1.0539 | 0.99097 | 0.95972 | 0.9821 | 1.0113 | 1.0918 | 1.0116 | 1.0366 | 1.0083 | 1.0143 | 1.0134 | 0.99856
GPU-PIM | 0.85861 | 0.94095 | 1.1126 | 0.6014 | 0.6539 | 0.8302 | 0.86143 | 2.635 | 0.93606 | 0.93457 | 0.67188 | 1.287 | 1.0299 | 0.55524 | 1.162 | 1.2711 | 0.61688 | 0.63086 | 1.3866 | 2.4607 | 1.3501 | 1.2992 | 0.68662 | 1.2278 | 1.3386 | 1.0045
Best Application Offloading | 1.1627
Chart: Normalized Energy Efficiency (Inst./Joule)
| BFS | BICG | BLK | CCL | CONV | CORR | FDTD | GRAM | LUH | MVT | PR | RED | SCP | SLA | STRM | APSP | CFD | CONS | FWT | GUPS | LIB | MST | PVC | SP | TRA | GMean
GPU-PIC | 1.0329 | 1.2374 | 1.0045 | 1.0122 | 0.93868 | 1.1479 | 0.99917 | 1.2057 | 1.0105 | 1.2358 | 1.0079 | 1.0535 | 1.0657 | 1.0114 | 1.0463 | 1.1784 | 0.99741 | 0.99831 | 1.0033 | 1.0943 | 1.0833 | 1.0161 | 1.0066 | 1.0106 | 1.0029 | 1.0531
GPU-PIM | 1.0489 | 2.5093 | 1.1069 | 1.0444 | 1.016 | 2.6406 | 1.0755 | 5.9462 | 1.1668 | 2.5099 | 1.0612 | 1.2497 | 1.1602 | 1.039 | 1.1647 | 2.5999 | 0.90769 | 1.0072 | 1.2518 | 2.1065 | 1.3017 | 1.3421 | 1.0377 | 1.3698 | 1.4973 | 1.4219
Best Application Offloading | 1.2781
Optimal application offloading scheme provides 16% and 28% improvements in performance and energy efficiency, respectively.
2.64
2.46
2.51
2.64
5.95
2.50
2.60
2.1

## Slide 14: Limitations of Application Offloading
Limitation 1: Lack of Fine-Grained Offloading
FDTD

## Slide 15: Limitations of Application Offloading
Limitation 1: Lack of Fine-Grained Offloading
Running K1 on GPU-PIM, and K2 and K3 on GPU-PIC provides the optimal kernel placement for improved performance.

## Slide 16: Limitations of Application Offloading
Limitation 1: Lack of Fine-Grained Offloading
Limitation 2: Lack of Concurrent Utilization of GPU-PIM and GPU-PIC
From the application we find that kernel K1 and K2 are independent from each other.
GPU-PIC is idle!

## Slide 17: Limitations of Application Offloading
Limitation 1: Lack of Fine-Grained Offloading
Limitation 2: Lack of Concurrent Utilization of GPU-PIM and GPU-PIC
Chart: Normalized Execution Time
| GPU-PIC | GPU-PIM | GPU-PIC | GPU-PIM | GPU-PIC | GPU-PIM | GPU-PIC | GPU-PIM | Concurrent Kernel Management | Concurrent Kernel Management | Kernel Offloading | Application Offloading | FDTD
 | 0 | 0 | 0 | 0 | 0 | 0
K1 | 0.33184 | 0.23943 | 0.34074 | 0.51792 | 0.23943 | 0.23943 | 0.34074 | 0.23943
K2 | 0.32742 | 0.17718 | 0.33184 | 0.33184 | 0.51792
K3 | 0.32742 | 0.32742 | 0.32742 | 0.38594
A
C
I
II
III
IV
V
B
K1 -> GPU-PIC
K2 -> GPU-PIM
K1 -> GPU-PIM
K2 -> GPU-PIC
Scheduling kernels based on their affinity is very important to achieve higher performance.

## Slide 18: Our Goal
To develop runtime mechanisms for
  automatically identifying architecture affinity of each kernel in an application
  scheduling kernels on GPU-PIC and GPU-PIM to maximize for performance and utilization

## Slide 19: Outline
Introduction and Motivation
Background and Challenges
Design of Kernel Offloading Mechanism
Design of Concurrent Kernel Management
Simulation Setup and Evaluation
Conclusions

## Slide 20: Design of Kernel Offloading Mechanism
Goal: Offload kernels to either GPU-PIC or GPU-PIM to maximize performance
Challenge: Need to know the architecture affinity of the kernels
We build an architecture affinity prediction model

## Slide 21: Design of Kernel Offloading Mechanism
Metrics used to predict compute engine affinity and GPU-PIC and GPU-PIM execution time.
Category | Predictive Metric | Static/Dynamic
I: Memory Intensity of Kernel | Memory to Compute Ratio | Static
 | Number of Compute Inst. | Static
 | Number of Memory Inst. | Static
II: Available Parallelism in the Kernel | Number of CTAs | Dynamic
 | Total Number of Threads | Dynamic
 | Number of Thread Inst. | Dynamic
III: Shared Memory Intensity of Kernel | Total Number of Shared Memory Inst. | Static

## Slide 22: Design of Kernel Offloading Mechanism
Logistic Regression Model for Affinity Prediction
where:
= model output ( < 0.5 => GPU-PIC, ≥ 0.5 => GPU-PIM)
=
= Coefficients of the Regression Model
= Predictive Metrics

## Slide 23: Design of Kernel Offloading Mechanism
Training Set: we randomly sample 60% (15) of the 25 GPGPU applications considered in the paper.
These 15 applications consists of 82 unique kernels that are used for training the affinity prediction model.
Test Set: the remaining 40% (10) of the applications are used as the test set for the model
Accuracy of the model on the test set: 83%

## Slide 24: Outline
Introduction and Motivation
Background and Challenges
Design of Kernel Offloading Mechanism
Design of Concurrent Kernel Management
Simulation Setup and Evaluation
Conclusions

## Slide 25: Design of Concurrent Kernel Management
Goal: Efficiently manage the scheduling of concurrent kernels to improve performance and utilization of the PIM-Assisted GPU architecture
For efficiently managing kernel execution on both GPU-PIM and GPU-PIC, we need
  Kernel-level Dependence Information
  Architecture Affinity Information
  Execution Time Information

## Slide 26: Design of Concurrent Kernel Management
For efficiently managing kernel execution on both GPU-PIM and GPU-PIC, we need
  Kernel-level Dependence Information
    Obtained through exhaustive analysis to find RAW dependence for all considered applications and input pairs
  Architecture Affinity Information
  Execution Time Information

## Slide 27: Design of Concurrent Kernel Management
For efficiently managing kernel execution on both GPU-PIM and GPU-PIC, we need
  Kernel-level Dependence Information
    Obtained through exhaustive analysis to find RAW dependence for all considered applications and input pairs
  Architecture Affinity Information
    Utilizes the affinity prediction model built for kernel offloading mechanism
  Execution Time Information

## Slide 28: Design of Concurrent Kernel Management
For efficiently managing kernel execution on both GPU-PIM and GPU-PIC, we need
  Kernel-level Dependence Information
    Obtained through exhaustive analysis to find RAW dependence for all considered applications and input pairs
  Architecture Affinity Information
    Utilizes the affinity prediction model built for kernel offloading mechanism
  Execution Time Information
    We build linear regression models for execution time prediction on GPU-PIC and GPU-PIM
    We use the same “Predictive metrics” and training set used for affinity prediction model

## Slide 29
Linear Regression Model for Execution Time Prediction Model
where:
= model output (predicted execution time)
= Coefficients of the Regression Model
= Predictive Metrics
Design of Concurrent Kernel Management

## Slide 30
Lets run through an example
Design of Concurrent Kernel Management
GPU-PIC Queue
GPU-PIM Queue
K4
idle
GPU-PIC is currently
executing kernel K4
GPU-PIM is
currently idle
K5
K6
K7
GPU-PIM has no
more kernels in its
work queue to
schedule

## Slide 31
We can potentially pick any kernel (assuming no data dependence among themselves and K4) from GPU-PIC Queue and schedule them onto GPU-PIM
But which one to pick?
Design of Concurrent Kernel Management
GPU-PIC Queue
GPU-PIM Queue
K4
idle
GPU-PIC is currently
executing kernel K4
GPU-PIM is
currently idle
K5
K6
K7

## Slide 32
We steal the first kernel that satisfies a given condition and schedule it on to GPU-PIM Queue.
Pseudocode:
time(kernel, compute_engine) returns the estimated execution time of “kernel” when executed on ”compute_engine”
Design of Concurrent Kernel Management
for X in GPU-PIC’s Queue
Estimated execution time of
currently executing
kernel K4 on GPU-PIC

## Slide 33: Outline
Introduction and Motivation
Background and Challenges
Design of Kernel Offloading Mechanism
Design of Concurrent Kernel Management
Simulation Setup and Evaluation
Conclusions

## Slide 34: Simulation Setup
Evaluated on GPGPU-Sim, a cycle accurate GPU simulator
Baseline configuration
  40 SMs, 32-SIMT lanes, 32-threads/warp
  768 kB L2 cache
GPU-PIM configuration
  8 SMs, 32-SIMT lanes, 32-threads/warp
  No L2 cache
GPU-PIC configuration
  32 SMs, 32-SIMT lanes, 32-threads/warp
  768 kB L2 cache
25 GPGPU Applications classified into 2 exclusive sets
  Training Set: The kernels are used as input to build the regression models
  Test Set: The regression models are only tested on these kernels

## Slide 35: Performance (Normalized to Baseline)
Performance improvement for Test Set applications
Training Set
Test Set
Chart: 
| BFS | BICG | BLK | CCL | CONV | CORR | FDTD | GRAM | LUH | MVT | PR | RED | SCP | SLA | STRM | GMean | APSP | CFD | CONS | FWT | GUPS | LIB | MST | PVC | SP | TRA | GMean
Kernel Offloading (Dynamic) | 1.0772 | 0.94095 | 1.1126 | 1.0311 | 0.6539 | 0.8332 | 0.99058 | 2.635 | 1.1282 | 0.93457 | 1.0722 | 0.97244 | 1.0251 | 1.0836 | 1.162 | 1.0585 | 1.2297 | 1.0627 | 0.9821 | 1.506 | 2.4607 | 1.3501 | 1.0366 | 1.063 | 1.0168 | 1.2918 | 1.2497
Kernel Offloading (Oracle) | 1.0772 | 1.0349 | 1.1126 | 1.0476 | 0.8322 | 1.0184 | 1.1033 | 2.635 | 1.1605 | 1.0352 | 1.2224 | 1.287 | 1.0299 | 1.1127 | 1.162 | 1.1492 | 1.4493 | 1.0627 | 0.9821 | 1.506 | 2.4607 | 1.3845 | 1.2992 | 1.1342 | 1.2278 | 1.3386 | 1.3409
Concurrent Kernel Management (Dynamic) | 1.8299 | 1.0388 | 1.1126 | 1.23 | 1.4817 | 0.8332 | 1.3362 | 2.635 | 1.2338 | 1.0356 | 1.34 | 2.2545 | 1.0251 | 1.51 | 1.162 | 1.3376 | 1.61 | 1.0828 | 0.9821 | 1.8675 | 2.4607 | 1.6969 | 1.2566 | 0.97359 | 1.0168 | 2.0169 | 1.4207
Concurrent Kernel Management (Oracle) | 1.836 | 1.0908 | 1.1126 | 1.25 | 1.4817 | 1.0001 | 1.5037 | 2.635 | 1.2588 | 1.0912 | 1.63 | 2.2545 | 1.0251 | 1.51 | 1.162 | 1.3956 | 1.65 | 1.0829 | 0.9821 | 1.8675 | 2.4607 | 2.0624 | 1.3728 | 1.1304 | 1.2278 | 2.2347 | 1.5311
  Kernel Offloading = 25%
  Concurrent Kernel Management = 42%

## Slide 36: Energy-Efficiency (Normalized to Baseline)
Energy-Efficiency improvement for Test Set applications
  Kernel Offloading = 28%
  Concurrent Kernel Management = 27%
Training Set
Test Set
Chart: 
| BFS | BICG | BLK | CCL | CONV | CORR | FDTD | GRAM | LUH | MVT | PR | RED | SCP | SLA | STRM | GMean | APSP | CFD | CONS | FWT | GUPS | LIB | MST | PVC | SP | TRA | GMean
Kernel Offloading (Dynamic) | 1.0338 | 2.5093 | 1.1069 | 1.0321 | 1.016 | 2.6364 | 0.99917 | 5.9462 | 1.1099 | 2.5099 | 1.0563 | 1.0535 | 1.0657 | 1.051 | 1.1647 | 1.4191 | 2.2759 | 1.0436 | 0.99831 | 1.2502 | 2.1065 | 1.3017 | 1.0161 | 1.0301 | 1.013 | 1.3986 | 1.2827
Kernel Offloading (Oracle) | 1.0338 | 1.3061 | 1.1069 | 1.0493 | 0.93868 | 1.1691 | 1.0538 | 5.9462 | 1.1524 | 1.3043 | 1.1734 | 1.2497 | 1.1602 | 1.0917 | 1.1647 | 1.2676 | 2.7365 | 1.0436 | 0.99831 | 1.2502 | 2.1065 | 1.2809 | 1.3421 | 1.0843 | 1.3698 | 1.4973 | 1.3989
Concurrent Kernel Management (Dynamic) | 1.0413 | 1.7868 | 1.1069 | 0.95 | 0.97029 | 2.6364 | 1.0278 | 5.9462 | 1.1201 | 1.7862 | 1.05 | 1.1575 | 1.0657 | 1.0505 | 1.1647 | 1.3566 | 2.14 | 1.0399 | 0.99831 | 1.2502 | 2.1065 | 1.1895 | 1.1677 | 1.0751 | 1.013 | 1.2009 | 1.2666
Concurrent Kernel Management (Oracle) | 1.0417 | 1.3061 | 1.1069 | 0.95 | 0.97029 | 2.6364 | 1.0538 | 5.9462 | 1.1497 | 1.3043 | 1.0563 | 1.1575 | 1.0657 | 1.051 | 1.1647 | 1.306 | 2.14 | 1.0399 | 0.99831 | 1.2502 | 2.1065 | 1.2809 | 1.2819 | 1.0733 | 1.3698 | 1.2359 | 1.3311
More results and detailed description
of our runtime mechanisms are in the paper.

## Slide 37: Conclusions
Processing-In-Memory is a key direction in achieving high performance with lower power budget.
Simply offloading applications completely onto PIM units is not optimal.
For effective utilization of PIM-Assisted GPU architecture, we need to
  Identify code segments for offloading onto GPU-PIM
  Efficiently distribute work between GPU-PIC and GPU-PIM
Our kernel-level scheduling mechanisms can be an effective runtime solution for exploiting processing-in-memory in modern GPU-based architectures.

## Slide 38
Scheduling Techniques for GPU Architectures
with Processing-In-Memory Capabilities
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayıran,
Asit Mishra, Mahmut Kandemir, Onur Mutlu, Chita Das.
PACT ‘16

## Slide 39: Backup Slides

## Slide 40: Era of Throughput Architectures
GPUs are scaling: Number of CUDA Cores, DRAM bandwidth
2016:
GTX 1080
(Pascal)
2560 cores
(320 GB/sec)
2010:
GTX 480
(Fermi)
448 cores
(178 GB/sec)
2012:
GTX 680
(Kepler)
1536 cores
(192 GB/sec)
Number of CUDA Cores are scaling rapidly
Memory bandwidth is scaling at a much slower pace
Memory bandwidth being a bottleneck!
Notes: As we know GPU are scaling both in terms of number of CUDA cores as well peak DRAM
Bandwidth. For example, the latest NVIDIA GPU GTX 1080 has more than 2000 cores.
Given such powerful GPUs, the question is -- Are we “still” using them efficiently?
Memory Bandwidth not increasing fast enough.

## Slide 41: Input sensitivity of Regression models
Chart: Normalized IPC
| Input-1 | Input-2 | Input-3 | Input-1 | Input-2 | Input-3 | Input-1 | Input-2 | Input-1 | Input-2 | Input-3 | Input-1 | Input-2 | Input-3 | Input-1 | Input-2 | Input-3 | Input-1 | Input-2 | Input-3 | Input-1 | Input-2 | Input-3 | geomean | BFS | PR | RED | STRM | CFD | MST | PVC | SP | a
GPU-PIM | 0.85861 | 0.88998 | 0.8655 | 0.67188 | 0.42359 | 0.65563 | 1.287 | 1.0923 | 1.2365 | 1.1643 | 1.162 | 0.61688 | 0.63101 | 0.61797 | 0.73617 | 1.2992 | 2.1821 | 0.5192 | 0.8113 | 0.68662 | 1.1904 | 1.2278 | 1.2465 | 0.87071
GPU-PIC | 1.0757 | 1.0372 | 0.99678 | 0.96089 | 0.93597 | 0.99401 | 0.97244 | 1.0021 | 1.0218 | 1.0054 | 1.0539 | 0.95972 | 0.96195 | 0.96424 | 1.0225 | 1.0366 | 0.99853 | 0.93768 | 0.98586 | 1.0083 | 1.0175 | 1.0143 | 1.0158 | 0.99956
Kernel Offloading (Dynamic) | 1.0772 | 1.0372 | 1.0171 | 1.0722 | 1.092 | 1.2002 | 0.97244 | 1.0923 | 1.2365 | 1.1643 | 1.162 | 1.0627 | 1.0728 | 1.0491 | 1.1146 | 1.1943 | 1.202 | 0.96113 | 0.99159 | 1.063 | 1.0191 | 1.0168 | 1.0198 | 1.0843
Kernel Offloading (Oracle) | 1.0772 | 1.2017 | 1.0171 | 1.2224 | 1.098 | 1.2159 | 1.287 | 1.0923 | 1.2365 | 1.1643 | 1.162 | 1.0627 | 1.0732 | 1.0491 | 1.1146 | 1.2992 | 2.1821 | 0.96384 | 1.1006 | 1.1342 | 1.1904 | 1.2278 | 1.2465 | 1.1754

## Slide 42: Accuracy of execution time-bin prediction model
Chart: Classification Error of Test kernels
GPU-PIM | 0.4 | 0 | 0 | 0 | 0 | -0.2 | 0 | 0 | -0.2 | -0.2 | -0.4 | -0.2 | 0.2 | 0 | -0.2 | 0 | -0.4 | -0.4 | -0.2 | 0.2 | 0.2 | 0 | 0 | -0.4 | 0.4 | 0.4 | 0.2 | 0 | 0 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.2 | 0.4 | 0 | 0.4 | 0 | 0 | 0.2
GPU-PIC | 0.4 | 0.2 | 0.2 | 0.2 | 0.2 | -0.2 | 0.2 | 0.2 | -0.2 | -0.2 | -0.2 | 0 | 0.2 | 0 | 0 | 0 | -0.4 | -0.4 | -0.2 | 0 | 0.4 | -0.2 | 0 | -0.2 | 0.4 | 0.4 | 0.2 | 0 | 0.2 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.4 | 0.2 | 0.4 | 0.2 | 0.4 | 0 | 0 | 0.2
Average Accuracy
GPU-PIM = 80%
GPU-PIC = 77%
Classification error of test kernel execution times.
Notes: PIM Classification error

## Slide 43: Modified CUDA runtime to support Kernel Offloading Mechanism
CUDA Runtime
Affinity Prediction Model
GPU-PIM
GPU-PIC
Execution Time Prediction Model
Kernel Distribution
Unit
ii
iii
iv

## Slide 44: Effects of Kernel Offloading Mechanism
Chart: Percentage of Execution Time
| BFS | BICG | BLK | CCL | CONV | CORR | FDTD | GRAM | LUH | MVT | PR | RED | SCP | SLA | STRM | APSP | CFD | CONS | FWT | GUPS | LIB | MST | PVC | SP | TRA | avg (test)
GPU-PIC | 51254405.8362 | 0 | 0 | 2361104.6683 | 0 | 371108.9491 | 3004183.863 | 0 | 4371628.9279 | 0 | 2996393.4243 | 2719361.9952 | 76226.9981 | 1082190.3801 | 0 | 472516.035 | 7009999.6755 | 2290601.7895 | 0 | 0 | 16205267.7167 | 1813400.5651 | 98924505.7888 | 347052.9563 | 8137497.8987
GPU-PIM | 33370.0008 | 16381198.9585 | 518401.9658 | 159227.9771 | 5409383.0197 | 48709891.3352 | 0 | 9065685.8529 | 1724703.4751 | 16415211.3507 | 436474.999 | 0 | 0 | 300584.9854 | 68227290.6276 | 5507711.868 | 718067.0193 | 0 | 1 | 2845498.233 | 3999498.2074 | 0 | 196842.9902 | 169849.0297 | 1179951.5303 | 7279953.777
Training
Test
Percentage of execution time GPU-PIM and GPU-PIC execute kernels with our kernel offloading scheme.

## Slide 45: Effects of Concurrent Kernel Management
Chart: Percentage of Execution Time
| BFS | BICG | BLK | CCL | CONV | CORR | FDTD | GRAM | LUH | MVT | PR | RED | SCP | SLA | STRM | APSP | CFD | CONS | FWT | GUPS | LIB | MST | PVC | SP | TRA | avg (test)
 | 0.9079 | 0.053998 | 0 | 0.42575 | 0.99771 | 0 | 0.36286 | 0 | 0.085142 | 0.054039 | 0.73676 | 0.99507 | 0 | 0.76584 | 0 | 0.25962 | 0.026809 | 0 | 0 | 0 | 0.48969 | 0.12044 | 0.010949 | 0 | 0.75248 | 0.2818
Training
Testing
Percentage of execution time when kernels are concurrently running on GPU-PIM and GPU-PIC with our concurrent kernel management scheme