## Slide 1: BCoal: Bucketing-based Memory Coalescing for Efficient and Secure GPUs
Gurunath Kadam, William & Mary
Danfeng Zhang, Penn State University
Adwait Jog, William & Mary
Notes: Good Morning everyone! My name is Gurunath, and I will be presenting our paper titled “BCoal … “.
This work was done at William and Mary and with our collaborator at Penn State.

## Slide 2: GPUs are Everywhere!
Games
Image
Processing
Financial
Computing
Genomics
Astronomy
Medical
Imaging
Audio
Processing
Machine
Learning
Physics
Simulation
High Data-Level
Parallelism
Encryption
Fast and
Energy Efficient
Secure GPU against attacks!!

## Slide 3
Previously at HPCA…
[Jiang+, HPCA’16]
[Kadam+, HPCA’18]
Correlation Timing Attack
Recovers AES Key
Exploits Deterministic GPU Coalescing Logic
RCoal
Randomizes GPU Coalescing Logic
Notes: Previously one such attack, called correlation timing attack, was demonstrated to recover the AES encryption Key.
This attack exploited the deterministic GPU coalescing, used for memory access optimization.
In response, we presented a defense scheme, RCoal, which randomized the GPU coalescing logic to mitigate the attack.

## Slide 4
Previously on HPCA…
Now … HPCA’20
[Jiang+, HPCA’16]
[Kadam+, HPCA’18]
Correlation Timing Attack
Recovers AES Key
Exploits Deterministic GPU Coalescing Logic
RCoal
Randomizes GPU Coalescing Logic
Not Secure with MSHRs and Caches
~9.4x Performance Overhead
BCoal
Bucket-based Coalescing Logic
Secure with MSHRs and Caches
Better Security and Performance Tradeoff
RCoal
Randomizes GPU Coalescing Logic
Notes: However, RCoal is not secure with MSHRs and caches, and result in high performance degradation.
Now, we present a performance efficient defense scheme, BCoal.
BCoal employs a Bucket-based coalescing logic to thwart the timing attack. BCoal is secure with MSHRs and caches.
BCoal offers a good security and performance tradeoff compared to the state-of-the-art.

## Slide 5: Outline
Introduction
Background
Prior Defense Scheme: RCoal
BCoal Defense Scheme
Evaluation
Conclusion
Notes: Outline of my talk. I will present some background on the GPU memory optimization techniques and correlation timing attack.
Then, I will discuss the previous defense scheme, RCoal and its shortcomings.
Following that I will present new performance efficient denfese scheme, BCoal and its evaluation.
…leading to the conclusion.

## Slide 6: Outline
Introduction
Background
  Memory Access Optimization in GPU
  Correlation Timing Attack on GPU
Prior Defense Scheme: RCoal
BCoal Defense Schemes
Evaluation
Conclusion
Notes: Bigger font – merge if possible

## Slide 7: Memory Access Optimizations in GPUs
# of Accesses α Execution Time
Different Optimizations to exploit Locality
  Coalescing Unit
  Caching
  Miss-Status Handling Registers (MSHRs)
Bandwidth is Precious!
Notes: Bandwidth is an important resource on GPUs, as a result, different optimization techniques are used to exploit the access locality.
The first optimization is access coalescing, which merges accesses going to the same memory block to generate as few accesses as possible.
Next, GPUs used caching at two levels, L1 and L2, to exploit temporal and spatial locality.
The cache missed accesses going to the next memory level are further optimized in MSHRs, which merges the accesses going to the same memory block.
If fewer accesses are generated then the execution time is short, otherwise with large number of accesses the execution time increases.
The number of accesses govern the execution time.

## Slide 8: Timing Attack Model [Jiang+, HPCA’16]
  Recovers AES Key on GPUs
Plaintext
Ciphertext
Ciphertext | Time
Ciphertext1 | T1
Ciphertext2 | T2
… | …
Notes: Next, we look at the correlation timing attack. We begin with the attack model.
The goal is to recover the AES encryption key.
The model assumes that the attacker can remotely access the encryption server, which stores the encryption key.
The attacker can send plaintexts to the server for encryption and time the execution time for each encryption.
The attacker then receives the ciphertext. The attacker can repeat the process to collect multiple cipertexts and related execution time.

## Slide 9: Timing Attacks on GPUs [Jiang+, HPCA’16]
Last Round Execution
Round Key
XOR
Input to the Round
T4 Table Lookup
Encryption Output to Attacker
  Recovers AES Key on GPUs
Notes: Now, we see the attack in detail: The attack focuses on the last round of the AES encryption.
The last round can be summarized in following equation.

## Slide 10: Timing Attacks on GPUs [Jiang+, HPCA’16]
Last Round Execution
Invert Table Lookup
Execution Time [Real Key Byte]
Guess Key Byte
Mem Address
GPU Memory Configuration
# of coalesced accesses [Guess Key Byte]
Correlation?
Correlation is HIGHEST for REAL key
  # of Accesses α Execution Time
+
1
2
3
4
Notes: To begin the attack, the attacker executes the encryption on the server and observes the execution time.
This execution time corresponds to the real key byte value, which attack is unaware of.
In second step, the attacker performs an invert table lookup. She then plugs in a guess key byte value to deduce the memory addresses generated.
The attack assumes that the attacker is aware of the memory layout.
With the help of the memory layout and the memory addresses, attacker can find out the number of coalesced accesses corresponding to the guess key byte.
For the final step the attacker exploits the relationship between the # of accesses and the execution time.
To do so, she correlates the # of coalesced accesses with the observed execution time. Among the guess key byte values, the correlation is higher for the correct guess.

## Slide 11: Timing Attacks on GPUs [Jiang+, HPCA’16]
Incorrect Guesses
Correct Guesses

## Slide 12: Outline
Introduction
Background
Prior Defense Scheme: RCoal
BCoal Defense Scheme
Evaluation
Conclusion
Notes: Bigger font – merge if possible

## Slide 13: RCoal: Randomized Coalescing Scheme
Attack exploits Deterministic Coalescing
RCoal Randomizes Coalescing Logic
  Randomly generates Duplicate Accesses

## Slide 14: RCoal Shortcomings
High Performance Degradation
  Inefficient Coalescing
  MSHRs and Caches Disabled
RCoal suffers ~27x increase in DRAM Accesses
RCoal suffers ~ 9.4x increase in Execution Time

## Slide 15: RCoal Shortcomings
High Performance Degradation
  Inefficient Coalescing
  MSHRs and Caches Disabled
Insecure with MSHRs and Caches
Without MSHRs and Caches
With MSHRs and Caches
SECURE
INSECURE
Need for Performance Efficient Defense Scheme!
Notes: Check order

## Slide 16: Outline
Introduction
Background
Prior Defense Scheme: RCoal
BCoal Defense Scheme
Evaluation
Conclusion
Notes: Bigger font – merge if possible

## Slide 17: Bucketing for Coalesced Accesses
12
13
14
15
E1
E2
E3
E4
Performance Efficient Secure Coalescing
  # of Coalesced Accesses α Execution Time
    Reduce Variance
16
E5
# of Coalesced Accesses
Execution Time
Correlation
Notes: We start by examining what bucketing means.
We aim to devise a performance efficient secure coalescing, which eliminates the relationship between the # of coalesced accesses and observed execution time.
It can be achieved by reducing the variance in the execution time.
Lets look at an example of 5 different encryptions generating 5 distinct number of coalesced accesses.
The corresponding execution time will be different as well.
Since, the execution time is governed by the # of coalesced accesses, the attacker can correlate them to recover the key.

## Slide 18: Bucketing for Coalesced Accesses
Performance Efficient Secure Coalescing
  # of Coalesced Accesses α Execution Time
    Reduce Variance
# of Coalesced Accesses
Execution Time
No Correlation
12
13
14
15
E1
E2
E3
E4
16
E5
16
16
16
16
E5
E5
E5
E5
Notes: To eliminate the correlation, we want to reduce the variance in the execution time.
This can be achieved by always generating same number of coalesced accesses.
The result is no correlation.

## Slide 19: Bucketing for Coalesced Accesses
Performance Efficient Secure Coalescing
  # of Coalesced Accesses α Execution Time
    Reduce Variance
  Bucketing
12
13
14
15
16
# of Coalesced Accesses
Padded Accesses
Fewer Buckets: Best Security, Performance Overhead
16
16
16
16
B16

## Slide 20: Bucketing for Coalesced Accesses
Performance Efficient Secure Coalescing
  # of Coalesced Accesses α Execution Time
    Reduce Variance
  Bucketing
Fewer Buckets: Best Security, Performance Overhead

## Slide 21: Bucketing for Coalesced Accesses
Performance Efficient Secure Coalescing
  # of Coalesced Accesses α Execution Time
    Reduce Variance
  Bucketing
12
14
16
# of Coalesced Accesses
Fewer Buckets: Best Security, Performance Overhead
Padded Accesses
More Buckets: Less Security, Low Performance Overhead
B12
14
16
13
15
B14
B16

## Slide 22: Bucketing for Coalesced Accesses
Performance Efficient Secure Coalescing
  # of Coalesced Accesses α Execution Time
    Reduce Variance
  Bucketing
    Fewer Buckets: Best Security, Performance Overhead
    More Buckets: Less Security, Low Performance Overhead
Bucketing offers Security/Performance Tradeoff
How to select Bucketing Features?

## Slide 23: Selecting Bucketing Features
Bucket Size 1
Desired Security / Performance Tradeoff
BCoal(16)
Bucket size 16
Bucket Size 16
BCoal(1, 16)
Single Bucket
Best Security
Performance
Two Buckets
Good Security
Performance

## Slide 24: Padded Access Generation (I)
MSHRs and Caches must not degrade the security
Learning from RCoal:
  Randomly Generates Duplicate accesses
  Disables MSHRs and Caches
Padded Accesses must be
  Unique: No optimization
  Random: Effect on Execution Time is unpredictable
Observation I: The Padded Accesses should be Unique and Random

## Slide 25: Evaluation of Unique and Random Padded Accesses on Security
Bucketing with 1 Bucket of Size 16
Multi-warp
Why Security degrades due to MSHRs and Caches?
Without MSHRs and Caches
With MSHRs and Caches
SECURE
INSECURE

## Slide 26
Padded vs. Real Accesses
  Different Merging and Caching Patterns
  Different Address Ranges
    Padded accesses: Entire address space
    Real accesses: Table T4 alone
  Affect Execution Time at Different Rates
  Effect of Padded Accesses can be filtered out
Security degradation with MSHRs and Caches
Observation II: The Padded and Real Accesses should be Homogeneous in terms of caching and merging patterns
Notes: Think of the transition from the previous slide

## Slide 27: Putting Everything Together …
Goals of Defense Scheme
  # of Coalesced Accesses α Execution Time
    Reduce variance
      Bucketing
  Secure with MSHRs and Caches
    Padded accesses should be
      Unique and Random
      Same address space as Real accesses
BCoal: Bucket-based Coalescing
  BCoal(16): Single bucket of size 16
  BCoal(1, 16): Two buckets of sizes 1 and 16
BCoal: A Performance-Efficient Defense Scheme
Notes: Rework this

## Slide 28: Outline
Introduction
Background
Prior Defense Scheme: RCoal
BCoal Defense Scheme
Evaluation
Conclusion
Notes: Bigger font – merge if possible

## Slide 29: BCoal Security & Performance Evaluation
Experimental Setup
  GPGPUSIM simulator
  Plaintext sizes
    32 Lines (Single Warp)
    64 Lines (Multi Warp)
    1024 Lines for Performance
  Security evaluation
    Same number of plaintext samples as that of the attack

## Slide 30: BCoal Security Evaluation: Empirical
Plaintext with 32 lines (Single Warp)
Plaintext with 64 lines (Multi Warp)
BCoal(16) + MSHRs + Caches
BCoal(1, 16) + MSHRs + Caches
BCoal(1, 16) + MSHRs + Caches
BCoal(16) + MSHRs + Caches

## Slide 31: BCoal Performance Evaluation
BCoal generates less DRAM Traffic
  Optimal number of coalesced accesses
  Secure with MSHRs and Caches
BCoal is Performance Efficient

## Slide 32: Further Details in Paper
Theoretical security analysis
Hardware Overhead
Performance evaluation of BCoal for various GPGPU applications
  Bucket sizes vs Number of buckets
Generalized BCoal configuration
  ~1.2% Average Performance Loss

## Slide 33: Outline
Introduction
Background
Prior Defense Scheme: RCoal
BCoal Defense Scheme
Evaluation
Conclusion
Notes: Bigger font – merge if possible

## Slide 34: Conclusion
BCoal: Bucketing Based Coalescing
  Efficient and Secure Coalescing
  Secure with MSHRs and Caches
  Better Security/Performance Tradeoff
Generalized BCoal Configuration
  Incurs minimal Performance Degradation
Questions?!
Thank You!!
Notes: In conclusion, BCoal employs a Bucketing Based Coalescing for Efficient and Secure Coalescing.
It is secure with MSHRs and Caches…