## Slide 1: Fault Site Pruning for Practical Reliability Analysis of GPGPU Applications
Bin Nie, Lishan Yang, Adwait Jog, and Evgenia Smirni
College of William & Mary
Notes: HPC DL VR.

## Slide 2: Soft Errors
Soft errors: most commonly observed errors
  Single bit flips
Masked output
  Correct answer.
Silent Data Corruption (SDC) output
  Wrong answer.
Other output
  Crash, hang, …
Notes: Soft errors 过度 most common observed error
字还是黑的
Intro是怎么写的

## Slide 3: Reliability Research: Fault Injection
Fault injection method
  Injecting single-bit errors into different locations (fault sites) in applications
Ground truth: huge unreachable exhaustive fault sites!
Closest to ground truth (Baseline):
  Random sampling based on statistics
GEMM:
fault sites!
Confidence Interval: 99.8%, Error Margin: 1.26%
 60K fault sites
Notes: GPU: parallel Typically. GEMM: matrix mul. GEMM: 16Kthd x #insn x #bit

## Slide 4
GPU Application
Kernel
…
GPU Architecture
Kernel 2
Kernel 1
…
CTA
…
Kernel
CTA 2
…
CTA 1
…
…
CTA
Warp
…
Warp 2
…
Warp 1
…
Notes: 4 & 5 连在一起

## Slide 5: GPU Architecture → Progressive Fault Sites Pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
Thread-wise pruning
....
....
....
....
GPU Application
Kernel
…
Kernel 2
Kernel 1
…
CTA
Warp
…
Warp 2
…
Warp 1
…
…
CTA
…
Kernel
CTA 2
…
CTA 1
…
Notes: 2 million exps

## Slide 6: Progressive Fault Sites Pruning
CTA-level
Thread-wise pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
....
....
....
....
2DCONV K1
proxy
A few CTAs are enough; the rest are pruned
Notes: 颜色 备选方案。 Pdf & ppt; U pan
圈出来，不同线框
Group 1,2,3 加文字
Icnt -> insn cnt
Check CTA, highlight

## Slide 7: Progressive Fault Sites Pruning
CTA-level → Thread-level
Thread-wise pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
....
....
....
....
2DCONV K1, CTA(0-1-0)
proxy
A few threads are enough; the rest are pruned
Notes: 加线太乱。
用不同颜色,

## Slide 8: Progressive Fault Sites Pruning
Thread-wise pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
....
....
....
....
PathFinder K1 |  |  |  | 
Thread “a” () |  |  | Thread “b” () | 
1 | shl.u32 $r3, s[0x0010], 0x00000001 |  | 1 | shl.u32 $r3, s[0x0010], 0x00000001
2 | cvt.u32.u16 $r1, %ctaid.x |  | 2 | cvt.u32.u16 $r1, %ctaid.x
3 | add.u32 $r3, -$r3, 0x00000100 |  | 3 | add.u32 $r3, -$r3, 0x00000100
4 | mul.wide.u16 $r4, $r1.lo, $r3.hi |  | 4 | mul.wide.u16 $r4, $r1.lo, $r3.hi
5 | mad.wide.u16 $r4, $r1.hi, $r3.lo, $r4 |  | 5 | mad.wide.u16 $r4, $r1.hi, $r3.lo, $r4
 | …… |  |  | ……
49 | cvt.s32.s32 $r2, -$r2 |  | 49 | cvt.s32.s32 $r2, -$r2
50 | and.b32 $p0¦$o127, $r5, $r2 |  | 50 | and.b32 $p0¦$o127, $r5, $r2
51 | ssy 0x00000228 |  | 51 | ssy 0x00000228
52 | mov.u32 $r2, $r124 |  | 52 | mov.u32 $r2, $r124
53 | @$p0.eq bra l0x00000228 |  | 53 | @$p0.eq bra l0x00000228
54 | add.half.u32 $r7, s[0x0038], $r1 |  |  | 
55 | mov.half.u32 $r2, s[0x0030] |  |  | 
56 | mul.wide.u16 $r8, $r2.lo, $r7.hi |  |  | 
57 | mad.wide.u16 $r8, $r2.hi, $r7.lo, $r8 |  |  | 
58 | shl.u32 $r8, $r8, 0x00000010 |  |  | 
 | …… |  |  | 
66 | min.s32 $r7, s[$ofs2+0x0040], $r8 |  |  | 
67 | ld.global.u32 $r2, [$r2] |  |  | 
68 | add.u32 $r2, $r2, $r7 |  |  | 
69 | mov.u32 s[$ofs3+0x0440], $r2 |  |  | 
70 | mov.u32 $r2, 0x00000001 |  |  | 
71 | l0x00000228: nop |  | 54 | l0x00000228: nop
72 | bar.sync 0x00000000 |  | 55 | bar.sync 0x00000000
73 | set.eq.s32.s32 $p0/$o127, $r6, $r1 |  | 56 | set.eq.s32.s32 $p0/$o127, $r6, $r1
74 | @$p0.ne bra l0x000002b8 |  | 57 | @$p0.ne bra l0x000002b8
75 | set.ne.s32.s32 $p1/$r1, $r2, $r124 |  | 58 | set.ne.s32.s32 $p1/$r1, $r2, $r124
 | …… |  |  | ……
529 | set.eq.s32.s32 $p0/$o127, $r6, $r1 |  | 512 | set.eq.s32.s32 $p0/$o127, $r6, $r1
530 | @$p0.ne bra l0x000002b8 |  | 513 | @$p0.ne bra l0x000002b8
531 | l0x000002b8: set.ne.s32.s32 $p0/$o127, $r2, $r124 |  | 514 | l0x000002b8: set.ne.s32.s32 $p0/$o127, $r2, $r124
532 | bra l0x000002c8 |  | 515 | bra l0x000002c8
533 | l0x000002c8: @$p0.eq retp |  | 516 | l0x000002c8: @$p0.eq retpz
PathFinder K1 |  |  |  | 
1 | shl.u32 $r3, s[0x0010], 0x00000001 |  | 1 | shl.u32 $r3, s[0x0010], 0x00000001
2 | cvt.u32.u16 $r1, %ctaid.x |  | 2 | cvt.u32.u16 $r1, %ctaid.x
3 | add.u32 $r3, -$r3, 0x00000100 |  | 3 | add.u32 $r3, -$r3, 0x00000100
4 | mul.wide.u16 $r4, $r1.lo, $r3.hi |  | 4 | mul.wide.u16 $r4, $r1.lo, $r3.hi
5 | mad.wide.u16 $r4, $r1.hi, $r3.lo, $r4 |  | 5 | mad.wide.u16 $r4, $r1.hi, $r3.lo, $r4
 | …… |  |  | ……
49 | cvt.s32.s32 $r2, -$r2 |  | 49 | cvt.s32.s32 $r2, -$r2
50 | and.b32 $p0¦$o127, $r5, $r2 |  | 50 | and.b32 $p0¦$o127, $r5, $r2
51 | ssy 0x00000228 |  | 51 | ssy 0x00000228
52 | mov.u32 $r2, $r124 |  | 52 | mov.u32 $r2, $r124
53 | @$p0.eq bra l0x00000228 |  | 53 | @$p0.eq bra l0x00000228
54 | add.half.u32 $r7, s[0x0038], $r1 |  |  | 
55 | mov.half.u32 $r2, s[0x0030] |  |  | 
56 | mul.wide.u16 $r8, $r2.lo, $r7.hi |  |  | 
57 | mad.wide.u16 $r8, $r2.hi, $r7.lo, $r8 |  |  | 
58 | shl.u32 $r8, $r8, 0x00000010 |  |  | 
 | …… |  |  | 
66 | min.s32 $r7, s[$ofs2+0x0040], $r8 |  |  | 
67 | ld.global.u32 $r2, [$r2] |  |  | 
68 | add.u32 $r2, $r2, $r7 |  |  | 
69 | mov.u32 s[$ofs3+0x0440], $r2 |  |  | 
70 | mov.u32 $r2, 0x00000001 |  |  | 
71 | l0x00000228: nop |  | 54 | l0x00000228: nop
72 | bar.sync 0x00000000 |  | 55 | bar.sync 0x00000000
73 | set.eq.s32.s32 $p0/$o127, $r6, $r1 |  | 56 | set.eq.s32.s32 $p0/$o127, $r6, $r1
74 | @$p0.ne bra l0x000002b8 |  | 57 | @$p0.ne bra l0x000002b8
75 | set.ne.s32.s32 $p1/$r1, $r2, $r124 |  | 58 | set.ne.s32.s32 $p1/$r1, $r2, $r124
 | …… |  |  | ……
529 | set.eq.s32.s32 $p0/$o127, $r6, $r1 |  | 512 | set.eq.s32.s32 $p0/$o127, $r6, $r1
530 | @$p0.ne bra l0x000002b8 |  | 513 | @$p0.ne bra l0x000002b8
531 | l0x000002b8: set.ne.s32.s32 $p0/$o127, $r2, $r124 |  | 514 | l0x000002b8: set.ne.s32.s32 $p0/$o127, $r2, $r124
532 | bra l0x000002c8 |  | 515 | bra l0x000002c8
533 | l0x000002c8: @$p0.eq retp |  | 516 | l0x000002c8: @$p0.eq retpz
MSK SDC OTR
MSK SDC OTR
Extrapolate
Notes: Use b to represent a. we ve done evertyh

## Slide 9: Progressive Fault Sites Pruning
Thread-wise pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
....
....
....
....
K-Means K1
34 loop iterations
Notes: No data dependency

## Slide 10: Progressive Fault Sites Pruning
Thread-wise pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
....
....
....
....
MVT K1
Notes: 图示 怎么选。等间距

## Slide 11: Evaluation
Fault Site Pruning vs. Baseline
  Baseline: 60K fault sites (confidence interval=99.8%, error margin=1.26%)
    Closest to ground truth
Notes: 16 benchmarks from rodinia and polybench

## Slide 12: Evaluation
Fault Site Pruning vs. Baseline (closest to ground truth)
  Baseline: 60K fault sites (confidence interval=99.8%, error margin=1.26%)
Notes: 16 benchmarks from rodinia and polybench

## Slide 13: Evaluation
23K
60K
1K
4K
354K
27M
Effectiveness
Notes: Log scale

## Slide 14: Evaluation
23K
60K
1K
4K
354K
27M
Effectiveness
Notes: 先放60K

## Slide 15: Evaluation
23K
60K
1K
4K
354K
27M
Effectiveness
Notes: 先放60K

## Slide 16: Evaluation
23K
60K
1K
4K
354K
27M
Effectiveness
Notes: 先放60K

## Slide 17: Evaluation
23K
60K
1K
4K
354K
27M
Effectiveness
Notes: 先放60K

## Slide 18: Evaluation
Effectiveness
23K
60K
1K
4K
354K
27M
 | Exhaustive Fault Sites | Pruned Fault Sites
Average |  | 
Min |  | 
Max |  | 
 | Exhaustive Fault Sites | Pruned Fault Sites
Average |  | 
Min |  | 
Max |  | 
108,403x Reduction!
Notes: Original ; 32x / 1000x reduction.

## Slide 19: Conclusion
GPGPU applications: huge unreachable exhaustive fault sites
Progressive Fault Site Pruning
  GPGPU-specific features
Accurate GPU reliability assessment
Significant reduction:
  Up to 7 orders of magnitude
  108,403x on average
Notes: Original ; 32x / 1000x reduction.

## Slide 20: Fault Site Pruning for Practical Reliability Analysis of GPGPU Applications
Bin Nie, Lishan Yang, Adwait Jog, and Evgenia Smirni
College of William & Mary
This work is supported by NSF grants CCF-17175332 (CRII) and CCF-1750667 (CORE Small)717532
Thank you :)
Notes: Thanks for the NSF grants, and thank you for listening. research Internship and other opportunities. I am glad to take any questions.
Good question!

## Slide 21
# Exhaustive fault sites
Program vulnerability factor (PVF)
t-statistic
(confidence interval)
Error margin
# samples
Unknown
Notes: Backup: why 60K? Fomular. Not necessary

## Slide 22: Progressive Fault Sites Pruning
Thread-wise pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
....
....
....
....
0
31
Destination Register
Notes: 图示 怎么选。等间距

## Slide 23: Progressive Fault Sites Pruning
Thread-wise pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
....
....
....
....
0
31
Destination Register
Notes: 图示 怎么选。等间距

## Slide 24: Progressive Fault Sites Pruning
Thread-wise pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
....
....
....
....
0
31
Destination Register
Notes: 图示 怎么选。等间距

## Slide 25: Progressive Fault Sites Pruning
Thread-wise pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
....
....
....
....
0
31
Destination Register
Notes: 图示 怎么选。等间距

## Slide 26: Progressive Fault Sites Pruning
Thread-wise pruning
Instruction-wise pruning
Loop-wise pruning
Bit-wise pruning
....
....
....
....
MVT K1
0
31
Destination Register
Notes: 图示 怎么选。等间距