## Slide 1: RCoal: Mitigating GPU Timing Attack via Subwarp-based Randomized Coalescing Techniques
Gurunath Kadam (College of William and Mary)
Danfeng Zhang (Penn State University)
Adwait Jog (College of William and Mary)

## Slide 2: Correlation Timing Attacks
Plaintexts | Ciphertexts | Time duration
Plaintext # 1
time1
timestart
- timestop = time1
Plaintext # 2
time2
Plaintext # 3
time3
…
…
Attacker
Server
Ciphertext # 1
Ciphertext # 2
Ciphertext # 3
…
K1 , K2 , … ,
Ki
, …
Key guesses
Correct Key
Correct Key??
Notes: This should be a general timing attack description

## Slide 3: Correlation Timing Attacks
GPU
Are GPUs vulnerable to Correlation Timing Attacks?
GPUs implement SIMD paradigm
Fast and energy efficient computations
Accelerate the cryptographic algorithms
Notes: Highlight the GPU – Make bigger put block
Highlight the importance of GPU in words

## Slide 4: Executive summary
Prior Work: Correlation Timing Attacks on GPUs ([Jiang/Fei/Kaeli, HPCA’16])
  Key idea: Last round memory accesses can be determined using AES key.
  Memory accesses are coalesced together deterministically by GPUs and hence can be calculated correctly by an attacker.
  Number of coalesced memory accesses correlates with the execution time.
  Attacker can recover AES key by correlating the execution time and the calculated coalesced accesses.
Our Contribution: Randomizing the Coalescing Mechanism (RCoal)
  Goal: Make the calculation of coalesced accesses harder for the attacker.
  Our proposal: Three novel coalescing mechanisms that randomize the size, number, and thread-elements of a sub-warp.
  Results: RCoal improves security by 24- to 961- times at a modest performance loss of 5 to 28%.
Notes: In to two slides – show successful and unsuccessful correlation plots

## Slide 5: Outline
Introduction
Background
  Memory Access Coalescing in GPU
  Baseline Correlation Timing Attack on GPU

## Slide 6: Outline
Introduction
Background
RCoal Security Schemes
Evaluation
Conclusions

## Slide 7: Outline
Introduction
Background
RCoal Security Schemes
Evaluation
Conclusions

## Slide 8: Outline
Introduction
Background
  Memory Access Coalescing in GPU
  Baseline Correlation Timing Attack on GPU
RCoal Security Schemes
Evaluation
Conclusion

## Slide 9: Memory Access Coalescing in GPUs
Streaming Multiprocessor
Warp pool
Warp
Thread # 1
Thread # 32
. . .
Warp Scheduler
LD/ST Unit
Global Memory
Coalescing Unit

## Slide 10: Memory Access Coalescing in GPUs
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x00
sid = 0
0x04
sid = 0
0x07
sid = 0
0x09
sid = 0
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
WARP
sid = subwarp id
tid = thread id
Block Address # 0
Block Address # 1
Block Address # 1
Block Address # 2

## Slide 11: Memory Access Coalescing in GPUs
Coalescing Unit
0x00
0x01
0x02
0x03
0x08
0x09
0x0A
0x0B
0x00
sid = 0
0x04
sid = 0
0x07
sid = 0
0x09
sid = 0
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
WARP
SUBWARP
sid = subwarp id
tid = thread id
Block Address # 0
Block Address # 1
Block Address # 2

## Slide 12: Outline
Introduction
Background
  Memory Access Coalescing in GPU
  Baseline Correlation Timing Attack on GPU
RCoal Security Schemes
Evaluation
Conclusion

## Slide 13: AES implementation on GPU
Symmetric Encryption with 128-bit key and 10 rounds.
S-box implementation involves table lookups.
[Jiang/Fei/Kaeli, HPCA’16] demonstrated that the last round is vulnerable.

## Slide 14: AES implementation on GPU
Symmetric Encryption with 128-bit key and 10 rounds.
S-box implementation involves table lookups.
[Jiang+, HPCA’2016] demonstrated that the last round is vulnerable.
Last round on GPU
cj | = jth column of the ciphertext (output of the round)
tid | = thread id
ti | = ith column of the input text to the last round (input to the round)
kj | = jth key byte of AES key
T4[] | = Table look-up operation (generates memory access)

## Slide 15: AES implementation on GPU
Last round on GPU
c7 58 ee 66 57 29 af ab 8b fd 76 4e e7 5b df 05
f7 92 2f b7 a6 01 6a 5c 2c b7 72 87 77 60 cd e8
. . .
2e 7d bb 49 22 58 22 cd 3d 19 0b ec 64 a6 a9 d4
bb 17 89 88 4f d2 a8 9f 1b 7a 4d c4 c8 73 27 c6
. . .
1d 84 26 a6 bd 41 f1 b3 5e bc 50 21 e1 4c c3 79
91 9b a7 58 b2 46 a1 b0 e6 b3 01 b5 14 cd 10 d9
59 fc e4 34 18 b7 84 61 1a 96 15 5e 36 b8 49 32
jth key byte
ith column
AES Key
Input to the last round
tid = thread id
cjtid = jth column of ciphertext

## Slide 16: AES implementation on GPU
Last round on GPU
c7 58 ee 66 57 29 af ab 8b fd 76 4e e7 5b df 05
f7 92 2f b7 a6 01 6a 5c 2c b7 72 87 77 60 cd e8
. . .
2e 7d bb 49 22 58 22 cd 3d 19 0b ec 64 a6 a9 d4
bb 17 89 88 4f d2 a8 9f 1b 7a 4d c4 c8 73 27 c6
. . .
1d 84 26 a6 bd 41 f1 b3 5e bc 50 21 e1 4c c3 79
91 9b a7 58 b2 46 a1 b0 e6 b3 01 b5 14 cd 10 d9
59 fc e4 34 18 b7 84 61 1a 96 15 5e 36 b8 49 32
jth key byte
ith column
AES Key
Input to the last round

## Slide 17: Last Round of AES on GPU

## Slide 18: Last Round of AES on GPU
LINE # 1
LINE # 2
LINE # 32
…
…
ti1
ti2
ti32
.
.
.
Input text
to Last Round
…
…
.
.
.
Thread # 1
Thread # 2
.
.
.
Thread # 32
.
.
.
T4[ti2]
T4[ti1]
T4[ti32]
Request # 1
Request # 2
.
.
.
Request # 32
Coalescing
Unit
.
.
.
⊕ kj
⊕ kj
⊕ kj
Replies # 1
Replies # 2
.
.
.
Replies # 32
cj1
cj2
cj32
.
.
.
Ciphertext

## Slide 19: Outline
Introduction
Background
  Memory Access Coalescing in GPU
  AES implementation on GPU
  Correlation Timing Attack on GPU
RCoal Security Schemes
Evaluation
Conclusion

## Slide 20: Correlation Timing Attack on GPU [Jiang+, HPCA’16]
Goal of the attack: Recover all 16 bytes of the AES Key
Attacker
Server
Plaintexts | Ciphertexts | Time duration
Plaintext # 1
Execution time1
Plaintext # 2
Execution time2
Plaintext # 3
Execution time3
…
…
Ciphertext # 1
Ciphertext # 2
Ciphertext # 3
…
Notes: After the goal, Attack model – using figure slide 2. What is available to the attacker – ciphertext, execution time and AES Tables.

## Slide 21: Correlation Timing Attack on GPU
Goal of the attack: Recover all 16 bytes of the AES Key
Last Round of AES is vulnerable
Last Round is invertible
Attacker can find number of coalesced accesses per warp
Memory access
of thread tid
Associate the number of coalesced accesses with execution time
Notes: After the goal, Attack model – using figure slide 2. What is available to the attacker – ciphertext, execution time and AES Tables.

## Slide 22: Coalesced Accesses and Execution Time
How an attacker can calculate the number of coalesced accesses?
Notes: Say on our set-up

## Slide 23: Calculation of number of coalesced accesses
Last Round of AES
Invertible
Memory access
of thread tid

## Slide 24: Calculation of number of coalesced accesses
…
…
cj1
cj2
cj32
.
.
.
Ciphertext
.
.
.
⊕ kjm
⊕ kjm
⊕ kjm
.
.
.
.
.
.
T4-1[cj2⊕kjm]
T4-1[cj1⊕kjm]
T4-1[cj32⊕kjm]
ti1,m
ti2,m
ti32,m
.
.
.
Guessed Table
Lookup Indices
.
.
.
.
.
.
Coalesced Accesses
(Ajm,n)
Correct value of key byte?

## Slide 25: Calculation of number of coalesced accesses
…
…
cj1
cj2
cj32
.
.
.
Ciphertext
Thread # 1
Thread # 2
.
.
.
Thread # 32
.
.
.
⊕ kjm
⊕ kjm
⊕ kjm
.
.
.
.
.
.
T4-1[cj2⊕kjm]
T4-1[cj1⊕kjm]
T4-1[cj32⊕kjm]
ti1,m
ti2,m
ti32,m
.
.
.
Guessed Table
Lookup Indices
.
.
.
.
.
.
Coalesced Accesses
(Ajm,n)
Correct value of key byte?

## Slide 26: Finding the Correct Key Value
Attacker encrypts ‘N’ number of plaintexts over server
  Records Ciphertext and Execution time
Aj0,1, Aj0,2, . . . . , Aj0,N
E1,E2,...,EN
Key Guess 0
Key Guess 1
Key
Guess 255
Corrj0
Corrj1
Corrj255
Key
Guess α
Corrjα
Maximum Correlation
Aj1,1, Aj1,2, . . . . , Aj1,N
Ajα,1, Ajα,2, . . . . , Ajα,N
Aj255,1, Aj255,2, . . . . ,Aj255,N
.
.
.
.
.
.
.
.
.
.
.
.
Recorded
Execution Time
Correct
Key Byte
# of Coalesced Accesses
Correlations
Notes: Eliminate the slide transition

## Slide 27: Finding the Correct Key Value
Attacker encrypts ‘N’ number of plaintexts over server
  Records Ciphertext and Execution time
Aj0,1, Aj0,2, . . . . , Aj0,N
E1,E2,...,EN
Key Guess 0
Key Guess 1
Key
Guess 255
Corrj0
Corrj1
Corrj255
Key
Guess α
Corrjα
Maximum Correlation
Aj1,1, Aj1,2, . . . . , Aj1,N
Ajα,1, Ajα,2, . . . . , Ajα,N
Aj255,1, Aj255,2, . . . . ,Aj255,N
.
.
.
.
.
.
.
.
.
.
.
.
Recorded
Execution Time
Correct
Key Byte
# of Coalesced Accesses
Correlations
Notes: Eliminate the slide transition

## Slide 28: Simulating Timing Attack on our Set-up
Correct guess
Incorrect guesses
Why is Correlation Timing Attack possible?
The baseline attack leverages the deterministic nature of the coalescing mechanism
  Fixed number of subwarps, number of subwarps = 1
  Fixed sizes of subwarp, size of subwarp = 32
  Deterministic mapping of the thread elements to subwarps
How to mitigate Correlation Timing Attacks on GPU?
Notes: TODO: Coalescing good for performance and bad for security

## Slide 29: Why is Correlation Timing Attack possible?
The baseline attack leverages the deterministic nature of the coalescing mechanism
  Fixed number of subwarps, number of subwarps = 1
  Fixed sizes of subwarp, size of subwarp = 32
  Deterministic mapping of the thread elements to subwarps
Defense mechanisms?

## Slide 30: Outline
Introduction
Background
RCoal Security Schemes
  Naïve Solution
  Fixed Sized Subwarp (FSS)
  Random Sized Subwarp (RSS)
  Random Threaded Subwarp (RTS)
Evaluation
Conclusion

## Slide 31: Outline
Introduction
Background
RCoal Security Schemes
  Naïve Solution
  Fixed Sized Subwarp (FSS)
  Random Sized Subwarp (RSS)
  Random Threaded Subwarp (RTS)
Evaluation
Conclusion

## Slide 32: Naïve Solution
Disable coalescing altogether?
  Correlation drops to ~0
  Correct key byte is indistinguishable
Up to 178% performance degradation
  Degradation increases with plaintext size
Correct guess
Naïve solution is Good for Security, Bad for Performance
Offers no tradeoff
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 33: Naïve Solution
Disable coalescing altogether?
  Correlation drops to ~0
  Correct key byte is indistinguishable
Up to 178% performance degradation
  Degradation increases with plaintext size
Correct guess
Naïve solution is Good for Security, Bad for Performance
Offers no tradeoff

## Slide 34: Learnings from Baseline Attack and Naïve Solution
Baseline attack leverages the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps

## Slide 35: Outline
Introduction
Background
RCoal Security Schemes
  Naïve Solution
  Fixed Sized Subwarp (FSS)
  Random Sized Subwarp (RSS)
  Random Threaded Subwarp (RTS)
Evaluation
Conclusion
targets weakness # 1: fixed number of subwarps

## Slide 36: RCoal: Fixed Sized Subwarp (FSS)
Coalescing Unit
0x00
0x01
0x02
0x03
0x08
0x09
0x0A
0x0B
DEFAULT: number of subwarps = 1
0x00
sid = 0
0x04
sid = 0
0x07
sid = 0
0x09
sid = 0
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
FSS: number of subwarps = 2
0x00
sid = 0
0x04
sid = 0
0x07
sid = 1
0x09
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
0x04
0x05
0x06
0x07
Notes: Fixed Size Subwarp eliminates the fixed number of subwarps based determinism.

## Slide 37: FSS Security against Baseline Attack
Correlation between the number of coalesced accesses and the execution time drops
Correct key byte is harder to find
Improved security

## Slide 38: FSS Performance
Memory accesses increase with number of subwarps
Execution time increases with number of subwarps
Performance degrades as number of subwarp increase
Can attacker still recover the AES key?
Notes: Better transition going into FSS attack

## Slide 39: FSS against FSS attack
Attacker can figure out the number of subwarps
Notes: Why FSS attack?

## Slide 40: FSS against FSS attack
Attacker can figure out the number of subwarps
Attacker can calculate per subwarp accesses
Correct guess

## Slide 41: FSS against FSS attack
Attack possible when the attacker can figure out number of subwarps!
  Coalescing still deterministic
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 42: Outline
Introduction
Background
RCoal Security Schemes
  Naïve Solution
  Fixed Sized Subwarp (FSS)
  Random Sized Subwarp (RSS)
  Random Threaded Subwarp (RTS)
Evaluation
Conclusion
targets weakness # 2: fixed size of a subwarp

## Slide 43: RCoal: Random Sized Subwarp (RSS)
Size distribution
Normal Distribution
Skewed Distribution
Mean of the distribution is same as FSS
Security and performance similar to FSS
We select RSS with Skewed Distribution
Mean of the distribution is different than FSS
Large subwarp offers better coalescing
Improved security compared to FSS
Improved performance compared to FSS


RCoal to mitigate the correlation timing
attacks
Targets the deterministic nature of the coalescing mechanism
  Fixed number of subwarps
  Fixed sizes of subwarp
  Deterministic mapping of the thread elements to subwarps
RCoal to mitigate the correlation timing
attacks

## Slide 44: Outline
Introduction
Background
RCoal Security Schemes
  Naïve Solution
  Fixed Sized Subwarp (FSS)
  Random Sized Subwarp (RSS)
  Random Threaded Subwarp (RTS)
Evaluation
Conclusion
targets weakness # 3: deterministic mapping
of thread elements to subwarps

## Slide 45: Random-Threaded Subwarp (RTS)
FSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 0
0x06
sid = 1
0x07
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
FSS+RTS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 1
0x06
sid = 0
0x07
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x04
0x05
0x06
0x07

## Slide 46: RCoal: Random-Threaded Subwarp (RTS)
FSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 0
0x06
sid = 1
0x07
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
FSS+RTS: number of subwarps = 2
0x00
0x01
0x06
0x07
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x04
0x05
0x06
0x07
sid = 0
sid = 0
sid = 1
sid = 1

## Slide 47: RCoal: Random-Threaded Subwarp (RTS)
RSS: number of subwarps = 2
0x00
sid = 0
0x01
sid = 1
0x06
sid = 1
0x08
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
RSS+RTS: number of subwarps = 2
0x00
sid = 1
0x01
sid = 1
0x06
sid = 0
0x08
sid = 1
tid = 0
tid = 1
tid = 2
tid = 3
Coalescing Unit
0x00
0x01
0x02
0x03
0x00
0x01
0x02
0x03
Coalescing Unit
0x00
0x01
0x02
0x03
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B
0x04
0x05
0x06
0x07
0x08
0x09
0x0A
0x0B

## Slide 48: Outline
Introduction
Background
RCoal Security Schemes
Evaluation
Conclusion

## Slide 49: Set-up
AES-128
Plaintext with 32 lines
GPGPUSIM
  15 SMs, 32 threads/warp, one subwarp per coalescing unit (base case)
  GDDR5 Memory with 6 MCs, 16 DRAM-banks, 4 bank-groups/MC
Enhanced Attack Algorithms
  Corresponding Attacks

## Slide 50: RCoal Security Enhancement
Except FSS, all defense mechanisms show improvement in the security
RSS based mechanisms generally offer better security
Theoretically 24x to 961x improvement (detailed analysis in paper)
Chart: Number of Subwarps
| 1 | 2 | 4 | 8 | 16 | 32
FSS | 0.99846 | 0.99941 | 0.99935 | 0.99771 | 0.94154 | 0
FSS+RTS | 0.99846 | 0.42426 | 0.2569 | 0.080777 | 0.04366 | 0
RSS | 0.99846 | 0.2467 | 0.15489 | 0.13513 | 0.14823 | 0
RSS+RTS | 0.99846 | 0.15216 | 0.095578 | 0.10696 | 0.065268 | 0
No coalescing,
No correlation

## Slide 51: RCoal Performance
Performance suffers as number of subwarp increase
RSS offers better performance as compared to FSS
RTS does not affect the performance
Chart: Number of Subwarps
| 1 | 2 | 4 | 8 | 16 | 32
FSS | 1 | 1.0822 | 1.1525 | 1.2189 | 1.2788 | 1.3801
FSS+RTS | 1 | 1.082 | 1.1527 | 1.2198 | 1.2787 | 1.3801
RSS | 1 | 1.0538 | 1.104 | 1.1534 | 1.2455 | 1.3801
RSS+RTS | 1 | 1.0544 | 1.1013 | 1.1547 | 1.2455 | 1.38

## Slide 52: Trade-off between Security and Performance

## Slide 53
Chart: Number of Subwarp
| 1 | 2 | 4 | 8 | 16 | 32
FSS | 0.99846 | 0.99941 | 0.99935 | 0.99771 | 0.94154 | 0
FSS+RTP | 0.99846 | 0.42426 | 0.2569 | 0.080777 | 0.04366 | 0
RSS | 0.99846 | 0.2467 | 0.15489 | 0.13513 | 0.14823 | 0
RSS+RTP | 0.99846 | 0.15216 | 0.095578 | 0.10696 | 0.065268 | 0
Chart: Number of Subwarps
| 1 | 2 | 4 | 8 | 16 | 32
FSS | 1 | 1.0822 | 1.1525 | 1.2189 | 1.2788 | 1.3801
FSS+RTS | 1 | 1.082 | 1.1527 | 1.2198 | 1.2787 | 1.3801
RSS | 1 | 1.0538 | 1.104 | 1.1534 | 1.2455 | 1.3801
RSS+RTS | 1 | 1.0544 | 1.1013 | 1.1547 | 1.2455 | 1.38
Security
(Lower the better)
Execution Time
(Lower the better)
RCoal_Score
Notes: Mention Rcoal in a BOX

## Slide 54: Conclusions
We proposed RCoal, a set of three novel defense mechanisms
  To mitigate the correlation timing attacks
  Randomizes the memory access coalescing
  Scales with the plaintext size (analysis in paper)
RCoal offers a trade-off between security and performance
RCoal improves security by 24- to 961- times at a modest performance loss of 5 to 28%.
Notes: Try to reduce background and introduce rcoal_score

## Slide 55: RCoal: Mitigating GPU Timing Attack via Subwarp-based Randomized Coalescing Techniques
Gurunath Kadam (College of William and Mary)
Danfeng Zhang (Penn State University)
Adwait Jog (College of William and Mary)
Thank you!
Questions?
We acknowledge the support of the National Science Foundation (NSF) grants (#1657336 and #1717532).

## Slide 56: Backup Slides

## Slide 57: Implementation
Bits needed
  # of threads * # warp scheduler * range
  = 32 * 2 * 5 = 320 bits
.
.
.
Memory Requests from
Threads
TID | SUB_ID | Request Size | Base Address | Offset Address
tid | sid | Entry |  | 
tid | sid | Entry |  | 
tid | sid | Entry |  | 
Pending Request Table
Memory Access Coalescing
.
.
.
.
.
.
.
.
.
Coalescing Unit
Global Memory

## Slide 58: RCoal Scaling
Plaintext with 1024 lines
  32 warps
Security
Chart: Correlation
| 1 | 2 | 4 | 8 | 16 | 32
FSS | 1 | 1 | 1 | 1 | 1 | 0
FSS+RTS | 1 | 0.41789 | 0.20496 | 0.086097 | 0.024681 | 0
RSS | 1 | 0.02934 | 0.0040024 | 0.024517 | 0.033002 | 0
RSS+RTS | 1 | 0.0055896 | 0.014546 | 0.0012553 | 0.013116 | 0

## Slide 59: RCoal Scaling
Plaintext with 1024 lines
  32 warps
Performance
Chart: Execution Time
| 1 | 2 | 4 | 8 | 16 | 32
FSS | 1 | 1.423 | 1.7565 | 2.0303 | 2.2726 | 2.6863
FSS-RTS | 1 | 1.4228 | 1.7568 | 2.0291 | 2.2728 | 2.687
RSS | 1 | 1.2896 | 1.5308 | 1.7638 | 2.1481 | 2.6863
RSS-RTP (Skewed) | 1 | 1.2896 | 1.5315 | 1.7649 | 2.1475 | 2.6863

## Slide 60: RCoal_Score
Security Oriented (a=1, b=1)
Performance Oriented (a=1, b=20)