## Slide 1: µC-States: Fine-grained GPU Datapath Power Management
Onur Kayıran, Adwait Jog, Ashutosh PattnaIk, Rachata Ausavarungnirun, Xulong Tang, Mahmut T. Kandemir, Gabriel H. Loh, Onur Mutlu, Chita R. Das

## Slide 2: Executive Summary
The peak throughput and individual capabilities of the GPU cores are increasing
  Lower and imbalanced utilization of datapath components
We identify two key problems:
  Wastage of datapath resources and increased static power consumption
  Performance degradation due to contention in memory hierarchy
Our Proposal - µC-States:
  A fine-grained dynamic power- and clock-gating mechanism for the entire datapath based on queuing theory principles
  Reduces static and dynamic power, improves performance

## Slide 3: Big Cores vs. Small Cores
SLA & MM
  Performance
  Leakage power
SCAN & SSSP
  Performance
  Leakage power
BLK & SCP
  Performance
  Leakage power
Chart: Normalized Value
| SLA | MM | SCAN | SSSP | BLK | SCP
IPC | 1.451 | 1.3049 | 1.0333 | 1.0055 | 0.83748 | 0.88277
Leakage | 1.4356 | 1.4356 | 1.4356 | 1.4356 | 1.4356 | 1.4356

## Slide 4: Outline
Summary
Background
Motivation and Analysis
Our Proposal
Evaluation
Conclusions

## Slide 5: Background
Per GPU core:
  4 wavefront schedulers
  64 shader processors
  32 LD/ST units
Evaluation of larger GPU cores
A High-End GPU Datapath
Instruction Cache
Wavefront Scheduler
Register File
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
LD/ST
SFU
SFU
SFU
SFU
SFU
SFU
SFU
SFU
Interconnect Network
Shared Memory/L1 Cache
Constant Cache
Wavefront Scheduler
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
SP
Wavefront Scheduler
Wavefront Scheduler
Dispatch Unit
Dispatch Unit
Dispatch Unit
Dispatch Unit
Texture Cache
Notes: Give a high level description of how everything works: instruction cache and buffer, then goes to wf scheduler. Accesses the register file, goes to functional units (i.e., sp, sfu or ld/st depending on the type of instruction), goes through the interconnect to access L1 caches. Note that this figure depicts a single GPU core.
We evaluate large GPU cores unlike any previous academic papers

## Slide 6: Background
The datapath can be modeled as a simple queuing system
  Component with the highest utilization is the bottleneck
Utilization Law [Jain, 1991]:
  Utilization = Service time * Throughput
  SP and SFU units have deterministic service times
  LD/ST unit waits for response from the memory system
  Used to calculate the component with highest utilization
Little’s Law [Little, OR 1961]:
  Number of jobs in the system = Arrival rate * Response time
  Response time includes queuing delays
  Used to estimate Response Time of memory instructions in LD/ST unit
Analyzing Core Bottlenecks
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
Wavefront
Scheduler
(SCH)
Fetch/Decode
(IFID)
Pipeline Register
Operand Collector
Pipeline Register
Execution Unit

## Slide 7: Background
Power-gating reduces static power
Clock-gating reduces dynamic power
Power-gating leads to loss of data
  Employ clock-gating for:
    Instruction buffer, pipeline registers, register file banks, and LD/ST queue
Power-gating overheads
  Wake-up delay: Time to power on a component
  Break-even time: Shortest time to power-gate to compensate for the energy overhead
Power- and Clock-Gatıng
Notes: Power gating has more potential power benefits
This slide can go to backups

## Slide 8: Outline
Summary
Background
Motivation and Analysis
Our Proposal
Evaluation
Conclusions

## Slide 9: Motivation and Analysis
Chart: ALU Utilization
| 4.0 | 3.0 | 3.0 | 4.0 | 2.0 | 2.0 | 1.0 | 2.0 | 2.0 | 8.0
 | 8 | 8 | 6 | 4 | 2 | 7 | 3 | 4 | 1 | 3
ALU and LDST Utilization w/ Real Experiments
Chart: ALU Utilization
| 3.0 | 1.0 | 4.0 | 5.0 | 4.0 | 4.0 | 7.0 | 4.0 | 2.0 | 3.0 | 2.0 | 3.0 | 5.0 | 3.0 | 3.0 | 2.0 | 4.0 | 1.0 | 8.0 | 4.0 | 6.0 | 2.0 | 3.0 | 1.0 | 1.0 | 4.0 | 5.0
 | 2 | 1 | 5 | 6 | 5 | 4 | 4 | 4 | 8 | 4 | 4 | 8 | 4 | 8 | 8 | 8 | 2 | 6 | 5 | 6 | 5 | 8 | 8 | 6 | 5 | 8 | 8
NVIDIA K20 GPU
NVIDIA GTX 660 GPU
Low ALU utilization
High LD/ST unit utilization
Notes: ALU utilization is very low
LDST utilization is typically on the high end

## Slide 10: Motivation and Analysis
Per-component Utilization W/ Simulation
High LD/ST unit utilization
Low ALU utilization
Potential bottlenecks
Notes: 1- Real exp. And simulations follow the same trends – high LDST utilization, low ALU utilization
2- Bottleneck for SP or SFU instructions in apps with high ALU utilization is one of IFID, SCH, OCEX, or EX units.
3- Bottleneck for LDST heavy apps are either the memory pipeline or the memory system

## Slide 11: Motivation and Analysis
Compute-intensive application
Application Sensitivity to Datapath Components
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
Wavefront
Scheduler
(SCH)
Fetch/Decode
(IFID)
Pipeline Register
Operand Collector
Pipeline Register
Execution Unit

## Slide 12: Motivation and Analysis
Compute-intensive application
  Halving the width of the red components -> No performance impact
  Halving the width of all components -> 30% lower performance
Application Sensitivity to Datapath Components
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
Wavefront
Scheduler
(SCH)
Fetch/Decode
(IFID)
Pipeline Register
Operand Collector
Pipeline Register
Execution Unit
Many components are
critical for performance

## Slide 13: Motivation and Analysis
Application with LD/ST unit bottleneck
Application Sensitivity to Datapath Components
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
Wavefront
Scheduler
(SCH)
Fetch/Decode
(IFID)
Pipeline Register
Operand Collector
Pipeline Register
Execution Unit

## Slide 14: Motivation and Analysis
Application with LD/ST unit bottleneck
  Halving the width of the blue components -> No performance impact
Application Sensitivity to Datapath Components
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
Wavefront
Scheduler
(SCH)
Fetch/Decode
(IFID)
Pipeline Register
Operand Collector
Pipeline Register
Execution Unit

## Slide 15: Motivation and Analysis
Application with LD/ST unit bottleneck
  Halving the width of the blue components -> No performance impact
  Halving the width of the blue + red components -> 4% performance loss
Application Sensitivity to Datapath Components
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
Wavefront
Scheduler
(SCH)
Fetch/Decode
(IFID)
Pipeline Register
Operand Collector
Pipeline Register
Execution Unit

## Slide 16: Motivation and Analysis
Application with LD/ST unit bottleneck
  Halving the width of the blue components -> No performance impact
  Halving the width of the blue + red components -> 4% performance loss
  Halving the width of the blue + red components + LD/ST unit -> 35% performance loss
Application Sensitivity to Datapath Components
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
Wavefront
Scheduler
(SCH)
Fetch/Decode
(IFID)
Pipeline Register
Operand Collector
Pipeline Register
Execution Unit
LD/ST unit is the bottleneck

## Slide 17: Motivation and Analysis
Application with memory system bottleneck
  Similar to QTC, but it has very high memory response time
Application Sensitivity to Datapath Components
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
Wavefront
Scheduler
(SCH)
Fetch/Decode
(IFID)
Pipeline Register
Operand Collector
Pipeline Register
Execution Unit

## Slide 18: Motivation and Analysis
Application with memory system bottleneck
  Similar to QTC, but it has very high memory response time
  Halving the width of LD/ST unit does not degrade performance
Application Sensitivity to Datapath Components
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
Wavefront
Scheduler
(SCH)
Fetch/Decode
(IFID)
Pipeline Register
Operand Collector
Pipeline Register
Execution Unit

## Slide 19: Motivation and Analysis
Application with memory system bottleneck
  Similar to QTC, but it has very high memory response time
  Halving the width of LD/ST unit does not degrade performance
  Halving the width of the wavefront scheduler -> 19% performance improvement
Application Sensitivity to Datapath Components
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
Wavefront
Scheduler
(SCH)
Fetch/Decode
(IFID)
Pipeline Register
Operand Collector
Pipeline Register
Execution Unit
Memory system is the bottleneck,
not the LD/ST unit.
Higher issue width degrades performance!

## Slide 20: Motivation and Analysis
In memory-bound applications, performance degrades with the increase in L1 stalls
Applications with Memory System Bottleneck
Chart: 
| BLK | SCP | RED | RAY | TRA | SPMV | ST2D | PVC | LIB | JPEG
Normalized performance | 0.7631 | 0.8562 | 0.89389 | 0.90969 | 0.91158 | 0.93131 | 0.97283 | 0.99139 | 1.0047 | 1.0168
Normalized stall cycles per L1 miss | 1.3508 | 1.1889 | 1.1703 | 1.1477 | 1.1043 | 1.1319 | 1.0134 | 0.98189 | 0.97306 | 0.97539
average | 1 | 1

## Slide 21: Motivation and Analysis
2 outstanding requests / unit time
Instruction latency = 1 time unit
Applications with Memory System Bottleneck
3 outstanding requests / unit time
More contention
Instruction latency > 2 time units
The problem aggravates with divergent applications
Single issue width
Double issue width
time
Wavefront 1
R1
R2
Time unit 1
time
W1-R1
Wavefront 1
Wavefront 2
Time unit 1
Time unit 2
W1-R2
W2-R1
W2-R2
When memory system is the bottleneck,
higher issue width might degrade performance!
Notes: Assume that the memory bandwidth is limited, and can only serve two requests in one unit time.
Divergent app: more requests from the same wavefront

## Slide 22: Motivation and Analysis
Observation: Low ALU utilization, high LD/ST unit utilization
Compute-intensive applications: Bottleneck can be fetch/decode units, wavefronts schedulers, or execution units
Memory-intensive applications: Bottleneck can be the LD/ST unit, or the memory system
Applications with memory system bottleneck: Divergent applications can lose performance with high issue width
Key Insights

## Slide 23: Outline
Summary
Background
Motivation and Analysis
Our Proposal
Evaluation
Conclusions

## Slide 24: µC-States
Goal:
  To reduce the static and dynamic power of the GPU core pipeline
  To maintain, and when possible improve performance
Power benefits:
  Based on bottleneck analysis
  Power- or clock-gates components that are not critical for performance
  Employs clock-gating for components that hold execution state, or hold data for long periods
Performance benefits:
  Reducing issue width when memory system is the bottleneck improves performance
  Only half the width of each component is gated
Key Ideas

## Slide 25: µC-States
Periodically goes through three phases
First phase: Execution units and LD/ST unit
  Power-gates execution units with low utilization
  Clock-gates LD/ST units when memory response time (estimated by Little’s Law) is high
Second phase: Register file banks and pipeline registers
  Compares the utilization of each component with its corresponding execute stage unit
  If lower, they are not bottleneck, and can be gated-off
Third phase: Wavefront scheduler and fetch/decode units
  Compares scheduler utilization to cumulative executive stage utilization
  If lower, issue width is halved
  If fetch/decode utilization is lower than scheduler’s, fetch/decode width is halved
Algorithm Details
Phase 1
Phase 2
Phase 3
IDOCSP
IDOCSFU
IDOCLDST
OCSP
OCSFU
OCLDST
OCEXSP
OCEXSFU
OCEXLDST
EXSP
EXSFU
EXLDST
SCH
IFID
Gating Controller
C
C
C
C
C
C
C
C
C
C
C
P
P
P
P
Notes: Mention again that some units are clock gated and some units are power gated.

## Slide 26: µC-States
Employed at coarse time granularity
Not sensitive to overheads related to entering or exiting power-gating states
Independent of the underlying wavefront scheduler
Issue width sizing is fundamentally different than thread-level parallelism management
  Comparison to CCWS [Rogers+, MICRO 2012]
More in the Paper

## Slide 27: Outline
Summary
Background
Motivation and Analysis
Our Proposal
Evaluation
Conclusions

## Slide 28: Evaluation Methodology
We simulate the baseline architecture using a modified version of GPGPU-Sim v3.2.2 that allows larger GPU cores
GPU-Wattch
  Reports dynamic power
  Area calculations for static power
  Conservative assumption of non-core components, such as the memory subsystem and DRAM, to contribute to 40% of static power
Baseline architecture
  16 Shader Cores, SIMT Width = 32 × 4
  36K Registers, 16kB L1 cache, 48kB shared memory
  GTO wavefront scheduler
  6 shared GDDR5 MCs

## Slide 29: Results Summary
Power Savings
Chart: Normalized Static Power
| BFS | BLK | JPEG | LIB | MUM | NN | RAY | SCP | SLA | TRA | FWT | BP | BTR | HOT | HW | LAV | PATH | MM | SAD | SPMV | PVC | PVR | MD | QTC | RED | SCAN | SPMV-S | ST2D | TRD | BH | DMR | MST | SP | SSSP | GMEAN
uC-States | 0.77252 | 0.97513 | 0.78713 | 0.93991 | 0.77114 | 0.96427 | 0.8553 | 0.83867 | 0.98631 | 0.76791 | 0.77084 | 0.99291 | 0.77265 | 0.98602 | 0.91201 | 0.77359 | 0.98343 | 0.98194 | 0.96715 | 0.773 | 0.77196 | 0.81783 | 0.77114 | 0.77119 | 0.77216 | 0.77355 | 0.77125 | 0.79363 | 0.77002 | 0.77895 | 0.97268 | 0.76823 | 0.771 | 0.77109 | 0.83789
C_HALF | 0.69656 | 0.69656
16% static power savings
All components are half-width
7% dynamic power savings
11% total power savings for the chip

## Slide 30: Results Summary
Performance
Chart: Normalized Performance
| BFS | BLK | JPEG | LIB | MUM | NN | RAY | SCP | SLA | TRA | FWT | BP | BTR | HOT | HW | LAV | PATH | MM | SAD | SPMV | PVC | PVR | MD | QTC | RED | SCAN | SPMV-S | ST2D | TRD | BH | DMR | MST | SP | SSSP | GMEAN
uC-States | 1.0258 | 1.1689 | 1.0024 | 0.99627 | 1.0274 | 1.0037 | 1.0491 | 1.1355 | 1.0028 | 1.0795 | 1.0113 | 1.0069 | 0.98849 | 1.0325 | 1.0016 | 0.99157 | 1.0103 | 1.0331 | 1.043 | 1.0685 | 0.99808 | 1.0143 | 0.99841 | 0.96595 | 1.0676 | 0.97934 | 0.97591 | 0.98282 | 0.99273 | 0.9993 | 0.99926 | 1.069 | 1.0077 | 0.99042 | 1.0203
C_HALF | 1.0316 | 1.1941 | 0.99553 | 0.94634 | 1.025 | 0.82062 | 1.0508 | 1.1328 | 0.68918 | 1.0879 | 1.0109 | 0.88111 | 0.95922 | 0.81686 | 0.69135 | 0.98237 | 0.65118 | 0.76632 | 0.69601 | 1.0865 | 1.004 | 0.94288 | 1.0001 | 0.65114 | 1.0788 | 0.96775 | 0.84451 | 0.93687 | 1.0089 | 0.98604 | 0.81405 | 1.0827 | 1.0099 | 0.99451 | 0.92472
All components are half-width
10% performance improvement over C_HALF
2% performance improvement over the baseline
9% performance improvement for applications with memory system bottleneck

## Slide 31: Results Summary
Heterogeneous-Core GPUs
Chart: Normalized Performance
| BLK_MM | BLK_SAD | BLK_NN | SCP_MM | SCP_SAD | SCP_NN | FWT_MM | FWT_SAD | FWT_NN | GMEAN
C_Half | 0.80651 | 0.8797 | 0.85181 | 0.84675 | 0.87945 | 0.9343 | 0.83077 | 0.93121 | 0.98375 | 0.88108
Heterogeneous | 1.0336 | 0.97148 | 0.95117 | 1.0335 | 0.96257 | 1.0156 | 1.0204 | 0.99356 | 1.0101 | 0.99869
A system with 8 small and 8 big cores
Performs better than 16 small cores
Performs as good as 16 big cores
Has smaller power consumption and area than the 16-core system

## Slide 32: Outline
Summary
Background
Motivation and Analysis
Our Proposal
Evaluation
Conclusions

## Slide 33: Conclusions
Many GPU datapath components are heavily underutilized
More resources in a GPU core can sometimes degrade performance because of contention in the memory system
µC-States minimizes power consumption by turning off datapath components that are not performance bottlenecks, and improves performance for applications with memory system bottleneck
Our analysis could be useful in guiding scheduling and design decisions in a heterogeneous-core GPU with both small and big cores
Our analysis and proposal can be useful for developing other new analyses and optimization techniques for more efficient GPU and heterogeneous architectures

## Slide 34: µC-States: Fine-grained GPU Datapath Power Management
Onur Kayıran, Adwait Jog, Ashutosh PattnaIk, Rachata Ausavarungnirun, Xulong Tang, Mahmut T. Kandemir, Gabriel H. Loh, Onur Mutlu, Chita R. Das
Thanks!
Questions?

## Slide 35: Results Summary
Dynamic adaptation of µC-States to changes in application behavior
Fraction of time that various components are power- or clock-gated
Distribution of static power savings across different components
Power comparison to GPU-Wattch
Sensitivity to TLP-enhancing resources
More In the PAPER

## Slide 36: Backup

## Slide 37: Additional Results
Average Time the Units are on
Chart: Average time the units are on
| BFS | BLK | JPEG | LIB | MUM | NN | RAY | SCP | SLA | STO | TRA | FWT | BP | BTR | GSS | HOT | HW | LAV | PATH | HIST | MM | SAD | SPMV | PVC | PVR | DMEM | MFLP | MD | QTC | RED | SCAN | SPMV-S | ST2D | TRD | BH | DMR | MST | SP | SSSP
IFID | 0.74952 | 0.7602 | 0.71429 | 0.75373 | 0.75061 | 0.94622 | 0.81579 | 0.77632 | 1 | 0.67857 | 0.64923 | 0.7069 | 1 | 0.75472 | 0.73684 | 1 | 0.92857 | 0.75195 | 1 | 0.69054 | 1 | 1 | 0.75735 | 0.75229 | 0.80165 | 0.75093 | 1 | 0.75047 | 0.75113 | 0.75431 | 0.75467 | 0.75103 | 0.75839 | 0.69672 | 0.75586 | 1 | 0.65 | 0.74785 | 0.75062
SCH | 0.50287 | 0.51531 | 0.60714 | 0.50746 | 0.50092 | 0.93022 | 0.56316 | 0.53947 | 1 | 0.5119 | 0.50154 | 0.50647 | 1 | 0.50943 | 0.57895 | 1 | 0.83333 | 0.50195 | 1 | 0.5043 | 1 | 0.96341 | 0.51103 | 0.50459 | 0.60331 | 0.50186 | 1 | 0.50093 | 0.50113 | 0.50647 | 0.50701 | 0.50155 | 0.51007 | 0.50492 | 0.50977 | 1 | 0.50333 | 0.5005 | 0.50062
EX_SP | 0.50382 | 0.98469 | 0.53571 | 0.9403 | 0.50031 | 0.96351 | 0.71053 | 0.67105 | 0.96739 | 0.7619 | 0.50051 | 0.50216 | 0.98148 | 0.50314 | 0.52632 | 0.96939 | 0.83333 | 0.50651 | 0.96053 | 0.5745 | 1 | 0.96341 | 0.50368 | 0.50153 | 0.60331 | 0.50062 | 1 | 0.50031 | 0.50038 | 0.50216 | 0.50234 | 0.50052 | 0.55369 | 0.50164 | 0.51953 | 0.97619 | 0.50111 | 0.50017 | 0.50021
EX_SFU | 0.50096 | 0.98469 | 0.53571 | 0.50249 | 0.50031 | 0.50064 | 0.50526 | 0.51316 | 0.96739 | 0.50397 | 0.50051 | 0.50862 | 1 | 0.50314 | 0.52632 | 0.93878 | 0.50794 | 0.50065 | 0.96053 | 0.50573 | 0.51191 | 0.51219 | 0.50368 | 0.50612 | 0.59091 | 0.50062 | 0.51136 | 0.50031 | 0.50038 | 0.50216 | 0.53738 | 0.50052 | 0.54362 | 0.50164 | 0.5026 | 0.50794 | 0.50111 | 0.50066 | 0.50021
EX_LDST | 0.52964 | 0.52041 | 0.89286 | 1 | 0.50338 | 1 | 0.96316 | 0.52632 | 0.96739 | 1 | 0.54923 | 0.50216 | 0.98148 | 0.98113 | 0.60526 | 1 | 0.92857 | 0.81836 | 1 | 0.51433 | 1 | 1 | 0.51471 | 0.50612 | 0.83884 | 0.50062 | 1 | 0.50124 | 0.93326 | 0.59914 | 0.81776 | 0.99845 | 0.8255 | 0.67869 | 0.58789 | 0.97619 | 0.75778 | 0.51457 | 0.50767

## Slide 38: Additional Results
Savings Breakdown
Chart: Savings Breakdown
| BFS | BLK | JPEG | LIB | MUM | NN | RAY | SCP | SLA | TRA | FWT | BP | BTR | HOT | HW | LAV | PATH | MM | SAD | SPMV | PVC | PVR | MD | QTC | RED | SCAN | SPMV-S | ST2D | TRD | BH | DMR | MST | SP | SSSP | AVG
IFID | 0.74099 | 0.70939 | 0.84523 | 0.72854 | 0.73776 | 0.15909 | 0.54495 | 0.66173 | 0 | 1.0377 | 0.86709 | 0 | 0.72563 | 0 | 0.21131 | 0.7338 | 0 | 0 | 0 | 0.71783 | 0.7328 | 0.58677 | 0.7382 | 0.73623 | 0.72683 | 0.72576 | 0.73653 | 0.71476 | 0.8972 | 0.72225 | 0 | 1.0354 | 0.74595 | 0.73774 | 0.5664
SCH | 0.9768 | 0.95236 | 0.77191 | 0.96777 | 0.98063 | 0.13711 | 0.85834 | 0.90487 | 0 | 0.97941 | 0.96973 | 0 | 0.9639 | 0 | 0.32748 | 0.9786 | 0 | 0 | 0.071886 | 0.96076 | 0.97342 | 0.77945 | 0.98061 | 0.98021 | 0.96973 | 0.96866 | 0.9794 | 0.96265 | 0.97277 | 0.96325 | 0 | 0.97589 | 0.98146 | 0.98121 | 0.71383
EX_SP | 17.1118 | 0.52786 | 16.012 | 2.0589 | 17.2331 | 1.2585 | 9.9832 | 11.3445 | 1.1246 | 17.226 | 17.1694 | 0.63865 | 17.1352 | 1.0557 | 5.7479 | 17.0192 | 1.3613 | 0 | 1.2617 | 17.1169 | 17.191 | 13.681 | 17.233 | 17.2307 | 17.1694 | 17.1631 | 17.2259 | 15.392 | 17.1872 | 16.5701 | 0.82113 | 17.2054 | 17.238 | 17.2366 | 11.498
EX_SFU | 1.663 | 0.051004 | 1.5471 | 1.6579 | 1.6651 | 1.664 | 1.6486 | 1.6223 | 0.10866 | 1.6645 | 1.6374 | 0 | 1.6557 | 0.20402 | 1.6397 | 1.664 | 0.13154 | 1.6265 | 1.6255 | 1.6539 | 1.6458 | 1.3632 | 1.6651 | 1.6649 | 1.659 | 1.5416 | 1.6644 | 1.5208 | 1.6607 | 1.6575 | 1.6397 | 1.6625 | 1.664 | 1.6655 | 1.406

## Slide 39: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2013 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. SPEC is a registered trademark of the Standard Performance Evaluation Corporation (SPEC). Other names are for informational purposes only and may be trademarks of their respective owners.