## Slide 1: Zorua: A Holistic Approach to Resource Virtualization in GPUs
Nandita Vijaykumar
Kevin Hsieh, Gennady Pekhimenko, Samira Khan,
Ashish Shrestha, Saugata Ghose, Adwait Jog, Phillip B. Gibbons, Onur Mutlu

## Slide 2: Overview
Problem: Major on-chip resources in GPUs are managed by the programmer/software
Key Issues: Leads to several challenges in obtaining high performance:
  Programming Ease: Requires programmer effort to optimize resource usage
  Performance Portability: Optimizations do not port well across different GPUs
  Resource Inefficiency: Underutilized resources even in optimized code
Our Goal:
  Reduce dependence of performance on programmer-specified resource usage
  Enhance resource efficiency for optimized code
Our Approach: Decouple the programmer-specified resource usage from the allocation in the hardware
Zorua: A Holistic Resource Virtualization Framework for GPUs
Key Results: Zorua enhances programming ease, performance portability and performance for optimized code

## Slide 3: GPUs today are used across many classes of applications …
GPU
Machine
Learning
Scientific
Simulation
Biomedical Imaging
Computer Vision
. . .

## Slide 4: On-Chip Resources in GPUs
Compute Units
Thread Slots
Register File
Scratchpad
Memory

## Slide 5
Thread Slots
Register File
Scratchpad
Memory
Thread
Block
Work
Group
<#Threads,#Registers>
<#Threads,#Registers,Scratchpad(KB)>
<#Threads>
<>
Thread Slots
Every thread in a thread block needs to be allocated
enough (worst-case) resources to execute and complete

## Slide 6: Abstraction of On-Chip Resources
Register File
Thread Slots
Scratchpad
Memory
Hardware
Programmer/Software
<#Threads,#Registers> per block
<#Threads,#Registers,Scratchpad(KB)> per block
<#Threads> per block
<> per block
Tight coupling between
resource specification and allocation

## Slide 7: Key Issues
Static Underutilization
Dynamic Underutilization

## Slide 8: 1. Static Underutilization
Thread Slots in Hardware
20
Thread Block
10 threads
<#Threads,#Registers,Scratchpad(KB)>
Parallelism:
1 thread block
11 threads
11 threads
Parallelism:
2 thread blocks
20 threads
Static underutilization may lead to
loss in parallelism

## Slide 9: To make things worse…
Same problem exists for other on-chip resources
  registers, scratchpad memory, thread blocks
The programmer needs to get it right for all of them at the same time

## Slide 10: Implication 1: Programming Ease
Chart: Threads/Block
| 32 | 64 | 96 | 128 | 160 | 192 | 224 | 256 | 288 | 320 | 352 | 384 | 416 | 448 | 480 | 512 | 544 | 576 | 608 | 640 | 672 | 704 | 736 | 768 | 800 | 832 | 864 | 896 | 928 | 960 | 992 | 1024
Normalized Execution Time | 1.1273 | 1 | 1.0187 | 1.0198 | 1.0208 | 1.0775 | 1.0771 | 1.0475 | 1.0947 | 1.0294 | 1.1306 | 1.1005 | 1.0438 | 1.2091 | 1.1716 | 1.1338 | 1.1138 | 1.1005 | 1.0583 | 1.033 | 1.5036 | 1.4601 | 1.4072 | 1.3677 | 1.3495 | 1.316 | 1.2692 | 1.2564 | 1.2366 | 1.2029 | 1.1763 | 1.1562
Performance
Cliffs
MST (Minimum Spanning Tree)
Requires programmer effort
to avoid sub-optimal specifications

## Slide 11: Implication 2: Performance Portability
Chart: Threads/Block
| 32 | 64 | 128 | 256 | 512
Maxwell | 1.4947 | 1.2639 | 1.0024 | 1.0004 | 1.3279
Kepler | 1.8206 | 1.1276 | 1 | 1.0127 | 1.1672
Fermi | 3.1634 | 2.2678 | 1.6901 | 1 | 1.9047
DCT (Discrete Cosine Transform)
Programs need to be
retuned to fit different GPUs

## Slide 12: Key Issues
Static Underutilization
Dynamic Underutilization

## Slide 13: 2. Dynamic Underutilization
__global__ void CUDAkernel2DCT(float *dst, float *src, int I){
int OffsThreadInRow = threadIdx.y * B + threadIdx.x;
...
for(unsigned int i = 0; i < B; i++)
bl_ptr[i * X] = src[i * I];
__syncthreads();
...
CUDAsubroutineInplaceDCTvector(…);
for(unsigned int i = 0; i < B; i++)
dst[i *I] = bl_ptr[i * X];
}
16 regs
32 regs
16 regs
Resource requirements of a thread vary throughout execution
Implication:
Resource inefficiency due to
worst-case static allocation

## Slide 14: Our Goal
Reduce the dependence of performance on resource specification
  Programming Ease
  Performance Portability
Improve efficiency of resource utilization
  Higher performance for optimized code

## Slide 15: Outline
Problem: Tight Coupling
Key Implications
Our Goal
Our Approach: Zorua
  Virtualization Strategy
  Design Challenges
  Design Ideas
Evaluation

## Slide 16: Our Approach
Register File
Register File
Thread Slots
Scratchpad
Memory
Hardware Resources
Programmer/Software
Thread Slots
Scratchpad
Memory
Virtual Resources
Decouple resource specification from allocation
Virtualize multiple on-chip resources
Zorua: A Holistic Virtualization Approach

## Slide 17
How do we design a virtualization strategy
to effectively address the key issues?

## Slide 18: 1. Static Underutilization
Thread Slots in Hardware
20
<#Threads,#Registers,Scratchpad(KB)>
Parallelism:
1 thread block
11 threads
11 threads
Parallelism:
2 thread blocks
22 threads
Flexibility in available resources
helps restore parallelism

## Slide 19: Addressing Key Issues
Static Underutilization
Dynamic Underutilization
Provide an illusion of a flexible amount
of resources
Enable dynamic allocation/deallocation
of resources

## Slide 20: Outline
Problem: Tight Coupling
Key Implications
Our Goal
Our Approach: Zorua
  Virtualization Strategy
  Design Challenges
  Design Ideas
Evaluation

## Slide 21: Zorua: Virtualization Strategy
Register File
Thread Slots
Physical Resources
Thread Slots
Virtual Resources
Register File
Scratchpad
Memory
Scratchpad
Memory
Fine-grained dynamic allocation provides
resource efficiency

## Slide 22: Zorua: Virtualization Strategy
Register File
Thread Slots
Physical Resources
Thread Slots
Virtual Resources
Register File
Scratchpad
Memory
Scratchpad
Memory
Swap Space
(in the mem. hierarchy)
Careful oversubscription using a swap space provides flexibility in the amount of resources

## Slide 23: Outline
Problem: Tight Coupling
Key Implications
Our Goal
Our Approach: Zorua
  Virtualization Strategy
  Design Challenges
  Design Ideas
Evaluation

## Slide 24: Zorua: Design Challenges
Challenge 1: Controlling the extent of oversubscription
  Spills are expensive
Challenge 2: Coordinating virtualization of multiple on-chip resources
  Resources are independently virtualized
  Resource requirements vary during execution

## Slide 25: Zorua Design: Key Questions
How do we determine the variation in resource requirements?
How do we use this knowledge to:
  control how much we oversubscribe at run time?
  coordinate allocation of multiple resources to maximize parallelism within the oversubscription budget?

## Slide 26: Outline
Problem: Tight Coupling
Key Implications
Our Goal
Our Approach: Zorua
  Virtualization Strategy
  Design Challenges
  Design Ideas
Evaluation

## Slide 27: Component 1: The Compiler
Leverage software to determine variation in resource requirements
Variation in resource requirements tends to occur in fine-grained phases
__global__ void CUDAkernel2DCT(float *dst, float *src, int I){
int OffsThreadInRow = threadIdx.y * B + threadIdx.x;
for(unsigned int i = 0; i < B; i++)
bl_ptr[i * X] = src[i * I];
__syncthreads();
...
CUDAsubroutineInplaceDCTvector(…);
for(unsigned int i = 0; i < B; i++)
dst[i *I] = bl_ptr[i * X];
}
16 regs
32 regs
16 regs
Use the compiler to:
Statically partition the program into phases
Add annotations with per-phase resource requirements

## Slide 28: Zorua Design: Key Questions
How do we determine the variation in resource requirements?
How do we use this knowledge to:
  control how much we oversubscribe at run time?
  coordinate allocation of multiple resources to maximize parallelism within the oversubscription budget?

## Slide 29: Component 2: Hardware Runtime System
Phase 3
Pending
Schedulable
Warp
Scheduler
Allocate Required
Resources
Phase 2
Phase 1
Deallocate Dead Resources
Control and coordination with
an adaptive runtime system:
the coordinator

## Slide 30: Putting It All Together
Zorua: A hardware-software cooperative framework
The compiler: annotates the program to partition it into phases and specify the resource needs of each phase
The coordinator: a hardware runtime system that makes oversubscription decisions and allocates/deallocates resources
Hardware virtualization support:
  Mapping tables for each resource (1.85kB ≈ 0.134% of the die area)
  Machinery to swap data between on-chip hardware & swap space

## Slide 31: Outline
Problem: Tight Coupling
Key Implications
Our Goal
Our Approach: Zorua
  Virtualization Strategy
  Design Challenges
  Design Ideas
Evaluation

## Slide 32: Methodology
Evaluation Infrastructure: Real GPUs (Fermi/Kepler/Maxwell), GPGPUSim, GPUWattch
Workloads
  Lonestar, CUDA SDK
System Parameters
  15 SMs, 32 threads/warp
  Warps/SM: Fermi: 48, Kepler/Maxwell: 64
  Registers: Fermi: 32768, Kepler/Maxwell: 65536
  Scratchpad: Fermi/Kepler: 48KB, Maxwell: 64KB
  Core: 1.4GHz, GTO scheduler , 2 schedulers/SM
  Memory: 177.4GB/s BW, 6 GDDR5 Memory controllers
Overheads of Zorua
  2-cycle latency for mapping table lookup for each resource
  Memory requests for swap space accesses

## Slide 33: Effect on Performance Variation
Zorua reduces the dependence of performance on resource specification
Maximum
Minimum
Average
Performance variation across different specification points
Lower Quartile
Upper Quartile
Baseline
WLM
Zorua
* Xiang et al., HPCA ‘14

## Slide 34: Effect on Performance Cliffs
Chart: Threads/Block
| 256 | 384 | 512 | 640 | 768 | 896 | 1024
Baseline | 1.1847 | 1.1937 | 1.7726 | 1.4628 | 1.2761 | 1.2203 | 1.1911
WLM | 1.0357 | 0.98572 | 1.1049 | 0.99149 | 0.93994 | 0.93229 | 1.6175
Zorua | 1.0136 | 0.9452 | 0.94782 | 0.9353 | 0.92633 | 0.92954 | 0.92325
Chart: Scratchpad/Block
| 10496 | 15744 | 20992 | 26240 | 31488 | 36736 | 41984 | 47232
Baseline | 1.0837 | 1 | 1.0834 | 1.6459 | 1.3873 | 1.248 | 1.108 | 1.0507
WLM | 1.0837 | 1 | 1.0834 | 1.6459 | 1.3873 | 1.248 | 1.108 | 1.0507
Zorua | 1.0837 | 1 | 0.99699 | 1.2202 | 1.13 | 1.1468 | 1.0251 | 0.96895
MST
NQU
Zorua alleviates the performance cliffs resulting from un-optimized specifications

## Slide 35: Effect on Performance Portability
Chart: Maximum Porting Performance Loss
| BH | DCT | MST | NQU | RD | SLA | SP | SSSP | AVG
Baseline | 0 | 1.0551 | 1.27 | 0.37501 | 0.33202 | 0.42802 | 0.60474 | 0.14758 | 0.52655
WLM | 0.39551 | 0.84102 | 0.96453 | 0.37501 | 0.49633 | 0.44483 | 0.43186 | 0.13521 | 0.51054
Zorua | 0.06979 | 0.28084 | 0.36068 | 0.29142 | 0.18456 | 0.2065 | 0.43186 | 0.084952 | 0.23882
Zorua reduces the performance loss from porting across GPU architectures
53%
24%

## Slide 36: Other Uses
Resource sharing in multi-programmed environments
Low latency preemption of kernels
Dynamic parallelism
…

## Slide 37: Conclusion
Problem: The tight coupling between programmer-specified resource usage and allocation of on-chip resources leads to challenges in:
  programming ease, performance portability, resource efficiency
Our Approach: Decouple specification and management of on-chip resources
Our Solution: Zorua: A holistic approach to virtualizing multiple on-chip resources in GPUs
Key Results:
  Zorua reduces dependence of performance on programmer-specified resource usage
    Zorua enhances programming ease and performance portability
  Zorua improves performance with more efficient resource utilization
Future Work: Zorua enables several other use cases

## Slide 38: Zorua: A Holistic Approach to Resource Virtualization in GPUs
Nandita Vijaykumar
Kevin Hsieh, Gennady Pekhimenko, Samira Khan,
Ashish Shrestha, Saugata Ghose, Adwait Jog, Phillip B. Gibbons, Onur Mutlu

## Slide 40: A Walkthrough
Thread
queue
Coordinator
Scratchpad
queue
Register
queue
Thread
Block
Scheduler
Register Mapping Table
Scratchpad Mapping Table
Thread Mapping Table
Acquire
resources
Warp
Scheduler
Release
resources

## Slide 41: Effect on schedulable warps

## Slide 42: Effect on energy consumption

## Slide 43: Summary of applications