## Slide 1: Introduction to SimpleScalar
1

## Slide 2: Overview
What is an architectural simulator?
– a tool that reproduces the behavior of a computing
device
Leverage a faster, more flexible software development cycle
  Permit more design space exploration
  Facilitates validation before H/W becomes available
  Level of abstraction is tailored by design task
  Possible to increase/improve system instrumentation
  Usually less expensive than building a real system
2
Device Simulator
Why we use a simulator?
System inputs
System outputs
System metrics

## Slide 3: A Taxonomy of Simulation Tools
Shaded tools are included in SimpleScalar Tool Set

## Slide 4: Functional vs. Performance
Functional simulators
  Model the function of each component
  Does not have timing accuracy
  Faster
Performance simulators
  Model system at finer detail
  Timing in addition to functionality
For example:
  Branch prediction accuracy vs. memory latency

## Slide 5: Trace- vs. Execution-Driven
Trace-Driven
  Simulator reads a ‘trace’ of the instructions captured during a
previous execution
  Easy to implement, no functional components necessary
Execution-Driven
  Simulator runs the program (trace-on-the-fly)
  Hard to implement
  Advantages
    No need to store traces
    Register and memory values usually are not in trace
    Support mis-speculation cost modeling

## Slide 6: SimpleScalar Tool Set
Computer system design and analysis infrastructure
– Processor/device (behavioral) models
build modeling applications that simulate real programs running on a range of modern processors and system
Support many ISAs and I/O interfaces
Alpha, PISA, ARM, and x86 instr. sets
Hosted on most any Unix-like machine
Application
Simplescalar
Simulators
Host
Machine
Application Input/output
Performance results
Freely available for academic
non-commercial use with source from
www.simplescalar.com

## Slide 7: Advantages of SimpleScalar
Highly flexible
  functional simulator + performance simulator
Portable
  Host: virtual target runs on most Unix-like systems
  Target: simulators can support multiple ISAs
Extensible
  Source is included for compiler, libraries, simulators
  Easy to write simulators
Performance
  Sim-Fast: 10+ MIPS
  Sim-OutOrder: 350+ KIPS

## Slide 8: Simulator Suite
Sim-Fast
Sim-Safe
Sim-Profile
Sim-Cache
Sim-BPred
Sim-Outorder
-420 lines
-functional
-4+ MIPS
-350 lines
-functional
w/checks
-900 lines
-functional
-Lot of stats
-~1000 lines
-functional
-Cache stats
-3900 lines
-performance
-OoO issue
-Branch pred.
-Mis-spec.
-ALUs
-Cache
-TLB
Performance Detail

## Slide 9: Sim-Outorder
Most complicated and detailed simulator
Supports out-of-order issue and execution
Provides reports
  branch prediction
  cache
  external memory
  various configuration

## Slide 10: Specifying Sim-outorder
Running a program
sim-outorder [sim opts] program [program opts]
e.g.
$SIMPLESIM/simplesim-3.0/sim-outorder
-config cfg_file bzip2_base.i386-m32-gcc42-nn
dryer.jpg

## Slide 11: Benchmark
SPEC 2006
– Six benchmarks (4 integer, 2 floating point) bzip2(INT)
equake(FP) hmmer(INT) mcf(INT) milc(FP) sjeng(INT)

## Slide 12: Installation of simplescalar
Simplescalar 3.0 is already installed bg machines
Path setup
  log on into one of the bg machines
  Go to your home directory: cd
  >vim .cshrc (or gedit .cshrc)
export SIMPLESIM=/home/scratch/massem/research/Simulators/simplescalar
> source .cshrc
  To verify, run
>echo $SIMPLESIM
the return should be /home/scratch/massem/research/Simulators/simplescalar

## Slide 13: Installation of simplescalar
Create a local directory
>mkdir simplescalar
>cd simplescalar
>cp -r $SIMPLESIM/simplesim-3.0/ss-benchmark ss-benchmark
>cp -r $SIMPLESIM/simplesim-3.0/config config
>cd ss-benchmark

## Slide 14: Running Benchmarks
14
Run benchmark (bzip2)
>cd bzip2
>$SIMPLESIM/simplesim-3.0/sim-outorder -config ../../config/tmp.cfg bzip2_base.i386-m32-gcc42-nn dryer.jpg

## Slide 15: Check results
Check simulation results
– vim sim1.out (or gedit sim1.out)
15

## Slide 16: Modify config
Modify a parameter in the config file
>cd ../../config
>vim tmp.cfg (or gedit tmp.cfg)
  Increase L2 Data Cache Latency from 4 to 10
-cache:dl2lat 10
  Change output file name (-redir:sim sim2.out)
  Save and close tmp.cfg

## Slide 17: Re-run Benchmark
Run benchmark (bzip2)
>cd ss-benchmark
>cd bzip2
>$SIMPLESIM/simplesim-3.0/sim-outorder
–config ../../config/tmp.cfg
bzip2_base.i386-m32-gcc42-nn dryer.jpg

## Slide 18: Check result
Check simulation results
– vim sim2.out (or gedit sim2.out)

## Slide 19: Global Simulator Options
Supported on all simulators
-print simulator help message
-enable debug message
-quit immediately
-read config parameters from <file>
-save config parameters into <file>
-h
-d
-q
-config <file>
-dumpconfig <file>
Configuration files
To generate a configuration file: -dumpconfig <file>
Change parameters in <file>
Comments allowed in configuration file, “#”
Reload configuration file using: -config <file>

## Slide 20: Log into bg machines using SSH
ssh <username>@bg1.cs.wm.edu
You can use machines from bg1 to bg9

## Slide 21: Running rest of benchmarks
mcf
> cd mcf
> $SIMPLESIM/simplesim-3.0/sim-outorder
–config ../../config/tmp.cfg mcf_base.i386-m32-gcc42-nn inp.in

## Slide 22: hmmer
> cd hmmer
> $SIMPLESIM/simplesim-3.0/sim-outorder
–config ../../config/tmp.cfg hmmer_base.i386-m32-gcc42-nn bombesin.hmm

## Slide 23: sjeng
> cd sjeng
> $SIMPLESIM/simplesim-3.0/sim-outorder
–config ../../config/tmp.cfg sjeng_base.i386-m32-gcc42-nn test.txt

## Slide 24: milc
> cd milc
> $SIMPLESIM/simplesim-3.0/sim-outorder
–config ../../config/tmp.cfg milc_base.i386-m32-gcc42-nn < su3imp.in

## Slide 25: equake
> cd equake
> $SIMPLESIM/simplesim-3.0/sim-outorder
–config ../../config/tmp.cfg equake_base.pisa_little < inp.in > inp.out